## Slide 1: Title: Partial overlapping AN and SR PUCCH resources
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, February 26th – March 2nd, 2018
Agenda Item: 7.1.3.2.1
Source: Ericsson
Document for: Discussion and Decision
R1-1803391

## Slide 2: Outline
Summary of views
Purpose of discussion
Discussion points on AN and SR overlapping resources

## Slide 3: Summary of proposals
 | AN with format 0 | AN with format 1 | AN with format 2/3/4
SR with format 0 | Drop SR at least overlapped symbols: Lenovo (or AN), CATT (SR after), Intel (drop all SR when k>1), Nokia (logical OR over all K SR processes) Drop SR or AN depends on priority Panasonic Multiplexing on the AN resource CATT (SR before), Ericsson, Oppo, Intel (k=1), LGE, Panasonic Change CS of overlapping symbols on AN resource ZTE | Drop SR at least overlapped symbols: Lenovo (or AN), CATT, Ericsson (all SR is dropped), Intel (drop all SRs) Drop SR or AN depends on priority Panasonic, ZTE(drop AN hop containing overlapping symbol if SR prioritize) Multiplexing: Panasonic Bundle HARQ-ACK Oppo Change CS of overlapping symbols on AN resource ZTE | Multiplexing (jointly coding) on AN resource: Lenovo (SR before), CATT, Ericsson, Oppo, LGE, Nokia (AN PF2 and SR PF0), Panasonic, ZTE, Intel Puncture short into long: Oppo Drop SR at least overlapped symbols: Lenovo (SR after) Drop AN: Oppo (SR before) Drop SR or AN depends on priority Panasonic

## Slide 4
 | AN with format 0 | AN with format 1 | AN with format 2/3/4
SR with format 1 | Drop SR at least overlapped symbols: Lenovo (or AN), CATT (SR before), Intel (drop all SR when k>1) Multiplexing on the AN resource Ericsson, Oppo (SR after), Intel (k=1), LGE Multiplexing on the SR resource CATT(SR after), Drop AN: Oppo (SR before) Change CS of overlapping symbols on SR resource ZTE | Drop SR at least overlapped symbols: Lenovo (or AN),CATT (SR before), Ericsson (not fully contained), Intel (drop all SRs) Drop SR or AN depends on priority Panasonic, ZTE(drop SR hop containing overlapping symbol if SR prioritize) Multiplexing on the AN resource Erisson ( SR is fully contained), Panasonic Multiplexing on the SR resource CATT(SR after), Channel selection (similar to LTE): Oppo, LGE | Multiplexing (jointly coding) on AN resource: Lenovo (SR before), CATT, Ericsson, Oppo, LGE, Nokia (AN PF2 and SR PF0), Panasonic, ZTE, Intel Puncture short into long: Oppo Drop SR at least overlapped symbols: Lenovo (SR after) Drop AN: Oppo (SR before) Drop SR or AN depends on priority Panasonic

## Slide 5: Purpose of discussion
Proposals for multiplexing AN and SR, as well as AN/SR and CSI vary a lot. It is difficult to make any progress.
It is important to focus what it is feasible in Rel-15 and have a proper design accordingly.
  That requires reasonable compromises form all parties.
  The short coming should be addressed in Rel-16.

## Slide 6: AN and SR overlapping PUCCH resources Discussion points
Observation 1:
  For prioritization of an SR transmission over HARQ-ACK transmission, the UE should be able to determine whether the HARQ-ACK bits correspond to a high priority scheduled DL transmission.
Observation 2:
  In TS 38.321 section 5.4.4 the UE picks a SR resource (i.e. a PUCCH resource) based on which LCH received data. It is possible to configure very few logical channels so each logical channel has its own PUCCH resources, but it is a corner case and not something the PHY should rely on. Hence, the PHY does not know which LCH triggered the SR/has data.
  It is up to UE implementation if the PHY know which LCH triggered the SR/has data. Hence, we can not assume the information from PHY to MAC is exchanged.

## Slide 7: AN and SR overlapping PUCCH resources Discussion points
Observation 3:
  There is strong concern from UE vendors and some NW vendors to support a short PUCCH transmission interrupting a long PUSCH transmission duration.

## Slide 8: Conclusion
Three following options are identified.
Option 1: UE assumes there is no information with respect to Mac/Phy layer priority for the UCI transmission on PUCCH.
  FFS design
Option 2: UE assumes there is information with respect to PHY layer priority for the UCI transmission on PUCCH.
  FFS details (priority rules and design)
Option 3:UE assumes there is information with respect to Mac layer priority for the UCI transmission on PUCCH.
  FFS how to determine the priority rules (RAN2 input is needed)
  FFS on how to transmit PUCCH
Potential way forward:
  The design of option 1 is the simplest one with respect on not relying on RAN2 or defining new priority rules. It can be considered as a starting points while progressing on the other options if possible.