## Slide 1: WF on V2X Sidelink Channel Modeling
Huawei, HiSilicon, Qualcomm, ZTE, Sanechips, Fraunhofer HHI, Intel, Cohere Technologies, InterDigital, NTT Docomo, Vodafone, LGE, NEC, General Motors, CATT, ITRI
3GPP TSG RAN WG1 Meeting #92 R1-1803392
Athens, Greece, February 26 – March 2, 2018
Agenda item: 7.5.2

## Slide 2: Background
Realistic LOS blockage modeling is particularly important for V2V communication because of:
  safety-critical characteristics of many applications
  low antenna heights
Other vehicles often block V2V communication
  Same applies to other V2X link types (e.g., V2P)
Up to 40% of links blocked by vehicles in urban

## Slide 3: Proposal
At least for above 6 GHz, the V2V sidelink channel is modeled according to the following three states:
  i) LOS
  ii) NLOS: LOS path blocked by static objects (e.g., building, tree)
  iii) NLOSv: LOS path blocked by mobile objects (i.e., vehicle)
  FFS details including at least the following aspects:
    How to determine the different states (e.g., statistically, deterministically),
    Whether the blockage loss is dependent on the blocker size, number, and/or the distance between Tx, Rx, blocker, etc.
    Small and large scale parameters for the different states
    Etc.