## Slide 1: Second Offline Summary on CA Aspects
Samsung
R1-1803409
3GPP TSG RAN WG1#92
Athens, Greece, Feb. 26 – March 2, 2018
Agenda item 7.1.3.4.2

## Slide 2: Semi-static HARQ-ACK Codebook
Proposal: When a UE is configured with semi-static HARQ-ACK Codebook, support determining the HARQ association set based on the minimum of {number of non-overlapping candidate PDSCH occasions per slot as determined by pdsch-symbolAllocation table, number of unicast PDSCH a UE can receive in a slot when a UE is configured with semi-static HARQ-ACK Codebook}
  FFS: the number of unicast PDSCH a UE can receive in a slot when a UE is configured with semi-static HARQ-ACK Codebook in terms of hard-coded, or part of UE capability?
  Conclusion: If UE indicates capability to receive only one PDSCH per slot, HARQ-ACK association set assumes one PDSCH per slot; else, it assumes number of non-overlapping candidate PDSCH occasions per slot as determined by the SLIV in the configured pdsch-symbolAllocation table
Consider the minimum of {number of candidate PDSCH occasions, configured number of HARQ processes} in determining the HARQ association set?
  Conclusion: Majority of companies consider the above to be beneficial in reducing the HARQ-ACK codebook size but there is no consensus on whether or not the benefits exist in practice (argument was that gNB will configure a large number of HARQ processes) or on whether or not this is an essential functionality
  No objection to the proposal if there will be UE categories that can support only a small number (e.g. 4-8) as the maximum number of HARQ processes

## Slide 3: Semi-static HARQ-ACK Codebook
Proposed conclusion: It is understood that before RRC connection, since it was agreed previously “HARQ-ACK is only one bit without bundling before RRC connection”, consequently, there is no need to define the default HARQ-ACK codebook before RRC connection
  Conclusion: No change to the above conclusion
Proposals: When a UE is configured with Semi-static HARQ-ACK Codebook and the UE detects within a DL association set a DCI format 1_1 indicating DL BWP switching, then the UE reports HARQ-ACK for the downlink association set for:
  Alt. 1: PDSCH receptions on the active DL BWP after switching
    Relies on the UE not failing to detect DCI format 1_1 – reduced HARQ-ACK codebook size
  Alt. 2: PDSCH receptions on the active DL BWP before switching.
    Relies on the UE not failing to detect DCI format 1_1 – reduced HARQ-ACK codebook size
  Alt. 3: DL association set is determined by the union of DL association sets over all DL BWP parts
    Does not rely on the UE detecting DCI format 1_1 – maximum HARQ-ACK codebook size

## Slide 4: Semi-static HARQ-ACK Codebook - Components
Proposals: Confirm the following working assumption with updates:
  Working assumption: In case a UE is configured for semi-static HARQ-ACK codebook determination, when the UE detects to receive only one PDSCH within a DL association set on the Pcell, the UE reports HARQ-ACK only for the one PDSCH
    FFS whether No additional constraints are necessary for the above operation
  Option2: If UE detects DCI format 1_0 with counter DAI value of 1 (R1-1801627, R1-1801827, R1-1801989)
    Supported by Nokia, Samsung, Huawei, HiSi, ZTE, Intel, LGE, Panasonic
  Option3: If UE detects only one PDSCH in the first slot of DL association set (R1-1801740, R1-1802573)
    Similar but have the k1 value for fallback HARQ-ACK codebook indicated by RRC (R1-1802845)
    Supported by CATT, LGE, Interdigital, Sharp, and Qualcomm
  Conclusion: Offline consensus is that option 2 is more advantageous than option 3.

## Slide 5: HARQ-ACK Codebook
Should Phase 1 support multiple PDSCHs at different time instances on a same BWP/cell being scheduled from same PDCCH monitoring occasion?
  E.g. both same-slot and cross-slot scheduling from same PDCCH monitoring occasion
  Consider/Yes (R1-1801740, R1-1801989), No? (R1-1802917)
How to select PUSCH for UCI multiplexing in time domain
  First PUSCH transmission in slot indicated for HARQ-ACK (R1-1802217, R1-1802418)
  PUSCH scheduled by first received UL grant in slot indicated for HARQ-ACK (R1-1801348)
  Transmit in PUCCH or PUSCH, whichever occurs earlier in slot (drop PUSCH if it is the PUCCH)
  Semi-consensus (due to low participation): using cell index only is sufficient – no need to consider instance/time of UL grant detection
    UE receives DL assignments with corresponding HARQ-ACK multiplexed in a PUSCH at an earlier or at the same PDCCH monitoring occasion as the UL grant scheduling the PUSCH
    PUSCH is assumed to have same first symbol as a corresponding PUCCH for HARQ-ACK transmission
HARQ-ACK for SPS PDSCH in multiple cells
  Specifications only allow configuration for a PUCCH format 0/1 resource but HARQ-ACK bits can be more than 2
  Option 1: Update RRC parameters to include configuration for a PUCCH format 2/3/4 resource
  Option 2: Bundle HARQ-ACK bits
Offline suggestion to avoid request for definition of RRC parameters providing PUCCH format 2/3/4 resource: In Rel-15, UE is not expected to be configured to report HARQ-ACK on the same PUCCH for more than 2 SPS PDSCH receptions

## Slide 6: EN-NR DC and NR CA
Simultaneous configuration of EN-NR DC and NR PUCCH Scell
  [Can be supported]
Simultaneous transmission of PUCCH and PUSCH in LTE for EN-NR DC
  [Can be supported]

## Slide 7: Other
PUSCH selection for HARQ-ACK multiplexing
  Based on the agreement from RAN1 NR AH 1801, UCI is multiplexed on PUSCH transmission [that starts at same or later symbol than corresponding PUCCH transmission in corresponding slot] on cell with the smallest index
  Additional proposals: Prioritize grant-based over grant-free PUSCH, prioritize PUSCH with smaller SCS or longer duration (R1-1801545, R1-1802108)
Support HARQ-ACK multiplexing of two PDSCHs before RRC setup by using C-DAI in DCI 1_0 (R1-1801740)
Semi-static HARQ-ACK codebook: If UE reported HARQ-ACK for a PDSCH reception occasion in a previous PUCCH slot, UE reports NACK for the PDSCH reception occasion in current PUCCH slot (R1-1802108)
Dynamic HARQ-ACK codebook: Whether to reorder counter DAI for a given PDCCH monitoring occasion to first count DCI 1_1 transmissions in first loop and then count DCI 1_0 transmissions in second loop (R1-1802217, R1-1802938)
No TB-based sub-codebook if all cells are configured for CBG-based HARQ-ACK (R1-1802217)
Semi-static HARQ-ACK codebook: 1-bit UL DAI indicates “less than or equal to 2 HARQ-ACK bits” or “maximum HARQ-ACK payload size“(R1-1802217)

## Slide 8: Other
Semi-static HARQ-ACK codebook: UEs capable of simultaneously receiving 2 PDSCHs, report 2 HARQ-ACK bits for a PDSCH reception occasion (R1-1802540)
  Introduce corresponding UE capability indication
Introduce RRC parameter to indicate interpretation of total DAI either according to current/LTE interpretation or with a predictive nature (R1-1802540)
Always pad TB-based HARQ-ACK bits for one (or two) PDSCH(s), if UE receives only CBG-based DCI format 1_1 (R1-1802845)
Semi-static HARQ-ACK codebook: Divide slot interval into N sub-intervals and reserve N entries for each slot and cell. HARQ-ACK for a PDSCH starting in sub-interval i is inserted in the i-th entry (R1-1802917)
Jointly consider counter DAI, DL total DAI, and UL total DAI to determine HARQ-ACK codebook in PUSCH (R1-1802697)
TA for carriers with multiple numerologies
Multi-slot scheduling: Is there anything missing from the current specifications other than UE not being expected to be scheduled PDSCH over more than 4 slots (otherwise, a larger bit-field for the DAIs is needed)
Whether to support PUCCH on a Scell for a UE

## Slide 9: References