3GPP TSG RAN WG1 Meeting #92			R1-1801325

Athens, Greece, February 26th – March 2nd, 2018

3GPP TSG-RAN WG4 Meeting AH-1801	R4-1801079

San Diego, US, 22 - 26 Jan, 2018

Title:	LS on measurement gap patterns

Response to:	-

Release:	Rel-15

Work Item:	NR_newRAT-Core

Source:	TSG-RAN WG4

To:	TSG-RAN WG2

Cc:	TSG-RAN WG1

Contact Person:

Name:	Han Jing

E-mail Address:	hw.hanjing@huawei.com

Attachments:	None

# Overall Description:

On top of the LS reply R4-1714503 last meeting, RAN4 further discussed the measurement gap patterns on both NSA and SA and made the following update.

Table 1. Measurement gap patterns configuration

| Gap Pattern Id | Measurement Gap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) |
| --- | --- | --- |
| 0 | 6 | 40 |
| 1 | 6 | 80 |
| 2 | 3 | 40 |
| 3 | 3 | 80 |
| 4 | 6 | 20 |
| 5 | 6 | 160 |
| 6 | 4 | 20 |
| 7 | 4 | 40 |
| 8 | 4 | 80 |
| 9 | 4 | 160 |
| 10 | 3 | 20 |
| 11 | 3 | 160 |
| 12 | 5.5 | 20 |
| 13 | 5.5 | 40 |
| 14 | 5.5 | 80 |
| 15 | 5.5 | 160 |
| 16 | 3.5 | 20 |
| 17 | 3.5 | 40 |
| 18 | 3.5 | 80 |
| 19 | 3.5 | 160 |
| 20 | 1.5 | 20 |
| 21 | 1.5 | 40 |
| 22 | 1.5 | 80 |
| 23 | 1.5 | 160 |

Table 2. Applicability for Gap Pattern Configurations supported by the E-UTRA-NR dual connectivity UE

| Measurement gap pattern configuration | Serving cell | Measurement Purpose | Applicable Gap Pattern Id |
| --- | --- | --- | --- |
| Per-UE measurement gap | E-UTRA + FR1, or E-UTRA + FR2, or E-UTRA + FR1 + FR2 | E-UTRA only | [0,1,2,3] |
|  |  | FR1 and/or FR2 | [0-11] |
|  |  | E-UTRAN and FR1 and/or FR2 | [0,1,2,3] |
| Per FR measurement gap | E-UTRA and, FR1 if configured | E-UTRA only | [0,1,2,3] |
|  | FR2 if configured |  | No gap |
|  | E-UTRA and, FR1 if configured | FR1 only | [0-11] |
|  | FR2 if configured |  | No gap |
|  | E-UTRA and, FR1 if configured | FR2 only | No gap |
|  | FR2 if configured |  | [12-23] |
|  | E-UTRA and, FR1 if configured | E-UTRA and FR1 | [0,1,2,3] |
|  | FR2 if configured |  | No gap |
|  | E-UTRA and, FR1 if configured | FR1 and FR2 | [0-11] |
|  | FR2 if configured |  | [12-23] |
|  | E-UTRA and, FR1 if configured | E-UTRA and FR2 | [0,1,2,3] |
|  | FR2 if configured |  | [12-23] |
|  | E-UTRA and, FR1 if configured | E-UTRA and FR1 and FR2 | [0,1,2,3] |
|  | FR2 if configured |  | [12-23] |
| Note: if GSM or UTRA TDD or UTRA FDD inter-RAT frequency layer is configured to be monitered, only measurement gap pattern #0 and #1 can be used for per-FR gap in E-UTRA and FR1 if configured, or for per-UE gap. |

Table 3: Applicability for Gap Pattern Configurations supported by the NR standalone operation UE

| Measurement gap pattern configuration | Serving cell | Measurement Purpose | Applicable Gap Pattern Id |
| --- | --- | --- | --- |
| Per-UE measurement gap | FR1, or FR1 + FR2 | E-UTRA only | 0,1,2,3 |
|  |  | FR1 and/or FR2 | 0-11 |
|  |  | E-UTRAN and FR1 and/or FR2 | 0,1,2,3 |
|  | FR2 | E-UTRA only | 0,1,2,3 |
|  |  | FR1 only | 0-11 |
|  |  | FR1 and FR2 | 0-11 |
|  |  | E-UTRAN and FR1 and/or FR2 | 0,1,2,3 |
|  |  | FR2 only | 12-23 |
| Per FR measurement gap | FR1 if configured | E-UTRA only | 0,1,2,3 |
|  | FR2 if configured |  | No gap |
|  | FR1 if configured | FR1 only | 0-11 |
|  | FR2 if configured |  | No gap |
|  | FR1 if configured | FR2 only | No gap |
|  | FR2 if configured |  | 12-23 |
|  | FR1 if configured | E-UTRA and FR1 | 0,1,2,3 |
|  | FR2 if configured |  | No gap |
|  | FR1 if configured | FR1 and FR2 | 0-11 |
|  | FR2 if configured |  | 12-23 |
|  | FR1 if configured | E-UTRA and FR2 | 0,1,2,3 |
|  | FR2 if configured |  | 12-23 |
|  | FR1 if configured | E-UTRA and FR1 and FR2 | 0,1,2,3 |
|  | FR2 if configured |  | 12-23 |

# Actions:

RAN4 respectfully asks RAN2 to take the above agreements into consideration in their future work

# Date of Next TSG-RAN WG4 Meeting:

3GPPRAN4#86                26 Feb - 2 Mar 2018	Athens,		GR

3GPPRAN4#86bis            16 - 20 Apr 2018		Melbourne,	AU