## Slide 1: WF on UL PTRS Port Indication
vivo, Intel, NEC, Lenovo, Motorola Mobility, ZTE, Sanechips, OPPO, Samsung, LG Electronics, MediaTek, Nokia, Nokia Shanghai Bell, Huawei, HiSilicon, CMCC, DOCOMO
RAN1#92b, Sanya, China, April 2018
Agenda item: 7.1.2.3.4
R1-180xxxx

## Slide 2: Background
Agreement:
  The bitwidth of IE in DCI for indicating PT-RS to DMRS port association for UL in CP-OFDM is 0,1 or 2 bits, taking into account the number of SRS ports, maximum ranks supported, and number of PT-RS ports.
Agreement:
  For non-codebook based UL transmission, the association between PTRS port(s) and DMRS port(s) are indicated explicitly in the DCI format 0_1.
    At least for 1 PTRS port case, reuse the table 7.3.1.1.2-25 and 7.3.1.1-26 defined in 38.212 (up to editor how to capture this)

## Slide 3: Proposal:
For the following case, the field of PTRS-DMRS association is 0 bit for both codebook based UL transmission and non-codebook based UL transmission
  High layer parameter maxRank is configured as 1.
Update the following Table 7.3.1.1.2-26 for PTRS-DMRS association for UL PTRS ports 0 and 1, UL-PTRS-ports = 2
Value of MSB | DMRS port | Value of LSB | DMRS port
0 | 1st DMRS port transmitting layers corresponding to SRS port 0 and 2, the 1st DMRS port which shares PTRS port 0 | 0 | 1st DMRS port transmitting layers corresponding to SRS port 1 and 3, 1st DMRS port which shares PTRS port 1
1 | 2nd DMRS port transmitting layers corresponding to SRS port 0 and 2, 2nd DMRS port which shares PTRS port 0 | 1 | 2nd DMRS port transmitting layers corresponding to SRS port 1 and 3, 2nd DMRS port which shares PTRS port 1