## Slide 1
3GPP TSG RAN WG1 Meeting #92bis R1-1805604
Sanya, China, 16th – 20th April 2018
Agenda item: 7.1.2.2.4
WF on beamFailureRecoveryTimer
InterDigital, MediaTek, Ericsson, ZTE, SaneChips, Huawei, HiSilicon, NTT DOCOMO, Intel, Samsung, CATT, [Qualcomm]

## Slide 2: Background
Agreements (RAN1 AH1801):
  Behavior of Beam-failure-recovery-Timer
    Start Beam-failure-recovery-Timer upon beam failure detection event declared by UE
    Stop Beam-failure-recovery-Timer upon reception of gNB response for beam failure recovery request transmission
Agreements (RAN1 AH1801):
  From RAN1 perspective, contention-free PRACH-based beam failure recovery is considered unsuccessful when one of the following conditions is met
    Upon expiry of Beam-failure-recovery-Timer
    Upon reaching max. # of BFRQ transmissions

## Slide 3: Background
RP ruling on beamFailureRecoveryTimer [RP-180579]
  For beamFailureREcoveryTimer:
  The current agreed specification remains as is: beamFailureRecoveryTimer is not specified until further guidance.
  RAN1 may further discuss in RAN1 whether and how the timer is used in the context of CBRA. RAN1 should consider the existing RAN2 MAC procedure and if/when agreed in RAN1, inform RAN2 if and how the timer is envisioned to be used and how UE behaves in the case of timer expiry.
  NOTE: From RAN1 perspective this would not be considered as a new RRC parameter or new feature, if a timer is agreed.

## Slide 4: Background
Use cases for beamFailureRecoveryTimer
  For contention-free PRACH-based BFR, the timer avoids UE stuck in candidate beam search (within dedicatedly configured beam set) in case there is no qualifying beam
  Candidate beam selection for contention-free PRACH-based BFR is based on L1-RSRP. For qualified candidate beam but poor SINR, the timer enables UE to try contention-based PRACH resources after timer expires

## Slide 5: Proposals
Send an LS to RAN2 with following information
  RAN1 confirms the need for beamFailureRecoveryTimer and keep its uses as current RAN1 agreement
    Note: unsuccessful CFRA based BFR upon expiry of beamFailureRecoveryTimer means that UE shall not use CFRA for BFR after beamFailureRecoveryTimer expired and no indication to higher layer is required
  The following use case will be captured in the LS
    Candidate beam selection for contention-free PRACH-based BFR is based on L1-RSRP. For qualified candidate beam but poor SINR, the timer enables UE to try contention-based PRACH resources after timer expires
      Note: CBRA resource can be used anytime when there is no candidate beam for CFRA resource