## Slide 1: Derivation of k0
Qualcomm
R1-1805723
3GPP TSG RAN WG1 #92b
Sanya, China, April 16 - 20 , 2018
Agenda item 7.1.1.1

## Slide 2: Background
It is currently being discussed whether k0 signaling should be kept, or k0 should be derived from other parameters already signaled
The intent of k0 is in principle to allow describing the signal generation for multiple numerologies with a common f0
The exact tone and RB location for each SCS is already fully described by the existing RMSI parameters

## Slide 3: Observations
The following should be assumed for an adopted solution
  It should be allowed that the UE can align FFT and f0 placement across multiple gNBs operating on the same channel even if the full sets of numerologies used by the gNBs are not identical

## Slide 4: Observations
The required guardband increases with SCS
  Based on the RAN4 definition, the number of RBs in the maximum transmission BW configuration for μ is 2, 3, or 4 RBs greater than twice the number of RBs for μ-1
Table 5.3.2-1: Maximum transmission bandwidth configuration NRB
SCS (kHz) | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | [160] | 216 | 270 | N/A | N/A | N/A
30 | 11 | 24 | 38 | 51 | 65 | [78] | 106 | 133 | 162 | 217 | 273
60 | N/A | 11 | 18 | 24 | 31 | [38] | 51 | 65 | 79 | 107 | 135

## Slide 5: Proposal
Include k0={-6; 0; 6} signaling, applicable only to the largest μ for which CC parameters are included in the RMSI
For the other numerologies, for which CC parameters are included in the RMSI, implicitly derive k0 such that f0 aligns with that of the highest μ signaled by the cell and consistent with the signaled start RB and number of RBs for each numerology