## Slide 1: Proposals on LTE-NR coexistence
Qualcomm
R1-1807693
3GPP TSG RAN WG1 #93
Busan, Korea, May 21 - 25, 2018
Agenda item 7.1.5

## Slide 2: Background
RAN1 has considered two UE types
  UE capable of dynamic power sharing, a.k.a. Type 1
  UE not capable of dynamic power sharing, a.k.a. Type 2
In the EN-DC power control procedure, RAN1 has considered that ‘NR’ in the Type 1 UE modem knows about the ‘LTE’ but not the other way around
  This is because the different time-lines between LTE and NR
  This resulted in the decision of not changing LTE power by RAN1 power control definition for Type 1 UEs
  This resulted in the decision of not supporting sTTI in EN-DC

## Slide 3: Background
The 4ms LTE timeline has always been assumed for LTE
  E.g. no look-ahead in LTE CA or DC
The NR Work Item is aimed to minimize impact resulting from NSA to LTE physical layer

## Slide 4: Background
RAN4 has defined MPR/A-MPR definitions, which made different set of assumptions
  ‘LTE side knows about NR side’, irrespective of whether NR UL grant arrives earlier or much later than LTE grant
  LTE PHR includes information about NR grant, even if NR UL grant arrives much later than LTE grant
The RAN4 decisions require substantial changes in the LTE processing time requirements

## Slide 5: Background
Consider that LTE and NR use different slot formats, numerologies, the situations depicted below will occur for Type 1 UEs
The RAN4 decision results in LTE power changes within the LTE subframe, which is not supported in the LTE air-interface

## Slide 6: Proposals (MPR/A-MPR)
Send an LS to RAN2 to capture the previously mentioned issues related to Type 1 UEs

## Slide 7: Proposals (MPR/A-MPR)
In case the RAN4 MPR/A-MPR definitions remain
  Need to adopt modifications in the RAN1 procedure to avoid significant changes to LTE timeline requirement for Type 1 UEs
  Need to adopt required modification in the RAN1 procedure to solve problems with signal continuity

## Slide 8: Proposals (MPR/A-MPR)
Change in the LTE PHR requirement
  The UE is not expected to update LTE PHR report if the LTE reporting timeline is not met
    i.e. UE does not need to include information received later than 4ms prior to the PHR reference UL subframe
Change in power dropping rule
  (1) the UE calculates LTE power (P_LTE_only) and LTE PHR considering no NR Tx
  (2) the UE calculates NR power (P_NR_only) considereing no LTE Tx
  (3) the UE calculates the LTE power (P_L) and NR power (P_N) according to the dynamic power sharing rule and RAN4 MPR definition
  (4) the UE performs the following
    If both P_LTE_only==P_L && P_NR_only==P_N
      UE transmits both LTE and NR at powers P_L and P_N, respectively
    Else
      UE transmits LTE at power P_L and it can either drop NR or transmit NR at any power level below P_N

## Slide 9: Proposals (MPR/A-MPR)
Possible text proposal to implement the proposal in previous slide

## Slide 10: Proposals (Phase continuity)
The proposal in the previous slide avoids pahase continuity issues when LTE and NR uses different PAs
There is still a phase continuity problem in the cases of intra-band EN-DC with common PA
  In order to solve this, adopt the following for both Type 1 and Type 2 UEs
    When the LTE and NR Tx overlaps
      The transmission boundaries are aligned
        Same start and end times
      Frequency hop boundaries are aligned
        Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary

## Slide 11: Proposals (Phase continuity)
Possible text proposal to implement the proposal in previous slide

## Slide 12: Background (TDM in TDD)
It has been proposed to overturn the decision from the last RAN1 meeting and apply TDM in LTE TDD Pcell
The proposal on adopting an allowed LTE subframe subset would significantly worsen the LTE link budget, therefore it should not be adopted

## Slide 13: Proposals TDM in TDD
Support only Case 2 TDM in EN-DC with LTE TDD
If above is not adopted and TDM Case 1 is supported in LTE TDD in EN-DC, agree on the following
  DL HARQ is based on DL reference HARQ configuration
  UL HARQ is based on LTE TDD configuration
  LTE UL transmission can occur in any UL subframe and UpPTS in the LTE TDD configuration
  UE is not expected to be configured with simultaneous MCG and SCG transmission

## Slide 14: Proposals (TDM in FDD)
Consider adopting the same (i.e. no LTE restriction to UL in reference configuration) for TDM in FDD as well in Rel-16 [R1-1719194 “WF on UL TDM in single Tx EN-DC”]

## Slide 15: Proposals (TDM)
Clarify in the RAN1 EN-DC procedures that a UE indicating single Tx capability is not expected to be configured with simultaneous transmission (both for Case 1 and Case 2)

## Slide 16: Proposals (FR1 and FR2)
Since there is no joint FR1+FR2 power cap, the EN-DC power control procedures only apply to FR1
Clarify this in the specification