## Slide 1: Proposals on remaining issues on overlapping PUCCHs
Ericsson
3GPP TSG RAN WG1 Meeting 93
Busan, Korea, 21st – 25th May 2018
Agenda item: 7.1.3.2.1
R1-1807848

## Slide 2: Option 2 (preferred option in R1-1807774 based on online discussion)
In a slot with overlapping PUCCH/PUSCH resources, at most two groups of overlapping PUCCH/PUSCH channels are defined in a slot.
  While there is a group of overlapping PUCCH resources in a slot,
    The UE determines a PUCCH resource and corresponding UCI for multiplexing of the PUCCH resources for the group with the earliest starting symbol in the slot.
      The determined PUCCH resource and the corresponding UCI replace the PUCCH resources and corresponding UCI in the group.
  When there is no overlapping PUCCH resources in the slot, the UE determines the timeline requirements for overlapping UL channels. If the requirement is met, the UE proceeds to the agreed Step 2.

## Slide 3: Previous agreement
Agreements:
Within a group of overlapping PUCCH/PUSCH channels satisfying the timeline requirements, adopt the following procedure
  Step 1: determine a set of non-overlapping (in time)PUCCH resource(s) for UCI multiplexing by considering only the PUCCH resources in the group (irrespective whether or not PUSCH(s) exists), where each PUCCH resource satisfies the timeline requirements
  Step 2:
    if the resulting PUCCH resource(s) in step 1 overlapping with PUSCH(s), multiplex UCIs on the overlapping PUSCH(s);
      FFS: When UCI includes SR
    Otherwise, multiplex UCI on the determined PUCCH resource(s)

## Slide 4: Proposal on CSI configurations
If a UE is configured with overlapping PUCCH resources for CSI-only reporting in a slot,
  If a UE is configured with multi-CSI-PUCCH-Config, the UE multiplexes all the CSI reports corresponding to CSI only PUCCH resources (overlapping or not) in the slot on a single multi-CSI-PUCCH resource, following the agreed priority rules for CSI reporting.
  If a UE is not configured with multi-CSI-PUCCH-Config, among all the PUCCH resources for CSI reporting, the UE selects maximum two non-overlapping PUCCH resources for CSI reports with the highest priority.
    If two non-overlapping PUCCH resources are selected, they should include at least one with PUCCH format 2.
If a UE is configured with more than two non-overlapping CSI reports in a slot, the UE selects the maximum two PUCCH resources with the highest priority CSI repots.
  If two non-overlapping PUCCH resources are selected, they should include at least one with PUCCH format 2.

## Slide 5: Proposal 1 (update the agreement)
Update the following agreement as follows:
Agreements:
In a slot, with Within a group of overlapping PUCCH/PUSCH channels where each group of overlapping channels satisfying “the timeline requirements for overlapping channels”, adopt the following procedure
  Step 1: determine a set of non-overlapping (in time)PUCCH resource(s) for UCI multiplexing by considering only the PUCCH resources in the group (irrespective whether or not PUSCH(s) exists), where each PUCCH resource satisfies the timeline requirements
    While there are overlapping PUCCH resources in a slot,
      The UE determines a PUCCH resource and corresponding UCI for multiplexing PUCCH resources that overlap with the PUCCH resource with the earliest starting symbol being overlapped with a PUCCH resource in the slot.
      The determined PUCCH resource and the corresponding UCI replace the overlapped PUCCH resources and corresponding UCI.
    When there is no overlapping PUCCH resources in the slot, the UE determines “the timeline requirements for overlapping UL channels”. If the requirement is met, the UE proceeds to Step 2.
  Step 2:
    if the resulting PUCCH resource(s) in step 1 overlapping with PUSCH(s), multiplex UCIs on the overlapping PUSCH(s);
      FFS: When UCI includes SR
    Otherwise, multiplex UCI on the determined PUCCH resource(s)

## Slide 6
While there are overlapping PUCCH resources in a slot,
  The UE determines the earliest PUCCH resource with the largest duration (resource A) that overlaps with at least another PUCCH resource.
    In case of multiple candidates for resource A, one is selected.
  The UE determines a set of PUCCH resources (resource set X) overlapping with PUCCH resource A.
  The UE determines a PUCCH resource and corresponding UCI for multiplexing the PUCCH resource A and PUCCH resources in set X.
  The determined PUCCH resource and the corresponding UCI replace resource set X and resource A and corresponding UCI.
When there is no overlapping PUCCH resources in the slot, the UE determines “the timeline requirements for overlapping UL channels”. If the requirement is met, the UE proceeds to Step 2.

## Slide 7: Proposal 2 (section 2.3 in R1-1807662)
When two or more configured non-overlapping CSI PUCCH resources overlap with one or more configured SR PUCCH resources in a slot such that among these PUCCH resources, any of these PUCCH resources overlaps at least with another one,
  SR is multiplexed and transmitted with CSI on the earliest in time CSI PUCCH resource.
Note: Based on the feedback, given Proposal 1 and the pseudo code for multiplexing rules are agreed, this will not be necessary.

## Slide 8: Proposal 3 (section 2.4 in R1-1807662)
When there are both HARQ-ACK for PDSCH scheduled by DCI and HARQ-ACK for SPS PDSCH within a slot to be transmitted on PUCCH, the UE determines one PUCCH resource for transmission of all HARQ-ACK bits based on the ARI and total number of HARQ-ACK bits in the slot.

## Slide 9: Background on Proposal 4(section 2.1 in R1-1807662)
When the HARQ-ACK/SR PUCCH resource determined by ARI and the configured CSI PUCCH resource overlap in a slot, if the UE is configured with only one PUCCH resource set for UCI transmission including HARQ-ACK and simultaneous transmission of HARQ-ACK/SR and CSI is enabled, select from one of the following alternatives:
  Alt 1: The UE is not expected to transmit the corresponding HARQ-ACK/SR and the CSI report in a PUCCH resource in that slot.
    Supportive companies: E//, Spreadtrum Comm., OPPO, Intel.
  Alt 2: HARQ-ACK/SR and CSI are transmitted together by PUCCH resource for CSI
    Supportive companies: ZTE, Panasonic, CATT, Lenovo, MOT, DCM, Vivo, Nokia
    Note: The timeline requirements for transmission of HARQ-ACK on CSI PUCCH resource is met.
  Alt 3: HARQ-ACK/SR is transmitted on the HARQ-ACK/SR PUCCH resource and CSI reporting is dropped in that slot.
    Supportive companies: Panasonic, Vivo, LG
  Alt 4: The UE is not expected to be provided simultaneousHARQ-ACK-CSI = TRUE.
    Supportive companies: Samsung, E///

## Slide 10: Proposal 4(section 2.1 in R1-1807662)
Proposal a:
  When a UE is configured for one PUCCH resource set for UCI transmission including HARQ-ACK, the UE is not expected to be provided with simultanouesARQ-ACK-CSI=TRUE.
  Supportive companies: Samsing, E//, Spreadtrum Comm., OPPO, Intel, [Panasonic?], Vivo, LG, QC
Proposal b:
  When a UE is configured with one PUCCH resource set for UCI transmission including HARQ-ACK and simultanouesARQ-ACK-CSI=TRUE, the HARQ-ACK/SR bits for PDSCHs scheduled by PDCCH are transmitted together with CSI on the PUCCH resource for CSI.
  Supportive companies: ZTE, Panasonic, CATT, Lenovo, MOT, DCM, Vivo, Nokia

## Slide 11: Proposal 5:
When a PUCCH resource with format 2 or 3 or 4 for carrying a UCI including HARQ-ACK bits corresponding to granted PDSCH, overlaps with K SR PUCCH resources, the SR and the other UCI bits are multiplexed using the same PUCCH format 2 or 3 or 4 resource.
When a PUCCH resource carrying only SR overlaps with PUSCH, the PUCCH is dropped.
When a PUCCH resource carrying SR and other UCI overlaps with PUSCH, if the UCI on PUCCH is going to be multiplexed on PUSCH, the SR bits are dropped from the UCI before multiplexing on PUSCH.

## Slide 12: Proposals on SR ID
Discuss and decide on proposals in section 2.2 in R1-1807662.

## Slide 13: Appendix
Discussion and background material for proposals for section 2.3 in R1-1807662.

## Slide 14: Background
Agreements (RAN1#92bis):
When a configured CSI PUCCH resource overlaps with one or more configured SR PUCCH resources in a slot,
  The UE multiplexes all UCIs on the CSI PUCCH resource using the corresponding UCI multiplexing rules for the overlapping PUCCH resources with the same starting symbol.
  FFS: When one SR PUCCH resource overlaps with two non-overlapping CSI PUCCH
Basically, based on previous agreements, when one of multiple SR PUCCH resources overlap with a CSI PUCCH resource configured with PF2/3/4, the multiplexing rule is that X bits are added to the CSI bits.
  Note: SR and CSI PUCCH resources can have same or different starting symbols.
When in the overlapping group of SR and CSI PUCCH resources, there are two or more non-overlapping CSI PUCCH resources, it is not clear:
  1) Which CSI PUCCH resource carriers the X bits
  2) Which SR PUCCH resource IDs are included X bits

## Slide 15: Summary Proposal
When two or more configured non-overlapping CSI PUCCH resources overlap with one or more configured SR PUCCH resources in a slot such that among these PUCCH resources, any of these PUCCH resources overlaps at least with another one,
  Alt 1: SR is multiplexed and transmitted with CSI on the earliest in time CSI PUCCH resource.
  Supportive companies: E///, DCM, Panasonic. OPPO, QC, Spreadtrum comm, MTK
  Alt 2: This is an error case due to poor configuration. No need for specification.
  Supportive companies: Nokia, Intel
Alt 3: When a SR PUCCH resource overlaps with one or more non-overlapping CSI PUCCH resources, the SR is multiplexed with the earliest CSI PUCCH resource.
  Supportive companies: LG, Lenovo, MOT, CATT

## Slide 16: Discussion
Alt 1 and Alt 3 are compared for 3 different cases. The outcome for case 1 and 2 is the same. The difference appears only for case 3.
Note that a benefit of Alt 3 that was discussed during offline was having the option of multiplexing some SR later (on 2nd CSI PUCCH resource), allows to send more positive SR potentially if triggered.
As it is illustrated, this is only valid in the case that only transmission occasions of an SR PUCCH overlap with a second CSI resource (SR3 in green in case 3). Otherwise, the SR would be multiplexed with 1st CSI PUCCH resource.
It is important to discuss the consequences of these design choices.

## Slide 17: Discussion - Alt 1
CSI1
CSI2
SR1
SR2
SR2
SR3
CSI1+
SR1+SR2+SR3
CSI2
Case 3
Slot n
Case 1
CSI1
CSI2
SR1
CSI1+
SR1
CSI2
Case 2
Slot n
CSI1
CSI2
SR1
CSI1+
SR1
CSI2
Case 1
Slot n
SR1

## Slide 18: Discussion - Alt 3
CSI1
CSI2
SR1
SR2
SR2
SR3
CSI1+
SR1+SR2
CSI2+
SR3
CSI1
CSI2
SR1
CSI1+
SR1
CSI2
Case 2
Slot n
Case 3
Slot n
CSI1
CSI2
SR1
CSI1+
SR1
CSI2
Case 1
Slot n
SR1