## Slide 1: WF on PUSCH time-domain resource allocation
NTT DOCOMO, Samsung, Panasonic, KDDI, OPPO, Ericsson, CATT, AT&T, vivo, Nokia, NSB, NTT, Sharp
3GPP TSG RAN WG1 Meeting 93
Busan, Korea, 21st – 25th May 2018
Agenda item: 7.1.3.3.1
R1-1807875

## Slide 2: Background
“Mini-slot” for mmw operation with analog-BF is necessary
It is essential to achieve high resolution of time-domain resource allocation for all channels
PDCCH/PDSCH
 Up to 3 beams/slot
PUCCH/PUSCH
 Up to 7 beams/slot

## Slide 3: Problem
For mmw with analog-BF operation, it is important to make sure that DL assignment and UL grant can be delivered for a given UE at one time
  Otherwise, gNB needs to form the beam to the UE twice just for the purpose of delivering UL grant
4-bit PUSCH time-domain RA cannot realize the above

## Slide 4: Proposal
Increase the max number of bits for PUSCH time-domain RA field in DCI format 0_1 from 4 to 6.
  Corresponding RAN1 spec need to be changed.
Corresponding RAN2 parameters need to be changed.
  Send a LS to RAN2 to update the parameter.

## Slide 5: Text proposals for 212 and 331