## Slide 1: WF for OCC configuration of PF1
NTT DOCOMO, Qualcomm, OPPO, Panasonic, Nokia, NSB, Samsung, KDDI, Intel, MediaTek, vivo, InterDigital, Huawei, HiSilicon, [SoftBank]
3GPP TSG RAN WG1 Meeting #93
Busan, South Korea, May 21st – 25th, 2018
Agenda Item: 7.1.3.2.2 Document for: Discussion and Decision
R1-1807899

## Slide 2: Background
Ambiguity in OCC configuration for PF1
  The configuration is determined by “Intra-slot frequency hopping” or “No intra-slot frequency hopping” in 6.3.2.4.1 of TS 38.211
  The conditions
    PUCCH-frequency-hopping = “disabled”
    PUCCH-frequency-hopping = “enabled” with the different PRB for two hops
    PUCCH-frequency-hopping = “enabled” with the same PRB for two hops
  Which includes iii, “intra-slot hopping” or “No intra-slot hopping”?
    Also, it is unclear that phase coherence is kept or not for enabled

## Slide 3: Proposal
In 6.3.2.4.1 of TS38.211,
  No intra-slot frequency hopping is replaced as higher layer parameter PUCCH-frequency-hopping = “disabled”.
  Intra-slot frequency hopping is replaced as higher layer parameter PUCCH-frequency-hopping = “enabled”.
  Add the following:
    The channel over which a symbol on the antenna port used for UL transmission is conveyed can be inferred from the channel over which another symbol on the same antenna port is conveyed only if the two symbols correspond to the same frequency hop, when frequency hop is enabled, irrespective of whether the frequency hop distance is zero or not.