## Slide 1: Proposals on remaining issues on overlapping PUCCHs
Ericsson
3GPP TSG RAN WG1 Meeting 93
Busan, Korea, 21st – 25th May 2018
Agenda item: 7.1.3.2.1
R1-1807857

## Slide 2: Proposals 1 (related to FFS in Step1&2 agreements):
When a PUCCH resource carrying SR and other UCI overlaps with PUSCH, if the UCI on PUCCH is going to be multiplexed on PUSCH, the SR bits are dropped from the UCI before multiplexing on PUSCH.

## Slide 3: Proposal 2 (section 2.4 in R1-1807662)
When there are both HARQ-ACK for PDSCH scheduled by DCI and HARQ-ACK for SPS PDSCH within a slot to be transmitted on PUCCH, the UE determines one PUCCH resource for transmission of all HARQ-ACK bits based on the ARI and total number of HARQ-ACK bits in the slot.

## Slide 4: Background on Proposal 3 (section 2.1 in R1-1807662)
When the HARQ-ACK/SR PUCCH resource determined by ARI and the configured CSI PUCCH resource overlap in a slot, if the UE is configured with only one PUCCH resource set for UCI transmission including HARQ-ACK and simultaneous transmission of HARQ-ACK/SR and CSI is enabled, select from one of the following alternatives:
  Alt 1: The UE is not expected to transmit the corresponding HARQ-ACK/SR and the CSI report in a PUCCH resource in that slot.
    Supportive companies: E//, Spreadtrum Comm., OPPO, Intel.
  Alt 2: HARQ-ACK/SR and CSI are transmitted together by PUCCH resource for CSI
    Supportive companies: ZTE, Panasonic, CATT, Lenovo, MOT, DCM, Vivo, Nokia
    Note: The timeline requirements for transmission of HARQ-ACK on CSI PUCCH resource is met.
  Alt 3: HARQ-ACK/SR is transmitted on the HARQ-ACK/SR PUCCH resource and CSI reporting is dropped in that slot.
    Supportive companies: Panasonic, Vivo, LG
  Alt 4: The UE is not expected to be provided simultaneousHARQ-ACK-CSI = TRUE.
    Supportive companies: Samsung, E///

## Slide 5: Proposal 3(section 2.1 in R1-1807662)
Proposal a:
  When a UE is configured for one PUCCH resource set for UCI transmission including HARQ-ACK, the UE is not expected to be provided with simultanouesARQ-ACK-CSI=TRUE.
  Supportive companies: Samsing, E//, Spreadtrum Comm., OPPO, Intel, Panasonic, Vivo, LG, QC
Proposal b:
  When a UE is configured with one PUCCH resource set for UCI transmission including HARQ-ACK and simultanouesARQ-ACK-CSI=TRUE, the HARQ-ACK/SR bits for PDSCHs scheduled by PDCCH are transmitted together with CSI on the PUCCH resource for CSI.
  Supportive companies: ZTE, CATT, Lenovo, MOT, DCM, Vivo, Nokia

## Slide 6: Proposal 4:
When a PUCCH resource with format 2 or 3 or 4 for carrying a UCI including only HARQ-ACK bits corresponding to granted PDSCH, overlaps with K SR PUCCH resources, the SR and the UCI bits are multiplexed using the same PUCCH format 2 or 3 or 4 resource.

## Slide 7: Proposals on SR ID
Discuss and decide on proposals in section 2.2 in R1-1807662.