## Slide 1: Discussion on Sidelink Bi-mode Transmission in NR-V2X
3GPP TSG-RAN WG1 Meeting#94
Gothenburg, Sweden, 20th - 24th August 2018
R1-1809775

## Slide 2: Introduction
In RAN #80 meeting, the new SID NR-V2X has been agreed with the objective 1 [1], as follows
Use case groups in NR-V2X
  Vehicle platooning, advanced driving, extended sensors, remote driving
  Stringent requirements: the maximum end-to-end latency of 3-10ms, the reliability of 99.99-99.999%, the packet size up to 60000 bytes
Enhance the Uu-based sidelink resource allocation mechanism and propose sidelink bi-mode transmission
  Mode-3 ensures higher reliability but with longer latency, while mode-4 offers quicker delivery opportunity but with poorer reliability.
  Bi-mode transmission scheme enables to fulfill the stringent latency and the stringent reliability, simultaneously.
3: Uu-based sidelink resource allocation/configuration (LTE V2X Mode3-like and Mode4-like) [RAN1, RAN2]:
Identify necessary enhancements of LTE Uu and NR Uu to control NR sidelink from the cellular network
Identify necessary enhancements of NR Uu to control LTE sidelink from the cellular network

## Slide 3: Performance Evaluation for PSCCH
At BLER of , SNR = 6dB for 1x2 ant., and SNR = -1dB for 1x4 ant.
As a result, PSCCH is not worse than PUCCH

## Slide 4: Sidelink Bi-mode Transmission
Phase-1: Vehicle-1 transmits the SCI over PSCCH and its associated TB over PSSCH, based on the procedure of mode 4, as an initial transmission
  Both Vehicle-2 and gNB decode the packet, first in SCI and then associated TB
  Very low latency, but fairly poor reliability, due to the inevitable channel collision
Phase-2: gNB, based on the reception status, transmits the PDCCH using DCI to inform the sub-channel information to Vehicle-1, and grant for its mode-3 based repetition
Phase-3: Vehicle-1, relying on the DCI information, transmits the SCI over PSCCH and its associated TB over PSSCH, to Vehicle-2 for its repetition through mode-3 based PC5 link

## Slide 5: Observations
The mode-4 based sidelink initial transmission in Phase-1 can realize a very short transmission latency (e.g., 3ms latency), and meanwhile guarantee the somewhat reliability (e.g., 90% PRR)
Unlike LTE-V2X mode-3, gNB enables to send a DCI in Phase-2 as a grant to inform the exact sub-channel information right after the PSCCH detection, so that the latency of mode-3 in repetition can be significantly reduced. This ensures the overall system latency
The mode-3 based sidelink repetition transmission in Phase-3, fully controlled by eNB, guarantees the stringent reliability (e.g., 99.999%)
With the mode-4 based sidelink initial transmission, the BLER, in general, can be kept low enough (e.g., 5-10% BLER), as a coarse transmission. This significantly reduces the necessity of the mode-3 based sidelink repetition, so as to ensure the overall performance in terms of low latency, high reliability, and high channel efficiency.

## Slide 6: Proposal
gNB has the capability to monitor the sidelink mode-4 based initial transmission, detect at least the associated SCI, and control the sidelink mode-3 based repetition.