## Slide 1: Summary on the phase continuity issue of intra-band EN-DC
Intel
R1-1809823
3GPP TSG RAN WG1 Meeting 94
Gothenburg, Sweden, August 20th-24th, 2018
Agenda item 7.1.4

## Slide 2: Issue description
For a common power amplifier (PA) structure, phase discontinuity of transmitted signal happens in some cases, e.g. starting positions of NR and LTE are not aligned.
  When the PA is shared, transmission power change of one CC may lead to the analog gain change of the shared PA, distorting the channel estimation and significantly degrading the uplink performance of both LTE and NR.
The issue can happen for both intra-band EN-DC and Intra-band CA with a single PA
In LTE, the similar situation happens for the case of parallel transmission of SRS and PUSCH for intra-band CA. UE is allowed to drop SRS transmission to solve this problem.
==================Cited from TS 36.213========================== For the case when an SRS transmission in a first serving cell happens to overlap in the same symbol as a PUSCH transmission in a second serving cell, and the first and second serving cells are in the same TAG, same band, and use the same cyclic prefix, the UE may drop the SRS transmission.

## Slide 3: Proposal (1/2)
Option 1:
  Introduce UE capability to indicate whether the following is needed or not for intra-band EN-DC or NR CA on a per band combination basis
    For a same band combination, it is assumed that this UE capability is not indicated together with single UL transmission.
  Option 1-1:
    For intra-band EN-DC and intra-band Carrier Aggregation (CA), the UE is not expected to be configured or scheduled with overlapped UL transmissions across CCs that do not meet the following conditions:
      The starting and end times are aligned;
      Frequency hop boundaries are aligned
        Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary
    PRACH is transmitted if PRACH is triggered and the above conditions are not met for overlapped transmissions.
    Supported companies:
      Qualcomm[2nd preference], Intel, MediaTek, [Huawei], [Sprint], CATT [2nd preference], Panasonic, Samsung[2nd preference]
  Option 1-2:
    For intra-band EN-DC and intra-band Carrier Aggregation (CA), the UE may drop the SCG transmissions in case of EN-DC or drop the later transmissions in case of NR CA, if the overlapped UL transmissions across CCs do not meet the following conditions:
      The starting and end times are aligned;
      Frequency hop boundaries are aligned
        Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary
    PRACH is transmitted if PRACH is triggered and the above conditions are not met for overlapped transmissions.
    Supported companies:
      [Ericsson]

## Slide 4: Proposal (2/2)
Option 2:
  Option 2-1
    For intra-band EN-DC and intra-band Carrier Aggregation (CA) and subcarrier spacing of SCG transmission(s) is 15kHz, the UE is not expected to be configured or scheduled with overlapped UL transmissions across CCs that do not meet the following conditions:
      The starting and end times are aligned;
      Frequency hop boundaries are aligned
        Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary
    PRACH is transmitted if PRACH is triggered and the above conditions are not met for overlapped transmissions.
    Supported companies:
      Qualcomm [1st preference], CATT [1st preference], Samsung[1st preference]
  Option 2-2
    For intra-band EN-DC and intra-band Carrier Aggregation (CA) and subcarrier spacing of SCG transmission(s) is 15kHz, the UE may drop the SCG transmissions in case of EN-DC or drop the later transmissions in case of NR CA, if the overlapped UL transmissions across CCs do not meet the following conditions:
      The starting and end times are aligned;
      Frequency hop boundaries are aligned
        Either both NR and LTE doesn’t hop or both NR and LTE hops at the same boundary
    PRACH is transmitted if PRACH is triggered and the above conditions are not met for overlapped transmissions.