## Slide 1: Limitations on EN-DC PHR
Qualcomm
R1-1809832
3GPP TSG RAN WG1 #94
Gothenburg, Sweden, August 20 - 24, 2018
Agenda item 7.1.4

## Slide 2: Proposal
Adopt one of the following alternatives
  Alt.1
    The PHR reported in LTE is not dependent on NR allocation, i.e. the LTE PHR in EN-DC is always calculated with the assumption of no NR transmission
  Alt.2
    The PHR reported in LTE depends only on NR scheduling information received simultaneously or earlier than LTE scheduling information
      Scheduling information includes for example PDCCH scheduling UL or PDCCH scheduling DL for which HARQ is sent in the UL, PDCCH including TPC, etc.
Note: Current RAN1 LTE specification implies Alt.1
Note: If RAN4 adopts EN-DC MPR/A-MPR framework where LTE maximum power depends only on LTE information then Alt.1 would be adopted