## Slide 1: Proposals on intra-band EN-DC MPR handling
Qualcomm
R1-1809833
3GPP TSG RAN WG1 #94
Gothenburg, Sweden, August 20 - 24, 2018
Agenda item 7.1.4

## Slide 2: Proposals
Alt.1. MPR/A-MPR applies to combined power
  LTE power is determined independent of NR (i.e. with assuming no NR transmission)
  LTE power is not changed if a later NR grant is received
    UE is expected to adjust NR power to take advantage of relaxation provided by MPR
Note: Alt.1 requires no RAN1 specification changes
Note: Alt.1. depends on adoption by RAN4
Note: Alt.1 does not depend on timeline constraints
Note: Whether Alt.1 needs new MPR/A-MPR values is up to RAN4

## Slide 3: Proposals
Alt.2. Delayed NR
  LTE power is determined with taking into account NR scheduling information received ‘in time’
  FFS handling of NR scheduling information received not in time
  FFS Optional/Mandatory
  FFS if Delayed NR method is configurable
Note: NR scheduling information includes DCI scheduling UL, DCI scheduling DL for which HARQ-ACK is sent, power control, etc.
Note: Alt.2. depends on adoption by RAN4

## Slide 4: Proposals
Alt.3. Change in power dropping rule
  (1) the UE calculates LTE power (P_LTE_only) considering no NR Tx
  (2) the UE calculates NR power (P_NR_only) considering no LTE Tx
  (3) the UE calculates the LTE power (P_L) and NR power (P_N) according to the dynamic power sharing rule and RAN4 MPR/A-MPR definition
  (4) the UE performs the following
    If both P_LTE_only == P_L && P_NR_only == P_N
      UE transmits LTE and NR at powers P_L and P_N, respectively
    Else
      UE chooses a new P_N’ power within the bounds 0 <= P_N’ < P_N
      UE determines LTE power P_L’ based on P_N’
                If P_N’ == 0, P_L’ = P_LTE_only
                Elseif P_N’ == P_N, P_L’ = P_L
                Else P_L < P_L’ < P_LTE_only
      UE transmits LTE and NR at powers P_L’ and P_N’, respectively

## Slide 5: Other Proposals
Capability signaling for LTE processing time
  Doesn’t change LTE HARQ timeline
  FFS values
  FFS PHR impact

## Slide 6: Combined proposal (QC-only proposal)
Adopt Alt.1 with the following modification
  UE is allowed to drop NR if the MPR related NR power scaling is more than XdB or if the LTE-NR PSD difference is more than XdB
  X is up to RAN4
Potentially adopt Alt.2 if FFS can be resolved
  New signaling for
    ‘1-bit’ to configure Alt.2 mode
    ‘1-bit’ for Alt.2 UE capability
No new signaling for LTE processing time capability