## Slide 1: Offline discussion on LTE sTTI for EN-DC
LG Electronics, …
3GPP TSG RAN WG1 Meeting 94 R1-1809843
Gothenburg, Sweden, August 20 - 24, 2018
Agenda item: 7.1.4

## Slide 2: Background
Q) Is there any more specification impact to support LTE sTTI for EN-DC?
A) There is no more specification impact except for adopting LTE sTTI TDD scheduling/HARQ timing for case 1.
  For scheduling, limited specification impact to adopt LTE sTTI TDD scheduling/HARQ timing for case 1 is needed, and for MPR, it may require RAN4 work.

## Slide 3: Proposal
For supportability of LTE sTTI for EN-DC in Rel.15, one of the following options is determined:
  Option 1: A UE is not expected to be configured with sTTI if EN-DC is configured in Rel-15. Enhancement of sTTI in EN-DC scenario is treated under MR-DC WI in Rel-16.
  Option 2: LTE sTTI is supported for EN-DC for only semi static power sharing for only 7OS LTE sTTI. For the case 1 configuration, LTE sTTI scheduling/HARQ timing is adopted.
  Option 3: EN-DC UEs can be configured with LTE sTTI only if semi-static power splitting between MCG and SCG is configured, i.e. P’_LTE+P’_NR <= P’_total_EN-DC.