## Slide 1: Proposal on Rel-15 UE feature group 6-23, 4-19 and 8-2
Intel
R1-1809883
3GPP TSG RAN WG1 #94
Gothenburg, Sweden, August 20th – 24th
Agenda Item: 7.1.7
Document for: Discussion/Decision

## Slide 2: FG 6-23 (New)
Agreement on Thursday

## Slide 3: FG 6-23 (New) – Cont’d
Proposal
  Add FG 6-23
    FG name & component: Incapability motivated by impacts of PA phase discontinuity with overlapping transmissions with non-aligned starting or ending times or hop boundaries across carriers for intra-band EN-DC, intra-band CA, and FDM based ULSUP
    Need for gNB to know: Yes
    Type: Type 3 (per band per band combination)
    Need of FDD/TDD differentiation: No
    Need of FR1/FR2 differentiation: N.A.
    Responsible WG: RAN1
    RAN WG recommendation: Optional with capability signaling

## Slide 4: FG 4-19: SR/HARQ-ACK/CSI multiplexing once per slot using a PUCCH (or piggybacked on a PUSCH)
Proposal
4-1 | Basic UL control channel | 1) PUCCH format 0 over 1 OFDM symbols once per slot 2) PUCCH format 0 over 2 OFDM symbols once per slot with frequency hopping as “enabled” 3) PUCCH format 1 over 4 – 14 OFDM symbols once per slot with intra-slot frequency hopping as “enabled” 5) One SR configuration per PUCCH group 6) HARQ-ACK transmission once per slot with its resource/timing determined by using the DCI 7) Multiplexing of SR and HARQ-ACK on a PUCCH SR/HARQ multiplexing once per slot using a PUCCH (or piggybacked on a PUSCH) when SR/HARQ-ACK are supposed to be sent by overlapping PUCCH resources with the same starting symbols in a slot 8) HARQ-ACK piggyback on PUSCH 9) Semi-static beta-offset configuration for HARQ-ACK |  | Yes |  | N.A. | N.A. | N.A. |  | RAN4 to check feasibility of frequency hopping for PUCCH formats for FR2 |  | Mandatory without capability signaling | Mandatory without capability signaling
4-19 | SR/HARQ-ACK/CSI multiplexing once per slot using a PUCCH (or piggybacked on a PUSCH) when SR/HARQ-ACK/CSI are supposed to be sent | Overlapping PUCCH resources have the same starting symbols in a slot while precluding the case of SR/HARQ-ACK by overlapping PUCCH resources with the same starting symbols in a slot |  | Yes |  | Type 4 | No need | Yes |  |  | RAN1 | Mandatory with capability signaling | 
4-19a | SR/HARQ-ACK/CSI multiplexing once per slot using a PUCCH (or piggybacked on a PUSCH) when SR/HARQ-ACK/CSI are supposed to be sent | Overlapping PUCCH resources have different starting symbols in a slot |  | Yes |  | Type 4 | No need | Yes |  |  | RAN1 | Optional with capability signaling | 
4-19b | SR/HARQ-ACK/CSI multiplexing more than once per slot using a PUCCH (or piggybacked on a PUSCH) when SR/HARQ-ACK/CSI are supposed to be sent | Overlapping PUCCH resources have same or different starting symbols in a slot |  | Yes |  | Type 4 | No need | Yes |  |  | RAN1 | Optional with capability signaling | 

## Slide 5: FG 8-2/8-2a/8-2b: Basic power control
Proposals
8-2 | Basic power control operation | 1) Accumulated power control mode for closed loop 2) 1 TPC command loop for PUSCH, PUCCH respectively 3) One or multiple DL RS configured for pathloss estimation 4) Multiple DL RS up to 4 configured for pathloss estimation in FR2 5) One or multiple p0-alpha values configured for open loop PC 6) PUSCH power control 7) PUCCH power control 8) PRACH power control 9) SRS power control 10) PHR |  | Yes |  | Type 4 | No need | No need |  |  |  |  | Mandatory without capability signaling
8-2a | More than one DL RS configured for pathloss estimation in FR1 | More than one DL RS up to 4 configured for pathloss estimation in FR1 | 8-2 | Yes |  | Type 4 | No need | Yes |  |  |  |  | Optional with capability signaling