## Slide 1: NE-DC Power Sharing Options
7.1.4

## Slide 2: Option 1A
A UE configured with NE-DC is configured with P_LTE for LTE, r(<=1), and with P_NR for NR
LTE Power limit is set as follows
  For an LTE subframe that overlaps with any possible NR UL symbol(s)
    Set LTE power limit Pcmax<=P_LTE*r;
  Otherwise
    Set LTE power limit Pcmax<=P_LTE.
A possible NR UL symbol is identified as an NR symbol configured as flexible or UL based on cell-specific or UE-specific (if configured) tdd_UL_DL_Configuration_Common/dedicated.
NR power limit is set as Pcmax <= P_NR in all slots
When there is simultaneous transmission for LTE and NR with actual power p_lte_power and p_nr_power respectively, such that p_lte_power + p_nr_power > X_total, UE will scale down p_nr_power until the total transmit power does not exceed X_total
  X_total is computed based on r*P_LTE, P_NR
Notes
  At least from RAN1 perspective, there will be no change to other mechanisms (i.e., Power class, p-UE-FR1, Pemax) specified in RAN4 to limit UE maximum transmit power
  Specification details of LTE power limit, NR power limit and X_total will be handled by RAN4

## Slide 3: Option 1B
A UE configured with NE-DC is configured with P_LTE for LTE and with P_NR for NR
LTE Power limit is set as follows
  For an LTE subframe that overlaps with any possible NR UL symbol(s)
    Set LTE power limit Pcmax<=P_LTE
  Otherwise
    Set LTE power limit Pcmax without considering P_LTE
A possible NR UL symbol is identified as an NR symbol configured as flexible or UL based on cell-specific or UE-specific (if configured) tdd_UL_DL_Configuration_Common/dedicated.
NR power limit is set as Pcmax <= P_NR in all slots
When there is simultaneous transmission for LTE and NR with actual power p_lte_power and p_nr_power respectively, such that p_lte_power + p_nr_power > X_total, UE will scale down p_nr_power until the total transmit power does not exceed X_total
  X_total is computed based on P_LTE, P_NR
Note
  At least from RAN1 perspective, there will be no change to other mechanisms (i.e., Power class, p-UE-FR1, Pemax) specified in RAN4 to limit UE maximum transmit power
  Specification details of LTE power limit, NR power limit and X_total will be handled by RAN4

## Slide 4: Background (1) – From RAN1#94bis
Option 1a:
  For NE-DC dynamic power sharing, the following are specified:
  UE is configured with p_LTE for LTE, r(<=1), and with p_NR for NR
  For an LTE subframe that overlaps with any possible NR UL symbol(s), set LTE power limit Pcmax<=p_LTE*r; otherwise, set power LTE limit Pcmax<=p_LTE.
    A possible NR UL symbol is identified as an NR symbol configured as flexible or UL based on cell-specific or UE-specific (if configured) tdd_UL_DL_Configuration_Common/dedicated.
  The remaining power up to p_NR is allocated to NR by setting NR power limit as Pcmax<= min(p_NR, p_total-p_lte_actual) where p_lte_actual is the power allocated to LTE.
  Implications:
  MCG power is scaled
  Pcmax for LTE power control needs to be modified

## Slide 5: Background (2) -- From RAN1#94bis
Option 1b:
  For NE-DC dynamic power sharing, the following are specified:
  UE is configured with p_LTE for LTE, and with p_NR for NR
  For an LTE subframe that overlaps with any possible NR UL symbol(s), set LTE power limit Pcmax<=p_LTE; otherwise, set power LTE limit to Pcmax (p_LTE not considered).
    A possible NR UL symbol is identified as an NR symbol configured as flexible or UL based on cell-specific or UE-specific (if configured) tdd_UL_DL_Configuration_Common/dedicated.
  The remaining power up to p_NR is allocated to NR by setting NR power limit as Pcmax<= min(p_NR, p_total-p_lte_actual) where p_lte_actual is the power allocated to LTE.
  Implications:
  MCG power is scaled
  P_cmax for LTE power control needs to be modified and possibly other restrictions
  No capability to keep power same across all subframes if p_LTE is less than Pcmax