## Slide 1: Highlights on NR UE feature list
Ericsson
3GPP TSG RAN WG1 #95
Spokane, USA, November 12th – 16th, 2018
Agenda item – 7.1.7
R1-1813253

## Slide 2: 2-20 beam correspondence
Motivation
  Exploiting beam correspondence allows measurement and reporting from DL beam management procedures to support UL beamforming
    Avoids excessive air interface load from UL beam management procedures based on SRS beam sweeping (per UE)
    Simplifies network operation
  All UEs must be capable of a certain degree of beam correspondence to be able to access the network
    Transmit PRACH/MSG3 in the same direction as the detected SS/PBCH block
  Additional UL beam management procedures (SRS beam sweep) to support high gain (narrow) UL beamforming is an optimization
Proposal:
  Mandatory without capability signaling for FR2

## Slide 3: 2-33 CSI-RS capability
Motivation
  UE complexity driven by the number simultaneously active CSI-RS resources/ports, not the number of configured ones
    Introduction of Components 4 & 5 (simultaneous resources/ports) supersedes the need to limit configured CSI-RS resources/ports
    Restricting the number of configured CSI-RS resources can severely impact network performance and gNB flexibility
    CSI-RS resources are configured per BWP, too low capability necessitates RRC reconfiguration upon BWP switch
Proposals
  2-33:
    Component 1:16 configured CSI-RS resources is the smallest possible value
    Component 2: Remove component on maximum number of configured ports, this impacts neither complexity nor memory
    Component 3: 4 configured CSI-IM resources is the smallest possible value
    Component 5: 32 simultaneous NZP CSI-RS ports is the smallest possible value for FR1, 8 is smallest value for FR2

## Slide 4: 2-51 TRS
Motivation
  2-51 C 4: For FR2, up to 64 SSBs, corresponding to different beams, can be configured in a cell. Each beam should be associated to a TRS for tracking in a corresponding configured TCI state
    Otherwise, RRC reconfiguration is needed even when the UE moves within the cell!
    It is already mandatory for the UE to support 64 configured TCI states
  2-51 C5:
    Since QCL Type A cannot be conveyed across CCs, each CCs will need a separate set of TRSs
    In FR2, CA will be deployed already in the initial phase
    To support 8 carriers with a reasonable number of beams, close to 100 TRSs will be needed
  The number of “active” TRSs a UE can simultaneously track is reported as separate capability in Component 3.
  Note that one TRS is configured using 2 or 4 CSI-RS resources. The maximum number of CSI-RS resources that can be configured also provides an upper bound on the maximum number of TRSs
  Additionally, allowing UE to report burst length 1 or 2 introduces fragmentation as one TRS per group of Ues must be configured which leads to unnecessary overhead.
Proposals
  2-51:
    Component 4: 64 configured TRS per CC is the smallest possible value
    Component 5: 128 configured TRS across CCs is the smallest possible value
    Component 2 (burst length) to be removed, i.e. mandate support of both burst lengths

## Slide 5: 2-55 srs tx switch
Motivation
  The FG name for 2-55, “SRS Tx switching”, is misleading, since it controls the configuration of SRS transmission for DL CSI Acquisition purpose, with or without actual antenna switching
    A UE can report support of Tx antenna switching (1T2R, 2T4R, 1T4R) or support of only SRS transmission without switching (1T1R, 2T2R, 4T4R)
    A UE supporting ‘1T1R’, ‘2T2R’, or ‘4T4R’ should be capable of sounding on a fixed (non-switched) set of antennas according to its reported capability in FG 2-53
  Reciprocity-based DL beamforming is central to NR design
    Support of SRS transmission, without antenna switching, for DL CSI acquisition purpose crucial for NW performance
    Support of basic antenna switching (1T2R) will give a significant capacity boost and enable multi-layer transmission also in reciprocity-based operation
Proposal:
  2-55 is Mandatory with UE capability signaling for FR1
    Rename the FG to “SRS transmission for DL CSI acquisition”
    Change the wording “SRS antennas” to “subset/set of antennas sounded by SRS”
    Mandatory with capability signaling to support ‘1T2R’ and at least one of {‘1T1R’, ‘2T2R’, or ‘4T4R’} according to the UE’s reported capability in FG 2-53
    Clarify that ‘1T1R’, ‘2T2R’, or ‘4T4R implies sounding using the maximum number of ports/resource a UE supports according to the UE’s reported capability in FG 2-53 (may be a subset of Rx antennas)
      Clarify that this applies at least to UE classes which use the same antennas for Tx and Rx

## Slide 6: 2-59 Configured Spatial relations
Motivation
  The FG 2-59 proposes to introduce a limitation in the number of configured spatial relations.
    However, as has been concluded for FG 2-4 C-2, there is no significant complexity impact of the number of configured spatial relations.
Proposal:
  2-59 is removed