## Slide 1: R1-1903580 Outcome of offline discussion #2 for low PAPR RS
Agenda: 7.2.8.5
For: Decision
Wednesday February 27, 2019
3GPP WG1 meeting #96, Athens, Greece

## Slide 2: Offline agreement
For PUSCH DMRS with pi/2-BPSK modulation, two RRC parameters ScramblingID0 and ScramblingID1 can be configured by RRC as for CP-OFDM DMRS (16 bit per ID)
Used in cinit for length ≥30 as n_ID^{n_SCID=0}, n_ID^{n_SCID=1}
For length<30, these parameters are used as N_ID^PUSCH is configured as either ScramblingID0 or ScramblingID1 depending on DCI
DCI indicates n_SCID={0,1} dynamically, without increasing DCI size to select the above parameter
  Antenna port indication is re-used for n_SCID indication as follows:
    DMRS port 1000,1002,1004 and 1006 are interpreted as port 1000,1002,1004 and 1006 , respectively, with n_SCID=0
    DMRS port 1001,1003,1005 and 1007 are interpreted as port 1000,1002,1004 and 1006 , respectively, with n_SCID=1

## Slide 3: MSG3
For further discussion
  Whether to support Rel-16 DMRS or pi/2 BPSK for Msg3
Discussion outcome, make decision online
  Alt.1 Rel.16 DMRS is not supported for MSG3 transmissions, Rel.15 behavior is used for MSG3
  Alt.2 After RRC, Rel.16 DMRS can be used for MSG3, details FFS
  Alt.3, Rel.16 DMRS for MSG3 can be used both for initial access and in connected mode, by introducing pi/2 BPSK PUSCH for initial access, further details FFS

## Slide 4: Applicability
Agreement
  If Rel-16 DMRS is configured by RRC for PUSCH with pi/2 BPSK modulation, the Rel-16 DMRS applies when scheduled by DCI formats 0_1 and 0_0 and using at least C-RNTI, CS-RNTI, SP-CSI-RNTI and MCS-C-RNTI, when applicable or PUSCH transmission with configured grant
  FFS: Applicable search spaces for DCI format 0_0
  FFS: Applicability for TC-RNTI
  Note: It is up to the editor whether/how to capture this agreement
Outcome from offline:
  Proposal (related to the FFS in the agreement above):
    Rel.16 DMRS for USS is supported
    Offline Working assumption that Rel.16 DMRS for CSS is supported for DCI format 0_0 using C-RNTI, CS-RNTI and MCS-C-RNTI