## Slide 1: WF on PTRS multiplexing with other RSs for CP-OFDM
3GPP TSG RAN WG1 NR Ad-Hoc#2 R1-1711986
Qingdao, P.R. China 27th – 30th June 2017
Agenda Item: 5.1.2.4.1
ZTE

## Slide 2: Background
Agreements in RAN1#89
  The RBs containing PTRS can be derived from the scheduled RBs and the associated frequency density
  For a given RB, if present, one PTRS port should be mapped on one subcarrier carrying one or more DMRS ports of the associated DMRS port group
    FFS: to support different subcarriers by complementary option
  Support non-overlapping between PTRS and CSI-RS
    FFS whether PTRS or CSI-RS should be punctured or shifted on overlapping part if PTRS and CSI-RS are collided
  Support non-overlapping between PTRS and SRS
    FFS whether PTRS or SRS should be punctured or shifted on overlapping part if PTRS and SRS are collided
  FFS: Support non-overlapping between PTRS and SS block
    FFS whether PTRS or SS block should be punctured or shifted on overlapping part if PTRS and SS block are collided
Notes: i

## Slide 3: Proposal 1
  PTRS should be punctured on overlapping part when PTRS and CSI-RS are collided.
  PTRS should be punctured on overlapping part when PTRS and SRS are collided
  PTRS should be punctured on overlapping part if PTRS and SS block are collided.
Notes: i