## Slide 1: [CB708]
Offline Discussion of WA: choose the final carriers based on lowest CBR value

## Slide 2: Problem Analysis
Select the lowest CBR definitely helps to avoid UE to select a busy high-CBR carrier.
But for multiple low-CBR carriers, this unnecessarily force each UE to select a different carrier for its transmission, because
  CBR measurement does not count UE’s own usage of this carrier. Thus, the CBR of UE’s current Tx carrier, when measured by this UE, is naturally lower than the actual CBR measured by another UE.
  This means, if CBR of candidate carriers are same or comparable, the UEs follow “lowest CBR” are likely to end up selecting different TX carriers.
Need a balanced scheme which can both “avoid heavy-load” and “avoid uncecessary diversified carrier selections”.

## Slide 3: Proposed solution
Define a RRC-configured parameter of CBR margin:
Suppose the lowest CBR of candidate carriers is CBRmin
If there is more than 1 candidate carriers whose CBRs are within [CBRmin , CBRmin +CBRmargin], the selection among this subset of carriers is left to UE implementation.
Otherwise, choose the carrier of CBRmin.

## Slide 4: Discussion Results
Company view:
  There is a problem with lowest CBR. 5( QC, ZTE, OPPO, ITL, vivo)
  There is no problem with lowest CBR: 7 (Nokia, LG, Samsung, CATT, Hyundai, Ericsson, Huawei ).
Conclusion: Confirm the WA (using the carrier with lowest CBR).