## Slide 1: Way forward on provision of time reference
Huawei, HiSilicon, Ericsson, Deutsche Telekom, Vodafone, Telecom Italia, China Telecom
3GPP TSG-RAN2 Meeting #102
Busan, Korea, 21 – 25 May 2018
R2-1809154

## Slide 2: Background
The WI LTE HRLLC targets June 2018 (RAN#80) for completion. RAN2#102 is the last meeting before completion of the WI.
Provision of time reference is a second priority item for Rel-15 as identified in RAN plenary endorsed RP-180586.
At RAN2#102, under AI 9.15.4, an email discussion report of [101bis#50] and some contributions on the topic were submitted.
In RAN2#102 LTE session R2-1809052 Proposed solution on Provision of Time Reference was presented and very briefly discussed.
There is market demand to provide a solution for this use case in Release 15.

## Slide 3: Proposed WF (1/2)
In order to answer the market demand and provide a solution for this use case in Release 15, the cosigning companies ask RAN2 to agree on the proposals revised from R2-1809052, and to agree on an email discussion of the CRs (36.331, 36.306) for those proposals.
Proposal 1: The granularity of time reference is 0.25 us.
Proposal 2: In addition, an inaccuracy indication is optionally sent:
The indication indicates inaccuracy of a time reference information
  If the inaccuracy indication is transmitted, then the time reference is within the range {the time reference – inaccuracy value, the time reference + inaccuracy value}, E.g., if the inaccuracy is 2us and the UE will interpret the value of the time reference to be within the range the time reference ± 2us.
  If the inaccuracy indication is not transmitted, then the inaccuracy of the time reference information is not specified.
The inaccuracy indication range from 0.25 us to 1 ms. Details to encode can be discussed in the email discussion of the CR.

## Slide 4: Proposed WF (2/2)
Proposal 3: GPS/UTC time format (like in SIB16) can be used for signalling the time reference information.
Proposal 4: Agree on both broadcast solution (via SIB16) and unicast solution (via dedicated RRC signalling) to transmit the time reference information.
Proposal 5: Introduce separate UE capability for indicating support of receiving time synchronization information in dedicated RRC.