3GPP TSG-RAN WG2 Meeting #111-e	R2-2xxx

Electronic, 17th – 28th Aug, 2020

Agenda Item:	6.2.2

Source: 	Huawei, HiSilicon

Title:	Summary of [AT111-e][027][IAB] BAP Corrections

Document for:	Discussion and Decision

# Introduction

This paper aims at capturing the summary of the following offline discussion:

[AT111-e][027][IAB] BAP Corrections (Huawei)

Scope: Treat further R2-2007484, 7966, 7316, 7483, 7967, 7317

Determine agreeable parts, Agree CRs

Deadline: Aug 26, Intermediate deadlines by Rapporteur if needed

# Discussion on correction or clarification

## 2.1: Miscellaneous corrections

R2-2007966	Miscellaneous corrections to 38.340 for IAB	Huawei, HiSilicon	CR	Rel-16	38.340	16.1.0	0006	-	F	NR_IAB-Core

R2-2007316	Corrections on IAB-DU IP address allocation in 38.340	ZTE, Sanechips	CR	Rel-16	38.340	16.1.0	0002	-	F	NR_IAB-Core

- R2 clarify the “Destination IP address” covers the “Destination IPv4 address”, “Destination IPv6 address” and “Destination IPv6 prefix” in TS 38.340, detailed wording TBD (e.g. inclusion of “destination”)

Based on the agreement we have, following changes are proposed from rapporteur to clarify the above agreement.

- a destination IP address, which is indicated by Destination IAB TNL Address IE in IP header information IE, including an IPv4 address or IPv6 address or an IPv6 address prefix,

The above changes should be sufficient to clarify the above R2 agreement and understanding, which are included in the rapporteur miscellaneous CR.

Companies can comment on the wording together with the updated miscellaneous CR.

## 2.2: flow control

R2-2007967	Corrections on flow control BAP control PDU	Huawei, HiSilicon	CR	Rel-16	38.340	16.1.0	0007	-	F	NR_IAB-Core

- 	Ericsson think the figure is correct, but are not sure about the note. LG think also this note is not needed.

-	CATT think is better to clarify this.

- The figure change is agreed, whether to have the note can continue by email.

As discussed online, companies are asked to provide views on the following question.

RAN2 109-e meeting: The BH RLC channels to be reported by the polled IAB node is up to the polled IAB node implementation. The routing IDs to be reported by the polled IAB node is up to the polled IAB node implementation.

Question 1: Do you agree to add the NOTE “The BH RLC channel(s) and routing ID(s) to be included in the flow control feedback is up to IAB node implementation, once triggered” to implement the above agreements?

| Company | Agree or not? | Comment |
| --- | --- | --- |
| QC | Yes | It’s technically not necessary but it may be helpful and it may avoid future corrections as R2 chairman pointed out. |
| ZTE | Yes | It would be better to add this description. |
| Samsung | Yes | While even without the NOTE there should be no room for misunderstanding, the content on flow control is quite terse and this explanation is useful. |
| Ericsson | No strong view | Agree with QC, i.e. technically not necessary, but it can clarify. |
| Futurewei | Yes | It does not hurt to clarify this by adding a note. |
| LG | No, but | The current BAP spec doesn’t specify which BH RLC channel(s) and routing ID(s) are included in a flow control feedback, once triggered. This means that it’s already IAB node implementation. Thus, we think that there may be no misunderstanding even without the proposed note. However, we can go with majority. |
| Nokia | We should be consistent | We also have this agreement from RAN2#108: R2 assumes that e.g. when the buffer load exceeds the certain level, the DL hop-by-hop flow control feedback should be triggered, the details of this trigger is left for implementation (in this Rel) So flow-control triggering was left for implementation. Suggestions to capture this accurately in the spec have been repeatedly denied, therefore we should: either not capture the agreements in Question either, or capture all these agreements. |
| vivo | yes | Agree with the above comments |
| CATT | Yes | We think the clarification is needed. |

Summary: Majority are fine to agree the change to add the NOTE. For the comments from Nokia, the referred agreements are for flow control feedback trigger, which is a different issue with the question (on control PDU content set).

Proposal 1a: R2 agrees to add the NOTE “The BH RLC channel(s) and routing ID(s) to be included in the flow control feedback is up to IAB node implementation, once triggered”.

Together with the minutes, we can try to agree the CRs

R2-2007967	Corrections on flow control BAP control PDU	Huawei, HiSilicon	CR	Rel-16	38.340	16.1.0	0007	-	F	NR_IAB-Core

- The figure change is agreed, whether to have the note can continue by email.

Proposal 1b: R2 agrees CR R2-2007967.

R2-2007317	Corrections on IAB flow control in 38.340	ZTE, Sanechips	CR	Rel-16	38.340	16.1.0	0003	-	F	NR_IAB-Core

- Discuss by email, merge agreeable parts with Rapporteur CR.

1st changes (5.3.2): The change seems incorrect, based on R3 F1AP specification, from Rapp perspective. Please see the Annex I for the clarification on the F1AP configuration.

2nd changes (6.2.3.1): This is cosmetic change. The change does change any functionality and format. We’d better not touch the PDU format at this stage, if the change is not essential.

Therefore, the rapporteur considers the proposed change is not essential. Companies are asked to provide views on the following question.

Question 2: Do you agree the proposed changes in R2-2007317?

| Company | Agree or not? | Comment |
| --- | --- | --- |
| QC | No, to 1st changes. No to 2nd changes | On 1st changes: Initial version is correct. On 2nd changes: initial PDU format figure is clearer. |
| ZTE | No, to 1st changes No, to 2nd changes | Thanks for the clarification. Now I think 1st change is not necessary. For the 2nd change, since we agreed the flow control PDU figure proposed in R2-2007967 to allow extension of more routing IDs/BH RLC channel IDs, it is not necessary to consider the Figure proposed in R2-2007317. |
| Samsung | Do not agree to change in 5.3.2 Indifferent to change in 6.2.3.1 | In this CR it is claimed that, for the flow control polling PDU, the egress BH RLC channel is configured by the Uplink BH Non-UP Traffic Mapping IE. However, this latter IE is for uplink traffic, whereas flow control polling PDU is sent from parent to child i.e. on the DL. |
| Ericsson | No | Agree with QC. |
| Futurewei | No, to 1st changes. No to 2nd changes | Agree with QC & SS Agree with QC & ZTE |
| LG | Not agree to both changes |  |
| Nokia | No |  |
| vivo | No to both changes | For the BAP control PDU format figure in 6.2.3.1, it could be clearer if an index can be appended to BH RLC channel ID. |
| CATT | No to both changes | Agree with QC & ZTE. |

Summary: Majority considers it as not essential for the proposed changes in R2-2007317.

## 2.3: Other clarification

R2-2007484	Default configuration usage corrections in BAP	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.340	16.1.0	0005	-	F	NR_IAB-Core

- Discuss by email, merge agreeable parts with Rapporteur CR.

1st change (move “…from the upper layer”): In the current specification, traffic from downstream node will also be suspended due to no available egress link. Please see the Annex II for the clarification on the current specification.

For a BAP Data PDU to be transmitted, BAP entity shall: - if the defaultUL-BH-RLC-channel has been received in RRC and until the BH Routing Configuration is (re)configured by F1AP: - if the BAP Data PDU corresponds to a BAP SDU received from the upper layer:- select the egress link on which the egress BH RLC channel corresponding to defaultUL-BH-RLC-channel is configured as specified in TS 38.331 [3] for non-F1-U packets;

Therefore, the rapporteur considers the proposed change is not essential. Companies are asked to provide views on the following question.

Question 3: Do you agree the proposed 1st changes (see above) in R2-2007484?

| Company | Agree or not? | Comment |
| --- | --- | --- |
| QC | No | The CR changes the logical flow of the if…else block. There doesn’t seem to be anything wrong with the original text. |
| ZTE | Yes | It looks reasonable to move the condition“if the BAP Data PDU corresponds to a BAP SDU received from the upper layer”. During IAB node inter-donor DU migration procedure, it is meaningless to check the out-of-date F1AP based configuration of source path for the backhaul traffic from collocated BAP entity. So it is not necessary to enter the subsequent condition check, such as “else if there is an entry in the BH Routing Configuration whose BAP address matches the DESTINATION field...”, or “ else if there is at least one entry in the BH Routing Configuration whose BAP address matches the DESTINATION field...” For the original text, the descendant IAB node may use the out-of-date F1AP based configuration of source path to forward the data packet until it reaches the migrating IAB node. However, the packet will be eventually discard at migrating IAB node due to source path is not available. Based on these observations, we support the proposed 1st change. |
| Samsung | No | Condition A: BAP SDU received from higher layer Condition B: a new defaultUL-BH-RLC-channel has been received since the last routing reconfiguration The only difference in behaviour between existing spec and proposed change is the case where B is true but A is false. In existing spec we move on to the ‘else’ bit in this case; with the proposed change, nothing happens (i.e. suspension). A false but B true means that a BAP SDU has not been received from upper layers (but there is a BAP PDU to be transmitted) but a new defaultUL-BH-RLC-channel has been received since the last routing reconfiguration. Not sure why we should suspend operation in this case? |
| Ericsson | No | We agree with QC and SAM comments. |
| Futurewei | No | The logic for this change is not so clear. However, we agree that the current wording is also not crystal clear, and hence may be rather confusing. If the following text change proposed in R2-2007484 is agreed, this might hopefully help clear up any potential confusion. |
| LG | No | We have no problem with the current text after making the below agreement in this e-meeting. F1-U packets is NOT allowed to use the default BAP configuration (no need to clarify further in the TS). |
| Nokia | No | Having read Annex II, thank you for that. |
| vivo | no | This paragraph describes the egress link selection behaviour when an upper layer packet is received according to whether BH Routing Configuration is configured or not. The procedure of the original version can work well without change. The proposed change to move ‘if the BAP Data PDU corresponds to a BAP SDU received from the upper layer:’ to below the first if condition seems not correct. |
| CATT | No | Agree with Rapporteur analysis in Annex II. |

Summary: Majority considers it as not essential for the 1st changes (see above) in R2-2007484.

2nd change (change “until”): This is cosmetic changes, which seems not essential.

For a BAP Data PDU to be transmitted, BAP entity shall: - if the BAP Data PDU corresponds to a BAP SDU received from the upper layer, and - if the BH Routing Configuration has not been (re)configured by F1AP after the last (re)configuration of defaultUL-BH-RLC-channel by RRC:- select the egress link on which the egress BH RLC channel corresponding to defaultUL-BH-RLC-channel is configured as specified in TS 38.331 [3] for non-F1-U packets;

Companies are asked to provide views on the following question.

Question 4: Do you agree the proposed 2nd changes (see above) in R2-2007484?

| Company | Agree or not? | Comment |
| --- | --- | --- |
| QC | Agree | The cosmetic change reads better. |
| ZTE | No strong opinion |  |
| Samsung | Agree | Perhaps not essential (as in fixing something broken), but increases clarity. However this could then continue indefinitely e.g. ‘since’ is even better than ‘after’ etc. But we agree that existing ‘if… and until…’ is an unusual construct. |
| Ericsson | No strong opinion |  |
| Futurwei | Agree | New wording is much clearer |
| LG | Agree | The proposed change seems clear. |
| Nokia | Agree | We are also OK with Samsung’s suggestion of using “since” instead of “after”. |
| vivo | Agree | This change makes it clearer for reading. |
| CATT | No strong view | We can follow the majority view. |

Summary: Majority considers it as useful proposed 2nd changes (see above) in R2-2007484

R2-2007484	Default configuration usage corrections in BAP	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.340	16.1.0	0005	-	F	NR_IAB-Core

- Discuss by email, merge agreeable parts with Rapporteur CR.

Proposal 2: Merge the 2nd change (change “until”) in R2-2007484 into the Rapporteur CR.

R2-2007483	BAP routing configuration clarification	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.340	16.1.0	0004	-	F	NR_IAB-Core

- Discuss by email, merge agreeable parts with Rapporteur CR.

The BAP entity performs routing based on: - the BH Routing Configuration derived from BAP MAPPING CONFIGURATION message configured on the IAB-node or on the IAB-donor-DU, as specified in TS 38.473 [5].

The change is editorial and cosmetic changes, which seems not essential. In addition, in the miscellaneous CR, the detailed F1AP messages have been deleted so that we don’t need capture all those different F1AP messages in BAP spec.

Companies are asked to provide views on the following question.

Question 5: Do you agree the proposed changes R2-2007483?

| Company | Agree or not? | Comment |
| --- | --- | --- |
| QC | No | It may be better to have it consistent across the BAP spec and not list all F1AP messages. |
| ZTE | No |  |
| Samsung | Yes but… | Perhaps not essential (as in fixing something broken), but increases clarity. Why say ‘an F1AP message’ when we can name it? This being said, if the rapporteur wishes to remove all the mentions of specific messages, and majority in RAN2 supports this, then this change would not be advised. |
| Ericsson | No | We tend to agree with QC comments. |
| Futurewei | No | Agree with QC |
| LG | No |  |
| Nokia | Yes |  |
| vivo | No | It is enough to refer to 38.473. |
| CATT | No | Agree with QC. |

Summary: Majority considers it as not essential for the proposed change in R2-2007483.

# Conclusion and proposals

Based on the above summary, following proposals are given.

Proposal 1a: R2 agrees to add the NOTE “The BH RLC channel(s) and routing ID(s) to be included in the flow control feedback is up to IAB node implementation, once triggered”.

Proposal 1b: R2 agrees CR R2-2007967.

Proposal 2: Merge the 2nd change (change “until”) in R2-2007484 into the Rapporteur CR.

# Reference

- R2-2007296	Packet handling after receiving default ID configuration in RRC	LG Electronics Inc.	discussion	Rel-16	NR_IAB-Core

- R2-2007316	Corrections on IAB-DU IP address allocation in 38.340	ZTE, Sanechips	CR	Rel-16	38.340	16.1.0	0002	-	F	NR_IAB-Core

- R2-2007317	Corrections on IAB flow control in 38.340	ZTE, Sanechips	CR	Rel-16	38.340	16.1.0	0003	-	F	NR_IAB-Core

- R2-2007483	BAP routing configuration clarification	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.340	16.1.0	0004	-	F	NR_IAB-Core

- R2-2007484	Default configuration usage corrections in BAP	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.340	16.1.0	0005	-	F	NR_IAB-Core

- R2-2007966	Miscellaneous corrections to 38.340 for IAB	Huawei, HiSilicon	CR	Rel-16	38.340	16.1.0	0006	-	F	NR_IAB-Core

- R2-2007967	Corrections on flow control BAP control PDU	Huawei, HiSilicon	CR	Rel-16	38.340	16.1.0	0007	-	F	NR_IAB-Core

# Annex I

This is to clarify how the BH RLC channel for BAP control PDU is configured by F1AP for DL and UL.

For UL BAP control PDU from child to parent node (e.g. Flow control feedback), it is configured by Uplink BH Non-UP Traffic Mapping IE:

Non-UP Traffic Type (set to BAP control PDU) => Egress BH RLC CH ID in BH Information

#### 9.3.1.103	Uplink BH Non-UP Traffic Mapping

This IE indicates the mapping of uplink non-UP traffic to a BH RLC channel and BAP Routing ID.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Uplink Non-UP Traffic Mapping List |  | 0..1 |  |  |
| >Uplink Non-UP Traffic Mapping List Item IEs |  | 1 .. <maxnoofNonUPTrafficMappings> |  |  |
| >>Non-UP Traffic Type | M |  | 9.3.1.104 |  |
| >>BH Information | M |  | 9.3.1.114 |  |

#### 9.3.1.104	Non-UP Traffic Type

This IE indicates the type of non-UP traffic.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Non-UP Traffic Type | M |  | ENUMERATED(UE-associated F1AP, non-UE-associated F1AP, non-F1, BAP control PDU, ...) |  |

#### 9.3.1.114	BH Information

This IE includes the backhaul information for UL or DL.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| BAP Routing ID | O |  | 9.3.1.110 | This IE is not needed for the BAP control PDU. For UL F1-U traffic, the BAP address included in this IE also indicates the IAB-donor-DU via which the DL traffic is transmitted. |
| Egress BH RLC CH List |  | 0..1 |  |  |
| >Egress BH RLC CH List Item |  | 1.. <maxnoofEgressLinks> |  |  |
| >>Next-Hop BAP Address | M |  | 9.3.1.111 | This IE identifies the next-hop node on the backhaul path to receive the packet. The value of this IE should be unique in the whole list. |
| >>Egress BH RLC CH ID | M |  | BH RLC Channel ID 9.3.1.113 | This IE identifies the BH RLC channel in the link between the gNB-DU and the node identified by the Next-Hop BAP Address IE. |

For DL BAP control PDU from parent to child node (e.g. Flow control polling), it is configured by BH RLC Channel to be Setup Item IEs/BH RLC Channel to be Modified Item IEs IE:

BAP Control PDU Channel (set to true) => BH RLC CH ID

#### 9.2.2.7	UE CONTEXT MODIFICATION REQUEST

This message is sent by the gNB-CU to provide UE Context information changes to the gNB-DU.

Direction: gNB-CU ( gNB-DU

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.3.1.1 |  | YES | reject |
| gNB-CU UE F1AP ID | M |  | 9.3.1.4 |  | YES | reject |
| gNB-DU UE F1AP ID | M |  | 9.3.1.5 |  | YES | reject |
| BH RLC Channel to be Setup List |  | 0..1 |  |  | YES | reject |
| >BH RLC Channel to be Setup Item IEs |  | 1 .. <maxnoofBHRLCChannels> |  |  | EACH | reject |
| >>BH RLC CH ID | M |  | 9.3.1.113 |  | - |  |
| >>CHOICE BH QoS information | M |  |  |  |  |  |
| >>>BH RLC CH QoS | M |  | QoS Flow Level QoS Parameters 9.3.1.45 | Shall be used for SA case. |  |  |
| >>>E-UTRAN BH RLC CH QoS | M |  | E-UTRAN QoS 9.3.1.19 | Shall be used for EN-DC case. |  |  |
| >>>Control Plane Traffic Type | M |  | 9.3.1.115 |  |  |  |
| >>RLC Mode | M |  | 9.3.1.27 |  | - |  |
| >>BAP Control PDU Channel | O |  | ENUMERATED (true, …) |  | - |  |
| >>Traffic Mapping Information | O |  | 9.3.1.95 |  | - |  |
| BH RLC Channel to be Modified List |  | 0..1 |  |  | YES | reject |
| >BH RLC Channel to be Modified Item IEs |  | 1 .. <maxnoofBHRLCChannels> |  |  | EACH | reject |
| >>BH RLC CH ID | M |  | 9.3.1.113 |  | - |  |
| >>CHOICE BH QoS information | O |  |  |  |  |  |
| >>>BH RLC CH QoS | M |  | QoS Flow Level QoS Parameters 9.3.1.45 | Shall be used for SA case. |  |  |
| >>>E-UTRAN BH RLC CH QoS | M |  | E-UTRAN QoS 9.3.1.19 | Shall be used for EN-DC case. |  |  |
| >>>Control Plane Traffic Type | M |  | 9.3.1.115 |  |  |  |
| >>RLC Mode | O |  | 9.3.1.27 |  | - |  |
| >>BAP Control PDU Channel | O |  | ENUMERATED (true, …) |  | - |  |
| >>Traffic Mapping Information | O |  | 9.3.1.95 |  | - |  |
| BH RLC Channel to be Released List |  | 0..1 |  |  | YES | reject |
| >BH RLC Channel to be Released Item IEs |  | 1 .. <maxnoofBHRLCChannels > |  |  | EACH | reject |
| >>BH RLC CH ID | M |  | 9.3.1.113 |  | - |  |

# Annex II

This is to clarify the BAP behaviors for upstream traffic from child node during IAB migration, since defaultUL-BH-RLC-channel has been received in RRC and until the BH Routing Configuration is (re)configured by F1AP.

During the IAB migration phase, if the defaultUL-BH-RLC-channel has been received in RRC and until the BH Routing Configuration is (re)configured by F1AP, the traffic from child node cannot met the green conditions, due to not “from upper layer”.

Then, BAP will check the blue and purple conditions.

- In case migrating IAB does not have dual connection, none of them can be met, because the original link will become “not available”, during the migration phase. This means the traffic from child node will be suspended at BAP layer until the new F1AP is configured.

- In case migrating IAB node has dual connection, there may be one link (e.g. SCG) still available. If the original F1AP configuration allow the traffic from child to be routed on that link, BAP will forward the data as usual. No need of suspending.

In summary, it is the correct behaviors for traffic from child node to skip the green conditions and operations.

5.2.1.3 Routing The BAP entity performs routing based on: - the BH Routing Configuration derived from an F1AP message as specified in TS 38.473 [5]. Each entry of the BH Routing Configuration contains: - a BAP Routing ID consisting of a BAP address and a BAP path identity, which is indicated by BAP Routing ID IE, and - a Next Hop BAP Address which is indicated by Next-Hop BAP Address IE. For a BAP Data PDU to be transmitted, BAP entity shall: - if the BAP Data PDU corresponds to a BAP SDU received from the upper layer, and - if the defaultUL-BH-RLC-channel has been received in RRC and until the BH Routing Configuration is (re)configured by F1AP: - select the egress link on which the egress BH RLC channel corresponding to defaultUL-BH-RLC-channel is configured as specified in TS 38.331 [3] for non-F1-U packets; - else if there is an entry in the BH Routing Configuration whose BAP address matches the DESTINATION field, whose BAP path identity is the same as the PATH field, and whose egress link corresponding to the Next Hop BAP Address is available: - select the egress link corresponding to the Next Hop BAP Address of the entry; NOTE 1: An egress link is not considered to be available if the link is in BH RLF. NOTE 2: For each combination of a BAP address and a BAP path identity, there should be at most one entry in the BH Routing Configuration. - else if there is at least one entry in the BH Routing Configuration whose BAP address matches the DESTINATION field, and whose egress link corresponding to the Next Hop BAP Address is available: - select an entry from the BH Routing Configuration whose BAP address is the same as the DESTINATION field, and whose egress link corresponding to the Next Hop BAP Address is available; - select the egress link corresponding to the Next Hop BAP Address of the entry selected above;