3GPP TSG RAN WG2 #111-e	draft R2-20xxxxx

Online, 17–28 August 2020

Source: 	Huawei, HiSilicon

Title: 	[Draft] Summary for Offline [041][TEI16] Other Corrections

Agenda Item:	6.16

Document for:	Discussion and decision

# Introduction

This document contains a list of TDocs covered in the following offline discussion:

[AT111-e][041][TEI16] Other Corrections (Huawei)

Scope: Treat R2-2007948, 7962, 7945, 8007

Determine agreeable parts in a first phase, Agree CRs in a second phase

Deadline: Aug 27 0900 UTC, Intermediate deadlines by Rapporteur if needed.

Companies are invited to share their views on each TDoc submitted.

# Discussion

## 2.1 R2-2007948 Correction on HO from NR to EN-DC

R2-2007948	Correction on HO from NR to EN-DC	Huawei, HiSilicon	CR	Rel-16	38.331	16.1.0	1948	-	F	TEI16

Q1.1: Do you agree with the intention and the corresponding change?

| Company | Intention agreeable (Yes/No) | Change agreeable (Yes/No) | Comments |
| --- | --- | --- | --- |
| Huawei | Yes | Yes | [Proponent] For HO from NR to EN-DC which was agreed in TEI16, the UE behaviour of sending RRCReconfigurationComplete message in response to the RRCReconfiguration for NR part configuration in EN-DC will go into the following entrance, but the specific condition is missing. 1> if the UE is configured with E-UTRA nr-SecondaryCellGroupConfig (UE in (NG)EN-DC): 2> if the RRCReconfiguration message was received via E-UTRA SRB1 as specified in TS 36.331 [10]; or 2> if the RRCReconfiguration message was received via SRB3 within DLInformationTransferMRDC; or 2> if the RRCReconfiguration message was received via E-UTRA RRC message RRCConnectionReconfiguration within MobilityFromNRCommand; 3> if the RRCReconfiguration is applied due to a conditional reconfiguration execution: 4> submit the RRCReconfigurationComplete message via the E-UTRA MCG embedded in E-UTRA RRC message ULInformationTransferMRDC as specified in TS 36.331 [10], clause 5.6.2a. 3> else: 4> submit the RRCReconfigurationComplete via E-UTRA embedded in E-UTRA RRC message RRCConnectionReconfigurationComplete as specified in TS 36.331 [10], clause 5.3.5.3/5.3.5.4/5.4.2.3; |
| Ericsson (Tony) | No | No | This issue was already discussed in the last meeting and the CR on the similar topic were not pursued (the change is basically the same). We believe that we should not discuss paper again and again and we are not fine to accept this change now. From RAN2#110e: Handover from EN-DC to NR R2-2005703 Correction for handover from EN-DC to NR Huawei, HiSilicon CR Rel-15 38.331 15.9.0 1691 - F NR_newRAT-Core R2-2005704 Correction for handover from EN-DC to NR Huawei, HiSilicon CR Rel-16 38.331 16.0.0 1692 - A NR_newRAT-Core 2 Treated by email [008] [008] Both Not Pursued |
| Nokia (Ping) | Yes | Yes | We agree the intention of this CR for HO from NR to EN-DC. |
| ZTE (LiuJing) | Yes | Yes | We are generally fine with the CR. Seems this CR is different from R2-2005703 (one is NR->EN-DC, the other is EN-DC to NR). Please correct me if I misunderstand anything. |
| Intel (Sudeep) | Yes | Yes | Agree that a correction is needed. |
| Samsung (Sangyeob) | Yes | Yes | We are OK with this CR. |

## 2.2 R2-2007962 RRC connection release procedure without security for EN-DC cell reselection

R2-2007962	Correction to RRC connection release procedure without security for EN-DC cell reselection	Samsung Electronics Co., Ltd	CR	Rel-16	36.331	16.1.1	4418	-	F	TEI16

Q2: Do you agree with the intention and the corresponding change?

| Company | Intention agreeable (Yes/No) | Change agreeable (Yes/No) | Comments |
| --- | --- | --- | --- |
| Huawei | Yes | Yes |  |
| Ericsson (Tony) | Yes | Yes |  |
| Nokia (Ping) | Yes | Yes |  |
| ZTE (LiuJing) | Yes | Yes |  |
| Qcom | Yes | Yes |  |
| Intel (Sudeep) | Yes | Yes | Looks like it was accidentally missed out. |
| Samsung (Sangyeob) | Yes | Yes | [Proponent] |

## 2.3 R2-2007945 FR2 inter-RAT measurement gap requirement indication

R2-2007945	FR2 inter-RAT measurement gap requirement indication 	Nokia, Nokia Shanghai Bell	CR	Rel-16	38.306	16.1.0	0397	-	F	NR_newRAT-Core

Q3: Do you agree with the intention and the corresponding change?

| Company | Intention agreeable (Yes/No) | Change agreeable (Yes/No) | Comments |
| --- | --- | --- | --- |
| Huawei | No | No | We don’t see there’s any ambiguity. The independentGapConfig capability is to indicate whether the UE supports per-FR gap whereas interRAT-NeedForGapsNR is to indicate whether gaps are needed. |
| Ericsson (Tony) | No | No | We agree with Huawei. We fail to understand where is the ambiguity here. |
| Nokia (Ping) | Yes | Yes | [Proponent] When UE operating on the E-UTRA, the FR2 inter-RAT measurement gap requirement can be indicated via two fields (i.e. interRAT-NeedForGapsNR and independentGapConfig). interRAT-NeedForGapsNR This field defines for each supported E-UTRA band or band combination whether measurement gaps are required to perform SSB based inter-RAT measurements on each supported NR band. Or independentGapConfig This field indicates whether the UE supports two independent measurement gap configurations for FR1 and FR2 specified in clause 9.1.2 of TS 38.133 [5]. The field also indicates whether the UE supports the FR2 inter-RAT measurement without gaps when (NG)EN-DC is not configured. It is not clear for network which field should be referred in order to determine the FR2 inter-RAT measurement gap requirement in below cases: Case1: independentGapConfig is NOT present (i.e. Gap is needed for all FR2 measurement) interRAT-NeedForGapsNR = false for a specific FR2 band measurement. (i.e. Gap is NOT needed for one specific FR2 band measurement) Case2: independentGapConfig = supported (i.e. Gap is NOT needed for all FR2 measurement) interRAT-NeedForGapsNR = true for a specific FR2 band measurement. (i.e. Gap is needed for one specific FR2 band measurement) We think RAN2 need to clarify UE behaviour with either of below solution: Option1: the UE shall set the same gap requirement for FR2 bands in both fields. Option2: network should refer to interRAT-NeedForGapsNR instead of independentGapConfig to determine the FR2 measurement gap requirements |
| ZTE (LiuJing) | Yes | No, Perfer Option 1 | We think the issue identified in CR is valid. Although independentGapConfig is used to indicate the per-FR gap capability, this capability can also be used to determine the gap requirement. For instance, a UE operates on EUTRAN or NR FR1 frequency does not need gap when only measuring FR2 frequencies. Regarding the proposed solutions, we prefer Option1, it does not make sense to report different “gap requirement” in the two fields. |
| Qcom | Yes | See comment | We agree with the intention as current spec language, for the independentGapConfig if supported, indicates that UE supports FR2 Inter-RAT gapless measurement while in LTE SA. This aspect overlaps with the interRAT-NeedForGapsNR capability. This addition to the description of the independentGapConfig capability was based on an observation provided by RAN4 in LS (R4-1811405). Having said, the motive behind the LS was to find a way out for UEs that are capable of gapless measurement on FR2 while no gapless capability was defined for Rel.15 that allows such behavior. Now in Rel.16 and since a capability has been defined (interRAT-NeedForGapsNR) that allow gapless measurement (on any band and not only FR2) is there a need to keep the observation provided by RAN4 LS??? If we decided to keep the independentGapConfig capability description as is, then we will be supporting the CR. |
| Intel (Candy) | Yes | No | We think that the intention and the issue are valid. However, not sure why UE will report differently. We think that they should be the same. We can go with option 1. |
| Samsung (Sangyeob) | Partly | No | We tend to see the point from Nokia and we think that NW will follow interRAT-NeedForGapNR if both fields are signalled from UE but different gap requirement. But we don't see any value to clarify what the CR suggest i.e. it is strange to specify the NW behaviour as in the CR. We prefer to leave up to NW implementation. |

## 2.4 R2-2008007 UE behavior with E-UTRA cell selection upon mobility from NR failure for enhanced EPS voice fallback

R2-2008007	CR on UE behavior with E-UTRA cell selection upon mobility from NR failure for enhanced EPS voice fallback	Samsung Electronics Co., Ltd	CR	Rel-16	38.331	16.1.0	1969	-	F	TEI16

Q4: Do you agree with the intention and the corresponding change?

| Company | Intention agreeable (Yes/No) | Change agreeable (Yes/No) | Comments |
| --- | --- | --- | --- |
| Huawei | Yes | Yes, but | To align with the description in 5.4.3.5 Mobility from NR failure, the suggested wording could be “ or when selecting an E-UTRA cell in case of Mobility from NR failure if voiceFallbackIndication is included in the MobilityFromNRCommand message as specified in 5.4.3.5:" |
| Ericsson | Yes | Yes |  |
| Nokia | Yes | Yes |  |
| ZTE | Yes | Yes |  |
| Qcom | Yes | Yes |  |
| Intel (Sudeep) | Yes | Yes |  |
| Samsung (Sangyeob) | Yes | Yes | [Proponent] We think the original text in the CR is sufficient/clean but we are OK with the suggestion from Huawei if majority think it is more clearer. |

# Conclusion

To be added.