3GPP TSG-RAN WG2 Meeting #111 electronic	                                                                       R2-200xxxx

Online, August 17th - 28th, 2020

Agenda item:	6.10.1

Source:	CMCC

Title:	Summary of MDT stage-2 issues

Document for:	Discussion, Decision

# Introduction

This contribution collects company views on following issues:

R2-2007386	How to Determine Whether a Cell is Part of the Area Indicated by AreaConfiguration	Samsung	discussion	NR_SON_MDT-Core[17]

=>	Not pursued

=>	Can be discussed in the email discussion on stage2 correction.

# Discussion

It is pointed in [1] that how to determine whether a cell is part of the area indicated by areaConfig is unclear, because SIB1 includes multiple PLMN-IdentityInfo, each of which includes multiple PLMN-Identity. The IE AreaConfig is choice of three lists; cellGlobalIdList, trackingAreaCodeList and trackingAreaIdentityList.

|  | AreaConfig | SIB1 |
| --- | --- | --- |
| CellGlobalIdList | N * [PLMN identity + cell identity] | Y * PLMN-IdentityInfo PLMN-IdentityInfo = [X * PLMN identity + TAC + Cell id] |
| TrackingAreaCodeList | N * TrackingAreaCode |  |
| TrackingAreaIdentityList | N * [PLMN identity + TrackingAreaCode] |  |

Samsung thinks that a simple option is to consider only first PLMN-Identity in first PLMN-IdentityInfo of the PLMN-IdentityInfoList, and cellIdentity corresponding to the first PLMN-IdentityInfo. For instance,

If CellGlobalIdList is used, UE has to check if a pair of PLMN-identity and CellIdentity in the CellGlobalIdList are identical to a specific (or any) pair of PLMN-identity and CellIdentity in SIB1. The straightforward choice would be the first PLMN-IdentityInfo of the PLMN-IdentityInfoList.

If TrackingAreaCodeList is used, UE has to check if a TAC in the List is identical to a TAC in a specific (or any) PLMN-IdentityInfo. Again the straightforward choice would be the first PLMN-IdentityInfo.

If TrackingAreaIdentityList is used, UE has to check if a pair of PLMN-identity and TAC in the TrackingAreaIdentityList is identical to a specific (or any) pair of PLMN-identity and TAC in SIB1. The straightforward choice would be the first PLMN-IdentityInfo of the PLMN-IdentityInfoList.

Companies are invited to provide views on the proposal that considering only first PLMN-Identity in first PLMN-IdentityInfo of the PLMN-IdentityInfoList, and cellIdentity corresponding to the first PLMN-IdentityInfo when determining whether a cell is part of the area indicated by areaConfig:

| Company | Agree or not | Additional comments if any |
| --- | --- | --- |

# TP for TS 37.320

/*start of changes*/

##### 5.1.1.1.2	Configuration effectiveness

The logged measurement configuration is provided in a cell by dedicated control while UE is in CONNECTED and implies:

-	logged measurement configuration for downlink pilot strength measurements (or events) logging is active

-	in IDLE UE state in E-UTRAN, or

-	in IDLE mode, CELL_PCH and URA_PCH states in UTRAN, or

-	in CELL_FACH state when second DRX cycle is used in UTRAN, or

-	in IDLE and INACTIVE states in NR

-	until logging duration timer expires or stops

-	logged measurement configuration for MBSFN measurement logging is active

-	in IDLE and CONNECTED UE states in E-UTRAN

-	until logging duration timer expires or stops

-	logged measurement configuration and logs are maintained when the UE is in any state as described above, despite multiple periods interrupted by UE state transitions, e.g. for downlink pilot strength measurements when the UE is in CONNECTED state for E-UTRAN and NR and CELL_DCH, CELL_FACH state when second DRX cycle is not used in UTRAN

-	logged measurement configuration and logs are maintained when the UE is in any state as described above in that RAT, despite multiple periods interrupted by UE presence in another RAT

There is only one RAT-specific logged measurement configuration for Logged MDT in the UE. When the network provides a configuration, any previously configured logged measurement configuration will be entirely replaced by the new one. Moreover, logged measurements corresponding to the previous configuration will be cleared at the same time. It is left up to the network to retrieve any relevant data before providing a new configuration.

NOTE:	The network may have to do inter-RAT coordination.

When a logging area is configured, logged MDT measurements are performed as long as the UE is within this logging area. For NR, when determining whether a cell is part of the logging area, only the first PLMN-Identity of the plmn-IdentityList in the first PLMN-IdentityInfo of the PLMN-IdentityInfoList (in SIB1), and cellIdentity corresponding to the first PLMN-IdentityInfo are considered. If no logging area is configured, logged MDT measurements are performed as long as the RPLMN is part of the MDT PLMN list. When the UE is not in the logging area or RPLMN is not part of the MDT PLMN list, the logging is suspended, i.e. the logged measurement configuration and the log are kept but measurement results are not logged. In addition, for MBSFN logged measurements, logged MDT measurements are performed in logging intervals when the UE receives MBMS service from a MBSFN area according to the target MBSFN area(s) configuration When the UE is not in the logging area or does not receive MBMS service from a MBSFN area that matches the target MBSFN area(s) configuration in the logging interval the logged measurement configuration and the log are kept but measurement results are not logged.

NOTE:	The logging duration timer continues.

In case the new PLMN that does not belong to the MDT PLMN list provides a logged measurement configuration any previously configured logged measurement configuration and corresponding log are cleared and overwritten without being retrieved.

/*end of changes*/

Companies are invited to provide views on above TP for TS37.320:

| Company | Agree or not | Additional comments if any |
| --- | --- | --- |

# Conclusions

# References

- R2-2007386	How to Determine Whether a Cell is Part of the Area Indicated by AreaConfiguration, Samsung