## Slide 1: RAN2 status on NR study – Rapporteur input to SA2/RAN3 joint session
NTT DOCOMO, INC. (Rapporteur)
R2-164501
TSG RAN WG2 meeting #94
23-27 May 2016, Nanjing, China

## Slide 2: RAN2 input to the joint session
CN-RAN connection
  The latest status on potential deployment scenarios is reported.
CN-RAN functional split (*)
NW slicing (*)
(*) Not reported since these topics were not discussed sufficiently to provide RAN2 views.

## Slide 3: Deployment scenarios for LTE-NR
The following scenarios were agreed to be studied.
  NR tightly integrated in LTE via EPC.
  LTE tightly integrated in NR via NextGen Core.
  NR tightly integrated in LTE via NextGen Core.
For all scenarios U-plane data is split at CN or RAN.

## Slide 4: Deployment scenarios for standalone NR
The following scenarios were agreed to be studied.
For single RAT operation:
  NR node B is connected to NG Core.
  LTE eNB is connected to NG Core (or EPC as today).

## Slide 5: Deployment scenarios for standalone NR and LTE Mobility
The following scenarios were agreed to be studied.
  LTE eNB is connected to EPC and NR Node B is connected to NextGen Core.
  Both LTE eNB and NR Node B are connected to NextGen Core.
Dash line: direct IF between LTE eNB and NR Node may or may not be present.

## Slide 6: Deployment scenarios for NR-WLAN interworking
The following scenarios was agreed to be studied.
  WLAN integration with NR

## Slide 7: Discussion point in the joint session (1/2)
Connection to EPC is considered as a potential scenario on LTE-NR tight interworking for aggregation below.
  NR tightly integrated in LTE via EPC.
Proposed to discuss and confirm if the scenarios involved with EPC is supported.

## Slide 8: Discussion point in the joint session (2/2)
A deployment scenario where WLAN connected directly to NextGen Core was discussed in RAN2.
Proposed to discuss if there are any impacts on NR radio protocol design.