## Slide 1: Note for offline discussion on clarification to PRS-info for FeMTC

## Slide 2: Comparison
Alt1 understanding:
  TPRS from the configuration index , the product of PRS occasion interval (10,20,40,80) and the PRS occasion group length (2,4,8,16,32,64,128) equals a value in the set of legacy PRS periods (160,320,640,1280).
    only the first four values in the 36.211 Table 6.10.4.3-1 can be used for FeMTC, as PRS periods.
Alt2 understanding:
  the product of the TPRS from the configuration index (5,10,20,40,80,160,320,640,1280) and the PRS occasion group length (2,4,8,16,32,64,128) equals a value in the set of legacy PRS periods (160,320,640,1280).
    all the values in the 36.211 Table 6.10.4.3-1 can be used for FeMTC
    here TPRS is used as PRS occasion interval, but its value range is largrer than the value range (10,20,40,80) agreed by RAN1, which will also change the RAN1 agreements on frequency hopping.

## Slide 3: Proposal
We send LS to RAN1
  to confirm with RAN1 which is the right understanding:
    Alt1: only the first four values in the 36.211 Table 6.10.4.3-1 can be used for FeMTC, as PRS periods.
    Alt2: all the values in the 36.211 Table 6.10.4.3-1 can be used for FeMTC
  to confirm with RAN1:
    If the maximum hopping distance (interval ) can be larger than 80

## Slide 4: Annex

## Slide 5
Alt1
RAN2 understanding on RAN1 agreements
Alt2

## Slide 6: Text proposal for Alt1*
prsOccGroupLen This field specifies the PRS occasion group length, defined as length of the number of consecutive PRS occasions comprising a PRS occasion group. Enumerated values define 2, 4, 8, 16, 32, 64 or 128 consecutive PRS occasions. and the product of the PRS periodicity T_PRS from the prs-ConfigurationIndex and the PRS occasion group length cannot exceed 1280. If omitted, the PRS occasion group length is 1. The product of prsOccGroupLen × PRS occasion interval, that is, the PRS periodicity TPRS from the prs-ConfigurationIndex, should be within the value set of {160, 320, 640,1280} subframes. The values that can be used for PRS occasion interval are 10, 20, 40 or 80 subframes. If this field is absent, the number of PRS occasions comprising a PRS occasion group is 1.
  * Blue for deletion and red for new adding

## Slide 7: Text proposal for Alt2*
prsOccGroupLen This field specifies the PRS occasion group length, defined as length of the number of consecutive PRS occasions comprising a PRS occasion group. Enumerated values define 2, 4, 8, 16, 32, 64 or 128 consecutive PRS occasions. and the product of the PRS periodicity T_PRS from the prs-ConfigurationIndex and the PRS occasion group length cannot exceed 1280. If omitted, the PRS occasion group length is 1. When the target device reveives a prsOccGroupLen together with a PRS periodicity TPRS for the same cell where the product prsOccGroupLen × TPRS exceeds 1280 ms or is below 160 ms, the target device may assume no PRS is transmitted by that cell. If this field is absent, the number of PRS occasions comprising a PRS occasion group is 1.
  * Blue for deletion and red for new adding

## Slide 8
If we go for Alt2：
  We may need further clarification on some cases, e.g. if prsOccGroupLen is set to128(it’s allowed for FeMTC), how to set TPRS to guarantee that prsOccGroupLen × TPRS doesn’t exceed 1280 ms?
  Since there always only one occasion exists in a PRS period, the further clarification may be needed for PRS frequency hopping for FeMTC