## Slide 1: Agreements on SR design for NR and outstanding issues
CB#311
2017-10-12
Prague

## Slide 2: Agreements (1/3)
An SR configuration consists of a collection of sets of PUCCH resources across different BWPs and cells with the following constraints:
  Per cell, at any given time there is at most one usable PUCCH resource per LCH
  This corresponds to the case of one single LTE-like set of SR PUCCH resources being configured per LCH per BWP, and only one BWP being active at a time

## Slide 3: Agreements (2/3)
Each LCH is mapped to none or one SR configuration.
Each SR configuration has its own SR counter and prohibit timer.
  This counter and timer control the SR configuration i.e. SR procedures on the group of LCHs mapped to the SR configuration in question.
  SR counters and timers are independent across different configurations.
  When max SR transmission counter is reached on a SR configuration, SR failure is declared and the UE triggers a RACH and releases all PUCCH resources.
BWP switching and cell activation / deactivation do not interfere with the operation of the counter and timer.

## Slide 4: Agreements (3/3)
The selection of which valid PUCCH resource for SR to signal SR on when the MAC entity has more than one valid PUCCH resource for SR in one ‘TTI’ is left to UE implementation.
  This covers the CA case (as in LTE) but also covers the case where availability of multiple PUCCH resource for SR in one ‘TTI’ is due to SR configurations (e.g. originating from different LCHs) overlapping in time.

## Slide 5: Outstanding issues
Maximum number of SR configurations per UL BWP
  Requested by RAN1
  No agreement on the maximum number in RAN2 at present, or even if such a number is necessary to be specified/worked out
Send an LS to RAN1, cc RAN4?