## Slide 1: Bearer type issues on VoLTE supported in Option4
China Telecom
TSG RAN WG2 -NR#2 27-29 Jun 2017, Qingdao, China
Agenda Item: 10.2.2.1
Document for: Discussion
R2-1707109

## Slide 2: Introduction
In RAN2#97bis it is agreed that the following combinations of bearer types cannot be configured simultaneously in LTE-NR DC simultaneously for user plane DRBs:
  MCG split bearer and SCG split bearer
  MCG split bearer and SCG bearer (same as LTE DC)
For LTE-NR DC Option4 where the MN is NR gNB and the SN is LTE eNB, usually eMBB service is provided by MCG bearer or MCG split bearer.
In some cases, the UE may perform the ordinary eMBB service and voice (VoIP) service at the same time. In this case, voice will prefer to be provided by LTE eNB for better coverage(e.g. lower frequency), eMBB will prefer to be provided by NR gNB.
For this case how to support the ordinary eMBB on NR and voice on LTE simultaneously?

## Slide 3: Consideration
Considering the limitted combinations, some possible combinations for ordinary eMBB and VoLTE perform simultaneously for Option4 maybe:
  MCG split bearer for eMBB and MCG split bearer for VoLTE
  MCG bearer for eMBB and MCG split bearer for VoLTE
It seems that VoLTE have no choice but carried by MCG split bearer(100% traffic splited to SN). But it is known that RoHC is not configured for Split bearer in LTE-DC, is it possible to make some enhancements of Split bearer to support the VoLTE functions (e.g. RoHC and Semi-Persistent Scheduling, etc.) in LTE-NR DC?
If VoLTE can not be carried by MCG split bearer, is there any other solution，such as the MN does not perform bearer split but just transfer voice traffic to SN?

## Slide 4: Proposal
When making decisions on the bearer types combinations and mergers, different services requirements in various scenarios should be considered，such as ordinary eMBB service and VoLTE service performed simultaneously in LTE-NR DC Option4.