## Slide 1: Proposals on IAB Use Cases and Deployment Scenarios
AT&T, Ericsson, Intel, KDDI, Nokia, Nokia Shanghai Bell, Qualcomm, Samsung
3GPP TSG-RAN WG2 NR Ad hoc 1801 R2-1801621 Vancouver, Canada, 22nd January – 26th January 2018
Agenda Item: 11.1

## Slide 2: Relay deployment scenarios
Motivation:
A key benefit of IAB is enabling flexible and very dense deployment of NR cells without the need for densifying the transport network proportionately.
A diverse range of deployment scenarios can be envisioned including support for outdoor small cell deployments, indoors, or even mobile relays (e.g. on buses or trains).
However, given the need to ensure the completion of a baseline design, it is proposed that the study focuses on physically fixed IAB node deployments.
Note this does not preclude operation of mobile relays, just that optimizations for mobile relays are not considered.
Proposal 1:
The Rel.15 study item focuses on IAB with physically fixed relays
  Optimization for mobile relays in future releases is not precluded

## Slide 3: In-band and out-of-band backhaul
Motivation:
In-band (access and backhaul links at least partially overlap in frequency) and out-of-band relays (access and backhaul links can operate independently) are important use cases for IAB
It is critical to study in-band operation which requires tighter interworking with the access links to accommodate half-duplex constraints (e.g. when the IAB node cannot transmit and receive simultaneously on the carrier) and avoid/mitigate interference
Proposal 2:
Common architecture supports both in-band and out-of-band IAB scenarios.
In-band IAB scenarios including (TDM/FDM/SDM) of access and backhaul links subject to half-duplex constraint at the IAB node are supported
Out-of-band IAB scenarios are also supported using the same set of RAN features designed for in-band scenarios.
  Study whether additional RAN features are needed for out-of-band scenarios

## Slide 4: Access/backhaul RAT options
Motivation:
IAB can potentially support operation in both mmWave and sub-6GHz spectrum
In addition to backhauling NR access links, backhauling of LTE access links may potentially be supported, although architecture solutions to support this use case need to be studied
It is also critical to ensure that legacy UEs (e.g. Rel. 15 and earlier) are able to be served by nodes which are backhauled using IAB
Proposal 3:
NR access over NR backhaul is studied with highest priority
Identify the additional architecture solutions required for LTE access over NR backhaul
The IAB design shall at least support the following UEs to connect to a node which is backhauled using IAB:
  Rel. 15 NR UE
  Legacy LTE UE if IAB supports backhauling of LTE access

## Slide 5: IAB and SA/NSA deployments
Motivation:
IAB relaying should be possible in both stand-alone (SA) and non-stand-alone (NSA) deployments.
  Supporting EN-DC on access links is beneficial for early IAB deployments as well as for later deployments supporting EN-DC only UEs.
  Supporting EN-DC on backhaul links is beneficial for networks that do not support stand-alone NR.
IAB operation under NSA should be studied since it requires LTE radio and connection for control plane signaling, along with NSA specific capabilities and requirements
Proposal 4:
SA and NSA on the access link will be supported
Both NSA and SA for the backhaul links will be studied

## Slide 6: Supporting Contributions
R2-1800389 | Nokia, Nokia Shanghai Bell | General views on the scope of the IAB study
R2-1800390 | Nokia, Nokia Shanghai Bell | IAB deployment scenarios
R2-1800391 | Nokia, Nokia Shanghai Bell | Relaying in NSA network
R2-1800411 | Qualcomm Inc | IAB deployment considerations
R2-1800568 | KDDI Corporation | High level overview on IAB
R2-1800570 | KDDI Corporation | Use cases for IAB
R2-1800571 | KDDI Corporation | NSA relay architecture
R2-1800953 | Intel Corporation | Scenario and architecture for IAB
R2-1801021 | Ericsson | Deployment scenarios and use cases for Integrated Access Backhaul
R2-1801023 | Ericsson | Support for EN-DC for IAB
R2-1801024 | Ericsson | Duplexing in IAB
R2-1801130 | Huawei Technologies France | Consideration on IAB Scenarios and Use Cases
R2-1801214 | AT&T | Use cases and deployment scenarios for IAB