## Slide 1: Response to R3-185000, R3-185001, R3-185002, R3-184948, R3-184673, R3-184674, R3-184675, R3-184676, R3-184677, R3-184605, R3-184751, R3-184752, R3-185059, R3-184998, R3-184999, R3-184678 and R3-184679 (Summary of contributions on TNL Address Discovery for Option 3)
NTT DOCOMO, INC.
R3-185099
3GPP TSG-RAN WG3 RAN3#101
Gothenburg, Sweden, 20th-24th August 2018 Agenda 31.3.3

## Slide 2: Introduction
Following WA was made in last meeting.
WA Specification needs to enable routing of TNL address requests at MME for TNL address discovery of Opt 3 in Rel-15
WA We use a protocol fn of S1 equivalent to current functionality (e.g. S1 TNL config transfer procedure to start TNL address discovery)
WA Routing function of TNL address requests resides in the MME; further details are FFS.
Based on above, several contributions are submitted in this meeting.
This paper summarizes them by updating [1].

## Slide 3: Summary of current status
Several options are proposed based on previous WA.
  eNB proxy (eNB serve as proxy towards the MME)
    Proposed in [2-10]
  Virtual eNB (en-gNB connects to MME as eNB)
    Proposed in [14]
On the other side, the previous WA is attacked by [11] and proposes following Option as alternative.
  X2 proxy (some eNB serves proxy towards gNB)
    Proposed in [11-13]
Next slide compares Option 1 and Option 2 and clarifies what is attacked point of previous WA.
MME
Forwarding
table
gNB
eNB
Registration:
TNL address discovery(*):
(*:assuming gNB will reply to the request)
Note that these arrows only indicates possible required signalling (i.e. not indicating standardization impact.)
gNB
MME
Forwarding
table
eNB
Pretend as eNB over S1
gNB
X2 proxy
Forwarding
table
eNB
Note that after X2 signalling is established, eNB and gNB will communicate directly.

## Slide 4: Comparison of options and attacked point of WA
 |  | 1. eNB Proxy | 2. Virtual eNB | Attacked point
Registration | gNB Configuration | Initial eNB IP@ | Initial MME IP@ | 
 | Additional interface | No addition | One more (S1 between MME and en-gNB; en-gNB needs support S1) | 
 | Impact on current message | S1:Modify “S1 setup req. /eNB config. update” | No impact | S1 impact is inevitable. (Note 2)
 | New node | No | No | 
 | Forwarding table format | en-gNB id, S1 TEID of Proxy eNB (Note2) (Proxy eNB may be Multiple) | Virtual eNB id, S1 TEID of virtual eNB (Similar as current) | Redundancy may exist in the table (Note 2)
Address discovery | Additional interface | No addition | One more (S1 between MME and en-gNB) | 
 | Impact on current message | S1:Modify “eNB/MME config. transfer” X2:Add a message to transfer the request and response(Note1) | No impact | Both S1 and X2 impact are inevitable. (Note 2)
 | Updating impact of eNB | All eNB EN-DC supports | No impact | Many eNBs need to be updated.
Others | Points to be considered | -Solution when one MME doesn’t cover some en-gNBs. | -Limit freedom of id allocation -May need pre-configuration of mapping | -Need to exchange several IP@ based on SA3 requirement (SCTP/IP-sec/ GTP) -May have more delay/messages if Note1 is assumed (Note 1-3)
Note1: Assumption is that en-gNB responses to the request from eNB.
Note2: Applicable only for 1. eNB proxy
Note3: Raised in offline discussion.

## Slide 5: Other discussion points
A. Whether en-gNB needs to support TNL address discovery function to find new eNB?[6]
  Not needed; It would be common understanding.
B. Who should reply to the request from eNB?
  Option 1 [2, 6]: Nodes except for en-gNB(e.g. MME, proxy eNB or X2 proxy)
    Less signalling; quick reply
    Needs to reserve one or more IP endpoints
      And, needs to inform new one if it is used.
    May need further implementation effort as it is different from current eNB TNL address discovery.
  Option 2 [11] : en-gNB
    Vice versa of Option 1
C. How to solve routing on inter-MME/X2 proxy case?
  Option 1:By en-gNB ID [13?]
    Operators may need to configure which en-gNB ID belongs which MME/X2 proxy.
  Option 2:By 4G TAC
    Operators may need to configure which 4G TAC belongs which MME/X2 proxy.
      For MME, it would be same as current.
    Option 2-1: broadcasted by E-UTRA cell overplayed to the NR cell[15-16]
      Need RAN2 involvement (e.g. how to specify PCI/ frequency of the LTE cell )
    Option 2-2:Broadcast NR cell for EN-DC[14]
      Need RAN2 involvement (i.e. include 4G TAC in SIB1)
  Option 3: just ask Other WGs [17-18]

## Slide 6: Way forward
RAN3 to narrow down/clarify the solution considering analysis provided in this paper.

## Slide 7: Reference
[1] R3-183906, “Wayforward on TNL Address Discovery for Option 3” , NTT DOCOMO,INC.
[2] R3-185000, “Introducing X2 TNL Address discovery for en-gNBs for EN-DC”, Ericsson
[3] R3-185001, “Introducing X2 TNL Address discovery for en-gNBs for EN-DC”, Ericsson
[4] R3-185002, “Introducing X2 TNL Address discovery for en-gNBs for EN-DC”, Ericsson
[5] R3-184948, “Introducing X2 TNL Address discovery for en-gNBs for EN-DC”, Ericsson, Vodafone
[6] R3-184673, “More consideration for EN-DC TNL address discovery”, ZTE
[7] R3-184674, (TP for NR BL CR for TS36.300) EN-DC TNL address discovery solution 3, ZTE
[8] R3-184675, (TP for NR BL CR for TS36.413) EN-DC TNL address discovery solution 3, ZTE
[9] R3-184676, (TP for NR BL CR for TS36.423) EN-DC TNL address discovery solution 3, ZTE
[10] R3-184677, (TP for NR BL CR for TS38.300) EN-DC TNL address discovery solution 3, ZTE
[11] R3-184605, “En-gNB X2 TNL address discovery ” , Huawei, Nokia, Nokia Shanghai Bell
[12] R3-184751, “Support for TNL address information discovery for EN-DC”, Nokia, Nokia Shanghai Bell
[13] R3-184752, “Support for TNL address information discovery for EN-DC” , Nokia, Nokia Shanghai Bell
[14] R3-185059, “Further discussion on TNL address discovery for EN-DC”, Qualcomm Incorporated
[15] R3-184998, “Option 3 ANR - X2 connectivity across MME pools for EN-DC”, Ericsson
[16] R3-184999, “[DRAFT] LS on X2 TNL Address discovery for EN-DC across MME borders”, Ericsson
[17] R3-184678, “Inter MME EN-DC TNL Address discovery”, ZTE
[18] R3-184679, “Draft LS on Transfer of inter-MME SON Configuration Information for EN-DC”, ZTE

## Slide 8: Annex mechanism of virtual eNB
gNB
MME
Forwarding table
eNB
gNB id (22~32bits):A
eNB id | S1 TEID
a | X
… | …
virtual eNB id (20bits*): a
*:Other length are also possible.
1. S1 setup request (eNB id:A, S1 TEID X)
UE
2. CGI reporting (NCGI:A+B,….)
Local cell id (14~4bits):B
3. eNB extracts virtual eNB id
from NCGI by configuration
4. eNB configuration transfer (eNB id :a)
MME configuration transfer (X2 TEID Y)

## Slide 9: Annex Comparison of all options
 |  | 1. eNB Proxy | 2. Virtual eNB | 3. X2 proxy
Registration | gNB Configuration | Initial eNB IP@ | Initial MME IP@ | X2 proxy IP@
 | Additional interface | No addition | One more (S1 between MME and en-gNB; en-gNB needs support S1) | One more(Note 1) (X2 between X2 proxy and en-gNB)
 | Impact on current message | S1:Modify “S1 setup req. /eNB config. update” | No impact | No impact
 | New node | No | No | Not necessarily (eNB can be updated to support.)
 | Forwarding table format | en-gNB id, S1 TEID of Proxy eNB (Note2) (Proxy eNB may be Multiple) | Virtual eNB id, S1 TEID of virtual eNB (Similar as current) | en-gNB id and X2 TEID of en-gNB
Address discovery | Additional interface | No addition | One more (S1 between MME and en-gNB) | One more(Note 1) (X2 between X2 proxy and eNB)
 | Impact on current message | S1:Modify “eNB/MME config. transfer” X2:Add a message to transfer the request and response(Note2) | No impact | X2:Modify “X2 Message Transfer”(Note2)
 | Updating impact of eNB | All eNB EN-DC supports | No impact | Only eNBs supporting X2 proxy(Note 3)
Others | Points to be considered | -Solution when one MME doesn’t cover some en-gNBs. | -Limit freedom of id allocation -May need pre-configuration of mapping | -Solution when one X2 doesn’t cover some en-gNBs. -Temporal unavailability of X2 proxy (e.g. by reset)
Note1: EN-DC X2 removal may be used if the X2 is not necessary for a while.
Note2: Assumption is that en-gNB responses the request from eNB.
Note3: Anyway, to support EN-DC, other eNBs also needs to be updated.