## Slide 1: Data forwarding on Inter-system HO
NTT DOCOMO, INC.
R3-187047
3GPP TSG-RAN WG3 RAN3#102
Spokane, Washington, USA, 12th Nov 2018 - 16th Nov 2018

## Slide 2: Background
Data forwarding on Inter-system HO is discussed for a long time.
However, there still be three solutions as described in [1].
  Solution 1 in [2], Solution 2 in [3] and [4], Solution 3 in [5]
This paper provides illustrates those solutions and way forward from operator perspective.

## Slide 3: Case 1: Intra-system handover
Forwarding Tunnel
- per DRB for PDCP SDU
- Per PDU session for packets not mapped to DRB level forwarding tunnels
End Marker
- Per tunnel
UPF
Target
RAN
1
Source
RAN
2
Tunnel
- Per PDU session
End Marker
- Per tunnel
Following was already agreed.
  Note that ,on not only Xn HO but also NG HO, same would be applied.

## Slide 4: Case 2: Inter-system handover (5G => 4G)(1/2)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 1
3 proposed solutions captured (red text shows difference)
  As lossless HO is not supported (mentioned in TS38.300), PDCP SDUs in source RAN may not be transferred.
    But, may be achieved by forwarding them as fresh packet.
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per QoS flow (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
- Per PDU session (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- One Per QoS flows mapped to one E-RAB (for 2)
- Per tunnel (for 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 2
Removing QFI, map to E-RAB tunnels
Removing QFI, map to E-RAB tunnels

## Slide 5: Case 2: Inter-system handover (5G => 4G)(2/2)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per tunnel (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2)
- Per E-RAB (for 3 & 4)
End Marker
- Per tunnel (for 2)
- Per tunnel (for 3 & 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3 & 4)
End Marker
- Per tunnel (for 2 & 3 & 4)
UPF
Target
RAN
1
2
GW
Source
RAN
3
4
Tunnel
- Per PDU session
End Marker
- Per tunnel
Solution 3
Removing PDU Session UP header(*)
*: This function is already implemented as it is required for sending normal packets.
(i.e. SDAP layer would just check the header within the GTP-U header, remove it and add SDAP header (in case it is necessary .))

## Slide 6: Case 3: Inter-system handover (4G => 5G)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3 ) - One Per QoS flows mapped to one E-RAB (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
Forwarding Tunnel
- Per E-RAB (for 2 & 3)
- Per PDU session (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per QoS flow (for 4)
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
Solution 2
Solution 1
3 proposed solutions captured (red text shows difference)
Apply packet filter to add per Flow QFI, map into PDU Session tunnel
Add to all packets from E-RAB QFI of one QoS flow mapped to E-RAB , map into PDU Session

## Slide 7: Case 3: Inter-system handover (4G => 5G)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3)
- Per E-RAB (for 4)
End Marker
- Per tunnel (for 2 & 3)
- Per tunnel (for 4)
Forwarding Tunnel
(direct also possible)
- Per E-RAB (for 2 & 3 & 4)
End Marker
- Per tunnel (for 2 & 3 & 4)
GW
Target
RAN
1
2
UPF
Source
RAN
3
4
Tunnel
- Per E-RAB
End Marker
- Per tunnel
Solution 3
Nothing specific
(SDAP header is not added (*))
*: It is same handling when one DRB includes only one QoS flow.
(In this case, QoS flow within the E-RAN can not needed to be differentiated anyway.)
Furthermore, forwarding data directly to PDCP layer is same handling with the intra-system HO (per DRB data forwarding).

## Slide 8: Summary of solutions
There would be some difference on impact for nodes (i.e. UPF and/or NG-RAN.)
However, only Solution 3 enables direct data forwarding (if there is direct path between source RAN node and target RAN node.)
To minimize the interruption time, it would be better to enable direct data forwarding as direct data forwarding would have less interruption time.
  Inter- system HO would occur during the transient period (e.g. (1) only some area is supported by 5GC in initial deployment , (2)some service is only supported by EPC (in transient period.))
Furthermore, in-direct data forwarding is inefficient if one physical RAN node connects to both EPC and 5GC or such nodes are co-located and provide possibility of direct data forwarding.
  On direct data forwarding, data would be forwarded within the node/directly between co-located nodes.
Next slide illustrates further on the interruption time.

## Slide 9: Interruption time on inter-system HO
To minimize interruption time, some data needs to be arrived before 10.
However, the time period from 8 to 10 would be very short as it is just between RAN node and UE. (i.e. No need to involve CN.)
On the other hand, indirect data forwarding may take more time in some deployment as it requires (both) CN involvement.
Thus, direct forwarding would be required to minimize interruption time.
UE
RAN node
In CN1
9. RACH procedure
CP for CN2
(MME or AMF)
RAN node for CN2
UP for CN2
(SGW or UPF)
CP for CN1
(MME or AMF)
UP for CN1
(SGW or UPF)
1.Measurement report
2.HO Required
3. Relocation req.
4.HO req.
5.HO req. ACK
6.Relocation resp.
7.HO Command
8.HO Command
(RRC Reconf.)
10.HO Complete
(RRC Reconf. Comp.)
DL Data
Indirect data forwarding
Direct data forwarding
Minimum
interruption
time

## Slide 10: Proposed Way forward
RAN3 to apply Solution 3 described in [5]

## Slide 11: Reference
[1] RAN3_101bis_agenda_with_Tdocs_20181012_EOM.doc
[2 ]R3-186128,,
[3] R3-186127, “(TP for NR BL CR for TS 38.300): Handling of Inter-system end markers (Solution 2)” , Nokia, Nokia Shanghai Bell
[4] R3-186256, “(TP for NR BL CR for TS 38.300): Handling of Inter-system end markers ”, Nokia, Nokia Shanghai Bell
[5] R3-186129, “TP for BL CR for 38.300 for inter-system HO” , Ericsson, Nokia