3GPP TSG-RAN WG3 #109-e							R3-205511

17-28 August 2020

Online

Agenda Item:	10.2.1.4

Source:	ZTE (moderator)

Title:	Summary of Offline for MR-DC UHI

Document for:	Approval

# Introduction

CB: # 1004_SONMDT_UEHist

-  Topics to discuss:

- UE history information of secondary node (e.g. PSCell, other information?)

- Xn, and X2 impacts

- Which node (MN or SN) collects UE history information?

- All MR-DC scenarios?

- Any other topic based on contributions submitted

- If there are agreements, can proceed to CRs

(ZTE - moderator)

Summary of offline disc R3-205511

# For the Chairman’s Notes

Propose the following:

# Discussion

## UE history information of secondary node? (e.g. PSCell, other information?)

UE history information of secondary node includes:

PSCELL list [1][2][3][4]

Cell type [1][2][3][4]

Time UE Stayed in Cell  [1][2][3][4]

New HO cause value [4] (e.g MN initiated Secondary Node Modification)

Provide your view:

Proposal: UE history information of secondary node includes 
PSCELL list, Cell type, time UE stayed in the cell, HO cause value (includes new cause value).

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes | Propose to be aligned with UE history information of MN. |

## Which node (MN or SN) collects UE history information?

Approach 1: SN collect UHI in the SN, SN provides UHI to MN, MN provides UHI to target SN [2] [3] [4]

Approach 2: MN collects UHI of old SN, MN provides old SN UHI to target SN [4]

Approach 3: pleas provides your solution

Provide your view

| Company | Approach | Comment |
| --- | --- | --- |
| CATT | 2 | SN may be removed and cannot keep UE context. MN is used as anchor which can take the responsibility to record SN related information and send UHI to SN. |

## Support all MR-DC scenarios

To confirm whether UHI of SN apply to all MR-DC scenario.

Provide your view

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes |  |

## Relationship of MN UHI with SN UHI

Approach 1: independent [2]

MN with SN released + SN collected SN UHI

Approach 2: co-related [3][4]

SN UHI co-related with MN UHI ( one dimension , two dimension)

Provide your view:

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Approach 2 | For cell coverage relationship, MN and SN are co-related. MN UHI and SN UHI may be used together to optimize mobility and should be co-related. For one or two dimension, as analysis in [3] ,one dimension may save storage resources. |

## SN UE history information from the UE

Proposal : It is proposed to enhance UE history information from UE for MR-DC. [3][4]

Provide your view:

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes |  |

# Conclusion, Recommendations [if needed]

If needed

# References

| 1 | R3-204898 | Discussion on support of UE history information (China Telecommunication) | discussion |
| --- | --- | --- | --- |
| 2 | R3-204936 | UE history information in EN-DC (Huawei) | discussion |
| 3 | R3-205131 | Enhancement of UE history information in EN-DC scenario (CATT) | discussion |
| 4 | R3-205310 | UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility) | discussion |
| 5 | R3-205311 | 37340 CR for UHI of MR-DC (ZTE) | other |
| 6 | R3-205312 | CR for UHI of MR-DC in TS36.423 (ZTE) | other |
| 7 | R3-205313 | CR for UHI of MR-DC in TS38.413 (ZTE) | other |
| 8 | R3-205314 | CR for UHI of MR-DC in TS38.423 (ZTE) | other |
| 9 | R3-205458 | Discussion for UE History Information in EN-DC (BEIJING SAMSUNG TELECOM R&D) | discussion |
| 10 | R3-205459 | X2AP impacts for UE history information in EN-DC (BEIJING SAMSUNG TELECOM R&D) | CR1541r, TS 36.423 v16.2.0, Rel-17, Cat. B |