3GPP TSG-RAN WG3 #109-e							R3-205511

17-28 August 2020

Online

Agenda Item:	10.2.1.4

Source:	ZTE (moderator)

Title:	Summary of Offline for MR-DC UHI

Document for:	Approval

# Introduction

CB: # 1004_SONMDT_UEHist

-  Topics to discuss:

- UE history information of secondary node (e.g. PSCell, other information?)

- Xn, and X2 impacts

- Which node (MN or SN) collects UE history information?

- All MR-DC scenarios?

- Any other topic based on contributions submitted

- If there are agreements, can proceed to CRs

(ZTE - moderator)

Summary of offline disc R3-205511

# For the Chairman’s Notes

Propose the following:

Proposal 1: enhancement of UE History Information for Secondary Node applies to all MR-DC scenario.

Proposal 2: UE history information of secondary node includes :PSCELL list,  time UE stayed in the cell.

Open issues:

FFS for Cell type, HO cause value be collected for UE history information of secondary node.

FFS Which node (MN or SN or both) collects UE history information(network side) for Secondary Node.

FFS whether to co-relate UE history information of Secondary node with Master node.

FFS enhance UE history information from the UE for Secondary Node.

# Discussion

## UE history information of secondary node? (e.g. PSCell, other information?)

UE history information of secondary node includes:

PSCELL list [1][2][3][4]

Cell type [1][2][3][4]

Time UE Stayed in Cell  [1][2][3][4]

New HO cause value [4] (e.g MN initiated Secondary Node Modification)

Provide your view:

Proposal: UE history information of secondary node includes 
PSCELL list, Cell type, time UE stayed in the cell, HO cause value (includes new cause value).

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes | Propose to be aligned with UE history information of MN. |
| Ericsson | Yes | It FFS if new cause values are needed |
| Qualcomm | Yes | We are not sure about including HO cause value. UE reported mobility history can’t include the HO cause value as UE will not be aware of the SN addition/modification/change. |
| China Telecom | Yes | Agree with QC, whether to include New HO cause value need FFS, OK to include PSCELL list, Cell type and time UE stayed in the cell. |
| Samsung | Yes | OK to include PSCELL, Cell type and time UE stayed in the cell FFS for New HO cause value |
| Huawei | Yes | Cause value is FFS |
| Nokia | Yes | We think that the cell type in case of PSCell should be FFS still. Historically, cell types were considered a burden to define, while little help in use. It should be thought through if the same burden is to be placed on SN nodes. |
| Lenovo, Motorola Mobility | Yes | FFS on cause value |
| ZTE | Yes |  |

Conclusion: UE history information of secondary node includes 
PSCELL list,  time UE stayed in the cell.

FFS for Cell type, HO cause value.

## Which node (MN or SN) collects UE history information?

Approach 1: SN collect UHI in the SN, SN provides UHI to MN, MN provides UHI to target SN [2] [3] [4]

Approach 2: MN collects UHI of old SN, MN provides old SN UHI to target SN [4]

Approach 3: pleas provides your solution

Provide your view

| Company | Approach | Comment |
| --- | --- | --- |
| CATT | 2 | SN may be removed and cannot keep UE context. MN is used as anchor which can take the responsibility to record SN related information and send UHI to SN. |
| Ericsson | 1 |  |
| Qualcomm | 2 | Currently UE doesn’t support sending UHI directly to SN as UEInformationResponse (which includes MobilityHistoryReport) is sent only to MN via SRB1 or SRB2 as highlighted below: UEInformationResponse The UEInformationResponse message is used by the UE to transfer information requested by the network. Signalling radio bearer: SRB1 or SRB2 (when logged measurement information is included) RLC-SAP: AM Logical channel: DCCH Direction: UE to network We therefore prefer Approach 2 to minimize RAN2 impacts, where MN can request and collect SN mobility history and can then forward SN UHI to target SN. |
| China telecom | 2 | For approach 1, it needs more X2/Xn signaling and may fail to provide UHI to MN during SN change procedure (i.e. the radio condition is tough between MN and SN). For approach 2, it is more adoptable since MN can already collect UE history information of MN for legacy handover, it can also collect UE history information of SN during SN addition/change/release procedures. |
| Samsung | 1 |  |
| Huawei | 1 | For approach 2, MN need to know the new PSCell cell ID for the intra-SN PSCell change. It need more interaction between MN and SN. Note also that we are talking about the network reported UE mobility history and not the UE reported mobility history. |
| Nokia | 1 | MN may not be aware of intra-SN PSCell changes so, it can’t track those. |
| Lenovo, Motorola Mobility | 1 | We need to take intra-SN PSCell change into account. |
| ZTE | 2 | The issue relates to answer in section 3.4. |

Conclusion : FFS Which node (MN or SN or both) collects UE history information(network side) for Secondary Node.

## Support all MR-DC scenarios

To confirm whether UHI of SN apply to all MR-DC scenario.

Provide your view

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes |  |
| Qualcomm | Yes |  |
| China Telecom | Yes |  |
| Samsung | Yes |  |
| Huawei | Yes |  |
| Nokia | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| ZTE | Yes |  |

Conclusion: enhancement of UE History Information for Secondary Node applies to all MR-DC scenario.

## Relationship of MN UHI with SN UHI

Approach 1: independent [2]

MN with SN released + SN collected SN UHI

Approach 2: co-related [3][4]

SN UHI co-related with MN UHI ( one dimension , two dimension)

Provide your view:

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Approach 2 | For cell coverage relationship, MN and SN are co-related. MN UHI and SN UHI may be used together to optimize mobility and should be co-related. For one or two dimension, as analysis in [3] ,one dimension may save storage resources. |
| Ericsson | Approach 2 | The essence is that for each PCell it is possible to understand the chronological sequence of PSCells the UE was connected to. How to encode it can be left to stage 3 discussions |
| Qualcomm | Approach 2 | As per our response to section 3.2, MN should handle both MN and SN UHI. Therefore a correlated UHI (Approach 2) is our preference. |
| China Telecom | Approach 2 | Similar view as QC, we prefer MN to collect UHI of both MN and SN, so we think co-related UHI is more suitable. |
| Samsung | Approach 2 | Agree with Ericsson |
| Huawei | Approach 1 | Note however that even if the IEs are separate, the information can be correlated since we include the time spent in cells and also when there is no SN. The benefit is that there is no extra burden for MN to merge the information. Having a separate list for SN makes sense since this is sent to SN for SN triggered mobility purposes. The information (when combined with the legacy report) can be used by MN for MN triggered SN change |
| Nokia | Approach 1 | UHI is meant to enable avoiding issues like ping-pongs (incl. multi-cell ping-pongs), so it is relevant for the node that controls mobility. In typical scenario, SN is responsible so SN UHI is enough for the SN. Matching it with MN UHI will cause burden, while does not seem to bring much benefits (and not sure if possible always, e.g. in case of intra-node HOs and intra-SN PSCell changes). |
| Lenovo, Motorola Mobility |  | Stage 3 issue. |
| ZTE | Approach 2 | Share the view with Ericsson. |

Conclusion: FFS whether to co-relate UE history information of Secondary node with Master node.

## SN UE history information from the UE

Proposal : It is proposed to enhance UE history information from UE for MR-DC. [3][4]

Provide your view:

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | Yes |  |
| Ericsson | Yes | It is proposed that the UE History Information from the UE is extended to mirror the addition of PSCell history. It is proposed that the SN can request the UE (via the MN) to provide the UE History Information from the UE so that it can use it together with the network based UE History Information |
| Qualcomm | Yes | We agree to enhance UE UHI with PSCell history information similar to PCell history. Regarding how and when to request SN UHI: For MN initiated SN change, MN knows when SN is changing and can request UHI during the SN change For SN initiated SN change, MN can request UHI upon receving SgNB Modification Required message. |
| China Telecom | Yes | Both UE History Information reported from the UE and collected by the network should be support in this release. |
| Samsung |  | This should be decided by RAN2 firstly. |
| Huawei | Yes | Having similar information as in network UHI seems reasonable. But the content of the UE history information from UE and how this is reported is in RAN2 scope. If this available in MN, this information should always be included together with the network collected UE history information sent to SN. Then depending on if RAN2 decides that this may also be sent to SN, the information need to be propagated to MN |
| Nokia | FFS for the time being | First, RAN3 shall decide the principles of RAN-side UHI. Once done, RAN2 could see if more can be obtained from the UE. |
| Lenovo, Motorola Mobility | Yes |  |
| ZTE | Yes |  |

Since one company still have concern for the time being, we concludes:

FFS of enhance UE history information from the UE for Secondary Node.

# Conclusion, Recommendations [if needed]

If needed

# References

| 1 | R3-204898 | Discussion on support of UE history information (China Telecommunication) | discussion |
| --- | --- | --- | --- |
| 2 | R3-204936 | UE history information in EN-DC (Huawei) | discussion |
| 3 | R3-205131 | Enhancement of UE history information in EN-DC scenario (CATT) | discussion |
| 4 | R3-205310 | UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility) | discussion |
| 5 | R3-205311 | 37340 CR for UHI of MR-DC (ZTE) | other |
| 6 | R3-205312 | CR for UHI of MR-DC in TS36.423 (ZTE) | other |
| 7 | R3-205313 | CR for UHI of MR-DC in TS38.413 (ZTE) | other |
| 8 | R3-205314 | CR for UHI of MR-DC in TS38.423 (ZTE) | other |
| 9 | R3-205458 | Discussion for UE History Information in EN-DC (BEIJING SAMSUNG TELECOM R&D) | discussion |
| 10 | R3-205459 | X2AP impacts for UE history information in EN-DC (BEIJING SAMSUNG TELECOM R&D) | CR1541r, TS 36.423 v16.2.0, Rel-17, Cat. B |