3GPP TSG-RAN WG3 #109-e	R3-205581

Online, 17-28 August 2020

Agenda Item:	10.2.5

Source:	CATT (moderator)

Title:	Summary of Offline discussion on 2 step RACH optimization

Document for:	Approval

# Introduction

This contribution triggers the discussion on the following issue.

CB: # 1011_SONMDT_2StepRACH

-  Topics to discuss:

- Rel-16 as BL?

- UE RACH report

- 2-step PRACH configuration

- Xn, F1 impacts

- LS to RAN2

- Any other topics based on contributions submitted

- If there are agreements, can proceed to LS

(CATT - moderator)

Summary of offline disc

Please provide you views before Wednesday online session.

# For the Chairman’s Notes

Propose the following:

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Issue 1: Whether 2-step RACH related PRACH parameters should be coordination between two NG-RAN nodes.

In most the contributions submitted this meeting[2][3][4][5][6], it is proposed to coordinate the PRACH parameters between the neighbor NG-RAN nodes in case 2-step RACH is configured. So, we propose to agree on support of PRACH parameters coordination for 2-step RACH. If there is any different view, please list your comments here.

| Company | Comment |
| --- | --- |

## Issue 2 Whether current NR PRACH Configuration IE could be re-used for 2-step RACH coordination or not?

As to how to support PRACH parameters coordination for 2-step RACH, different options are proposed as below:

Option 1:Re-use current NR PRACH Configuration IE[2][3]

Option 2: Introduce a new independent 2-setp PRACH Configuration IE[4]

Companies are invited to provide your views here

| Company | Comment |
| --- | --- |

## Issue 3 Whether PUSCH resource information needs to be communicated between neighbouring gNBs

For 2-step RACH configuration, it includes both PUSCH and PRACH resource information.As to whether PUSCH related resource should be transferred between two neighbor nodes,there are different views as below:

Option 1: PUSCH is always interference limited,so no need to do optimization on this point.[2]

Option 2: PUSCH resources need to be communicated between neighbouring nodes [6]

Companies are invited to provide your views here

| Company | Comment |
| --- | --- |

## Issue 4: Whether UE RA-Report should be enhanced to support 2-step RACH related optimization

In all of the contributions submitted this meeting, it is proposed to enhance the current UE RA-Report to support 2-step RACH related optimization. So, we propose to agree to support enhancement of UE RA-Report for 2-step RACH related optimization. If there is any different view, please list your comments here.

| Company | Comment |
| --- | --- |

## Issue 5: Which parameter should be introduced in UE RA-Report to support 2-step RACH optimization

Some contributions provide proposals on the parameters that should be introduced in UE RA-Report for RACH optimization as below.

  - Configured threshold used for RA type selection i.e. msgA-RSRP-Threshold-r16 and whether the DL quality associated to the random access attempt was above or below the threshold for each RACH attempt

  - The configured maximum transmission number of MSG A preamble i.e. msgA-TransMax-r16 and RACH type of each RACH attempt

  - Whether DL beam quality associated to the random access attempt is above or below the msgA-RSRP-ThresholdSSB-r16 for each RACH attempt

  - Whether fallback RAR is received in MSGB or not, i.e. Whether UE is requested to send message 3 for each 2-step RACH attempt.

  - PUSCH resources and PRACH resources allocated for msgA

  - Configuration of RA types by network

  - Whether the RO is shared

Companies are invited to provide your views on the above parameters, then based on output of the discussion, we could draft the LS to RAN2.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-204760 RACH optimization in 2 step RACH  Huawei

R3-205021 2-step RACH optimization for SON  Ericsson

R3-205116 Discussion on RACH optimization for 2-step RACH CATT

R3-205335 Initial consideration on Two-Step RACH Optimization for SON    ZTE, China Telecom, China Unicom

R3-205437 2-step RACH optimization CMCC

R3-205204  2--step RACH Configuration Exchange Nokia, Nokia Shanghai Bell