3GPP TSG-RAN WG3 #109-e	R3-205516

Online, 17-28 August 2020

Agenda Item:	10.2.3

Source:	CMCC (moderator)

Title:	Summary of inter-system inter-RAT energy saving support

Document for:	Approval

# Introduction

CB: # 1009_SONMDT_InterSystemEnergy

-  Topics to discuss:

- Deactivation indication

- Activation indication

- Cell state indication

- NG, S1 impacts (IEs, information to transfer, etc)

- Any other topics based on contributions submitted

- If there are agreements, can proceed to CRs

(CMCC - moderator)

Summary of offline disc

Since the scenarios and preliminary solutions have been discussed in the Rel-16 RAN-centric DCU SI, the views from the papers seem consistent.

The email discussion is divided into two phases:

Phase 1: Reach the agreements on cell state indication, cell activation request/response and enhancement of NG/S1 messages

Phase 2: Work on CRs based on the agreements in phase 1, if possible

# For the Chairman’s Notes

TBD

# Discussion

## Cell state indication

Based on the reference papers, an agreement can be made that when the NR capacity booster cell is switched-off by the NG-RAN node, the NG-RAN node should indicate the switch-off action to the eNB.

Proposal 1: A cell state indication should be sent from the NG-RAN node to the eNB to indicate the status of the concerned cell for energy saving purpose.

Question: Do you agree with the proposal?

| Company | Comments |
| --- | --- |
| Huawei | Agree |
| CATT | Yes |
| ZTE | yes |
| China Telecom | yes |
| China Unicom | Yes |
| Samsung | Yes |

## Cell activation request/response

Based on the reference papers, an agreement can be made that an eNB should send the cell activation request to the NG-RAN node when the eNB decides to activate the dormant capacity booster cell and a NG-RAN node should send the response/reply to the eNB to indicate that one or more cell(s) previously switched-off has (have) been activated.

Proposal 2: A cell activation request should be sent from eNB to NG-RAN node to request a previously switched-off cell/s to be re-activated.

Proposal 3: A cell activation response should be sent from NG-RAN node to eNB to indicate that one or more cell(s) previously switched-off has (have) been activated.

Question: Do you agree with the proposals?

| Company | Comments |
| --- | --- |
| Huawei | Agree |
| CATT | Yes |
| ZTE | YES |
| China Telecom | yes |
| China Unicom | Yes |
| Samsung | Yes |

## Enhancement of NG/S1 messages

From companies’ opinions, the Inter-system SON information in the following procedures can be enhanced to support inter-system inter-RAT energy saving.

- eNB CONFIGURATION TRANSFER (TS36.413)

- MME CONFIGURATION TRANSFER (TS36.413)

- UPLINK RAN CONFIGURATION TRANSFER (TS38.413)

- DOWNLINK RAN CONFIGURATION TRANSFER (TS38.413)

Proposal 4: Enhance Inter-System SON Information message on S1AP and NGAP to support inter-system Energy Savings.

Question: Do you agree with the proposal?

| Company | Comments |
| --- | --- |
| Huawei | Agree |
| CATT | Yes |
| ZTE | YES |
| China Telecom | Yes . we see the need to enhance the NG/S1 message to support ES feature in inter-system scenario. |
| China Unicom | Yes, S1AP and NGAP should support inter-system energy savings. |
| Samsung | Yes |

## Detailed IEs

A notify flag in the cell state indication is introduced to inform the status of the concerned cells is activated or deactivated.

Question: Do you agree to introduce these IEs?

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| CATT | Yes |
| ZTE | YES |
| China Telecom | yes |
| China Unicom | Yes |
| Samsung | Yes |

Cells to activate list, the activation ID and optionally the minimum activation time are proposed to be included in the cell activation request.

Question: Do you agree to introduce these IEs?

| Company | Comment |
| --- | --- |
| Huawei | No problem to have the first 2. Just question for clarification, what is the minimum activation time used? Is it essential for the inter-system ES? |
| CATT | OK with IEs other than activation ID. Since activation ID is not introduced in LTE, further discussion is needed on whether to introduce or not. |
| ZTE | OK with the first one. Since the Activation ID is not used in Inter system energy saving between E-UTRAN and UTRAN, more clarification is need . And for the minimum activation time IE, it seems not necessary. |
| China Telecom | OK with the first one |
| China Unicom | Yes, Cells to activate list, the activation ID are needed for indication, minimum activation time is beneficial for cell management and the granularity of this IE maybe hour, or 15 minutes, and potentially this IE could be optional. |
| Samsung | OK with Cells to activate list and optionally the minimum activation time. More clarification is needed for activation ID. |

The activated cells list and activation ID are proposed to be included in the cell activation response to inform the action result of the concerned cells.

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| CATT | Similar as above. |
| ZTE | Similar as above. |
| China Telecom | Similar as above |
| China Unicom | Agree |
| Samsung | Similar as the answer to previous question. |

## Work on CRs

Depending on the results of the above discussion, split of the CRs among companies can be done in the phase 2 discussion.

# Conclusion, Recommendations [if needed]

If needed

# References

- R3-204764 Inter-system inter-RAT energy saving, Huawei.

R3-205259 Discussion on inter-system inter-RAT energy saving, CATT.

R3-205328 Consideration on inter-system inter-RAT energy saving, ZTE, China Telecom, China Unicom.

- R3-204802 Inter-system Inter-RAT Energy Saving, Qualcomm.

- R3-205419 NGAP impacts for Inter-System Inter-RAT Energy Saving, Samsung.