3GPP TSG-RAN WG3 #109	R3-205499

17-27 August 2020

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on MBS Mobility with Service Continuity                                                                                   – CP and UP

Document for:	Approval

# Introduction

CB: # 18_MBS_Mobility_SvcCont_CPUP

- HW,LGU+

It is needed to exchange the ongoing MBS service information between gNBs, before or during HO.

The configuration of the MBS service in the target gNB should be sent to UE via the source gNB during MBS to MBS handover.

Further discuss the impacts over Xn/NG/F1/E1 interfaces to support “Intra-DU Inter-cell”, “Intra-CU Inter-DU” and “Inter-CU” cases.

Further discuss how to minimize data loss during MBS session to MBS session mobility.

The sequence numbers for the same MBS packet received by different gNBs should be aligned.

- Nok (4844)

UE-associated signaling is used over NGAP by the SMF to signal to the NG-RAN node the relation between a multicast context and UE’s PDU sessions.

Reuse the PDU Session Resource Modify Request message enhanced by adding the MBS Context ID corresponding to the multicast which the UE has joined/left via that PDU session.

- Nok (4845)

NG-RAN node directly signals to the MB-SMF to request the setup of the N3 shared tunnel. This applies to both context creation at first UE joining and incoming handover.

To enable the setup, the SMF should have included the MB-SMF ID in the PDU Session Resource Modify Request message and this is stored in the UE context. The UE transfers it at subsequent mobility as part of the UE context transfer enabling the target NG-RAN node to setup the N3 path.

NG-RAN node directly signals to the MB-SMF to request the release of the N3 shared tunnel. Message used is FFS. This applies to both context removal at last UE leaving and outgoing handover.

- Len,Moto

Confirm the issue on PDCP Count Value misalignment which may cause packet lost during handover if the existing data forwarding and SN STATUS TRANSFER message are used.

Discuss the penitential solutions if the issue on PDCP Count Value misalignment is confirmed.

++ Suggested guidelines/topics for discussion from Chair (looking at possible consensus):

+ Whether to exchange MBS configuration between nodes (merge disc. from 5443,5120)? (possible agreement/WA?)

+ Use UE-associated signaling? (possible agreement?) Reuse current PDU Session Resource Mod Req? Tunnel release? Other NGAP details? (possible agreement/WA?)

+ Merge disc. from 5120 (packet retransmission issue)

+ Discuss PDCP count misalignment issue?

+ Any E1 impacts?

+ Attempt NGAP,XnAP,E1AP TPs? (lots of FFSs)

(Nok - moderator)

Summary of offline disc R3-205499

# For the Chairman’s Notes

Propose the following:

R3-20xxx – agreed

R3-20xxx– agreed.

# Discussion

## Handover of MBS Session (between two MBS supporting gNBs)

Is it needed for the source gNB to be aware whether the MBS session being handed over has been setup in the target gNB before or during handover (R3-204691)?

| Company | Comment |
| --- | --- |
| Nokia | No. source gNB just needs to know if target gNB supports MBS or not in general. If target gNB supports MBS, then the MBS session will be setup at incoming handover. |
| Qualcomm | Yes. The information is useful for handover target selection. Dynamic MBS session setup should be supported. To reduce the handover delay and user plane interruption, we should minimize the dynamic MBS session setup. |
| Samsung | Not sure. If only consider the connected mode, it is not so critical to know that. |

Should the configuration of MBS in target gNB be sent to UE via source gNB in MBS to MBS handover (R3-204691)?

| Company | Comment |
| --- | --- |
| Nokia | Yes, as in normal handover. Either the DRB configuration or the MRB configuration. |
| Qualcomm | Yes. Agree with Nokia. |
| Samsung | Yes. Send it by dedicated RRC message. |

Should Xn Handover Request include MBS context information per MBS flow? (R3-204691)?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Qualcomm | Yes |
| Samsung | Yes |

Should NG Handover Request include MBS context information per MBS flow? (R3-204691)?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Qualcomm | Yes |
| Samsung | Yes |

Should MRB context info be included in F1 UE Context Setup/Modify? (R3-204691)?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Qualcomm | Yes |
| Samsung | Yes |

Do you agree that some mechanism is needed to minimize packet loss during handover of MBS session especially if target gNB has faster progress than source gNB? (R3-204691)

| Company | Comment |
| --- | --- |
| Nokia | Pending SA2 evaluation. |
| Qualcomm | Yes |
| Samsung | Generally it is beneficial to minimize the packet loss. But how to miminize the loss is related to the L2 protocol. We think we can revisit the lossless support later. |

Should sequence number for same packet received by source and target gNB be aligned to resolve the above packet loss issue? (R3-204691)

| Company | Comment |
| --- | --- |
| Nokia | Postponed. It is too early to discuss which mechanism should be used. Sequence number is unclear as to which sequence numbers is referred to here. |
| Qualcomm | Yes. This is a simple solution. |
| Samsung | This issue can be discussed later. |

Moderator’s summary:

Proposal 1: It is proposed to.

## CP session management for multicast session

Is it ok to introduce MBS context in UE-associated signaling over NGAP message to bind a multicast context with the UE’s PDU session for multicast sessions? (R3-204844)

| Company | Comment |
| --- | --- |
| Nokia | Yes. Better than non-UE associated. |
| Qualcomm | Yes. This question is duplicated with question 5 of CB#16 session management. |
| Samsung | Yes |

Is it ok to introduce MBS context in the PDU Session Modify Request message for the above (to bind a multicast context with the UE’s PDU session for multicast sessions)? (R3-204844)

| Company | Comment |
| --- | --- |
| Nokia | Yes. Seems a good candidate. |
| Qualcomm | Yes. This question is duplicated with question 5 of CB#16 session management. |
| Samsung | Yes |

Moderator’s summary:

Proposal 2: It is proposed to.

## UP Session Management for multicast session

Do you agree that the MBS multicast distribution tree must be updated between the gNB and the MB-UPF for the first UE joining an MBS multicast session at the gNB?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Qualcomm | Yes |
| Samsung | Yes |

Which of these two options do you prefer for updating the multicast distribution tree in above scenario: TNL information pyggy-backed in the joining response message sent from gNB to SMF (option 1) or independent new message sent by gNB to MB-SMF (option 2)

| Company | Comment |
| --- | --- |
| Nokia | Option 2. |
| Qualcomm | Option 1. This question is duplicated with question 6 of CB#16. |
| Samsung | Option 2 |

Do you agree that the MBS multicast distribution tree must be updated between the target gNB and the MB-UPF for the first UE requesting an MBS multicast session and accepted at incoming handover into the target gNB?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Qualcomm | Yes |
| Samsung | Yes |

Which of these two options do you prefer for updating the multicast distribution tree in above scenario: TNL information pyggy-backed in the handover response message sent from target gNB to SMF (option 1) or independent new message sent by target gNB to MB-SMF (option 2) ?

NOTE: it is expected that answer should be consistent with the answer above for the case of “joining”.

| Company | Comment |
| --- | --- |
| Nokia | Option 2. |
| Qualcomm | Option 1 |
| Samsung | Option 2 |

Moderator’s summary:

Proposal 3: It is proposed to.

# Conclusion

The following is proposed:

Proposal 1: It is proposed to .

Proposal 2: It is proposed to.

Proposal 3: It is proposed to.

# References

R3-203446

R3-203542