3GPP TSG-RAN WG3 Meeting #109-e	R3-205502

Electronic Meeting, 17th – 28th August, 2020

Agenda item:		22.4

Source:	vivo

Title:	Summary for CB: # 22_MBS_Counting

Document for:		Discussion and Decision

# 1		Introduction

This is to discuss the following CB: # 22:

C CB: # 22_MBS_Counting - Vv gNB can enquiry the CONNECTED/INACTIVE/IDLE UE’s interests for specific MBS service(s). gNB can count the number of UE(s) interested in specific MBS service(s) via UL feedback (e.g. HARQ feedback). gNB can provide the number of UE’s interested in specific MBS services to the CN. ++ Suggested guidelines/topics for discussion from Chair (looking at possible consensus): + Merge relevant disc. parts from 5364 + Should counting be considered in Rel-17? If so, should it reside in RAN or CN? (Possible agreement/WA) + (Chair: counting was a quite contentious discussion in the past) (Vv - moderator) Summary of offline disc R3-205502

Companies are encouraged to provide inputs until August 21st.

# 2	For the Chairman’s Notes

TBD

# 3		Discussion

## 3.1	Need of Counting

According to “R3-205364” and “R3-204886”, the MBS counting function is proposed to be considered in the Rel-17 MBS work item. The main motivations of the MBS counting function are listed as follows:

- The switching between PTP and PTM of MBS service(s)

- The suspension/resumption of MBS service(s)

The moderator consiers that the following objectives (as the above motivations for counting) of the WID are probably related:

Specify support for dynamic change of Broadcast/Multicast service delivery between multicast (PTM) and unicast (PTP) with service continuity for a given UE [RAN2, RAN3] Study the support for dynamic control of the Broadcast/Multicast transmission area within one gNB-DU and specify what is needed to enable it, if anything [RAN2, RAN3]

Question 1: Should counting be considered in Rel1-17?

| Company | Answer (Yes/No) | Comments |
| --- | --- | --- |
| vivo | Yes | To support the switching between PTP and PTM, the counting is an essential function especially for the switching from PTM to PTP, as the gNB using the broadcasting signaling to configure the UE for MBS reception may not be aware when/whether a UE (e.g. an IDLE/INACTIVE UE) is currently interested in receiving an MBS service. To support the dynamic control (e.g. temporary suspension of a MBS service in a cell) of the MBS transmission area, the gNB should also be able to collect the number of UEs receiving the MBS service. |
| Nokia | No | As far as multicast session is concerned, we don’t see the need for counting procedures as they used to be defined in LTE. |
| Qualcomm | No | Not for multicast. Can be discussed for broadcast. |
| Lenovo, Motorola Mobility | No | For 5G MBS, the assumption is the gNB already knowns the UE status on receiving a 5G MBS service when 5G MBS session starts. No need to have MBMS Service Counting Function |
| Huawei | NO | We think the concerned UEs list/or cells list for multicast/broadcast session could be pused by CN to RAN. Counting might be usefull for broadcast for suspension/resumption of MBS service but it should be deprioritized in this release. |
| ZTE | No | Agree with Nokia, Qualcomm, Lenovo, Huawei that counting is not needed for multicast session. As for broadcast session, another mechanism, called as MBMS interest indication in LTE eMBMS, can be used for UEs to indicate its interest to RAN. It means that RAN can estimate the number of interested UEs without relying on counting mechanism. Based on above observations, it is suggested that no counting mechanism is needed. |
| Samsung | No | Not needed for multicast. Can discuss it if idle mode UE is considered. |

## 3.2	Counting in RAN or CN or both

According to “R3-205364” and “R3-204886”, the MBS Counting function is proposed to be implemented in RAN. According to the LTE MBMS function, both RAN and CN has its own counting function, which are used for the control of the MBS services at different perspectives. For example, the Couting in RAN could be used for the suspension/resumption of MBS service in RAN, and the Couting in CN could be used to determine the MBSFN transmission area.

From the moderator’s understanding, the Couting in RAN means that the gNB can collect the UE’s MBS interest via the RAN signalling (e.g. RRC), and the Couting in CN means that the CN node can collect the UE’s MBS interest via the CN signalling (e.g. NAS).

Question 2: If counting is to be implemented in Rel-17, should counting be implemented in RAN or CN or both?

| Company | Answer (RAN/CN/Both) | Comments |
| --- | --- | --- |
| vivo | At least in RAN | We consider that the RAN or the CN may have different use cases for couting the number of UEs interested in a certain MBS service. The RAN counting is more suitable for the dynamic switching between PTP and PTM in RAN and the dynamic suspension/resumption of MBS service in RAN. The CN couting is more suitable for the CN-based switching between PTP and PTM and for the management of the multicast group. |
| Nokia | No | As far as multicast session is concerned, we don’t see the need for counting procedures as they used to be defined in LTE. Besides, CN is excluded from PtP/PtM switching. |
| Qualcomm | No | Counting is not needed for multicast. If counting is supported for broadcast, it should be RAN function. |
| Lenovo, Motorola Mobility | No | No need to have MBMS Service Counting Function |
| Huawei | No | No need for counting for Rel-17 |
| ZTE | No | No counting mechanism is needed for Broadcast and Multicast session. |
| Samsung | No |  |

## 3.2	Location of RAN Counting function

According to “R3-205364” and “R3-204886”, the RAN Couting is proposed to be located in the CU.

From the moderator’s understanding, the location of the Couting function can be decoupled from the location of the functions (e.g. suspension/resumption of the MBS service or switching between PTP and PTM) which could use the counting results, as the RAN entity implemented with the Counting function can provide the counting result(s) to the corresponding RAN entity using the counting results.

Question 3: If counting is to be implemented in RAN, should the RAN counting be implemented in CU or DU?

| Company | Answer (CU/DU) | Comments |
| --- | --- | --- |
| Vivo | CU | We consider that the RAN counting should be done via the RRC signalling (as LTE) in CU. Then the CU can provide the counting results to DU/CN/other CU which requires the counting results. Furthermore, the UE’s response to the counting request should also be verified by the network, e.g. via the MAC-I attached in the PDCP PDU of the SRB. Using the DU (which does not have the PDCP/RRC layer) to collect the UE interest could be difficult to verify the UE. |
| Nokia | Not applicable | As far as multicast session is concerned, we don’t see the need for counting procedures as they used to be defined in LTE. |
| Qualcomm | Either | Counting is not needed for multicast. For broadcast, if counting is needed, it can be supported in either RRC layer by CU or lower layer by DU. |
| Lenovo, Motorola Mobility | Not applicabe | No need to have MBMS Service Counting Function |
| Huawei | NO |  |
| ZTE | Not applicable | No counting mechanism is needed for Broadcast and Multicast session. |
| Samsung | Not applicabe |  |

# 4		Conclusion

TBD

# 5		Reference

| 22.4. Others |
| --- |
| R3-204886 | Counting the MBS interest (vivo) | discussion |
| R3-205364 | NG-RAN Architecture Discussion for MBS (CATT) | discussion Move to 22.2 |