3GPP TSG-RAN WG3 #109e	R3-205506

Online, 17-28 August 2020

Agenda Item:	22.3.1

Source:	Lenovo, Motorola Mobility (moderator)

Title:		Summary of Offline Discussion on MBS PDCP Count Value Misalignment

Document for:	Approval

# Introduction

CB: # 39_MBS_UP_count

- Len,Moto

Confirm the issue on PDCP Count Value misalignment which may cause packet lost during handover if the existing data forwarding and SN STATUS TRANSFER message are used.

Discuss the potential solutions if the issue on PDCP Count Value misalignment is confirmed.

- HW,LGU+ (merge as relevant from 4690)

Further discuss how to minimize data loss during MBS session to MBS session mobility.

The sequence numbers for the same MBS packet received by different gNBs should be aligned.

(Len - Moderator)

Summary of offline disc R3-205506

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

As discussed in [1]: For Scenario 3, i.e. MBS-to-MBS Handover scenario, as the source gNB and the target gNB perform the transmission of one MBS service independently, the transmission progress of MBS packets may be different. For example, the MBS packets from UPF/MB-UPF may arrive at different gNBs at different time because of various backhaul transmission delay; different gNBs may have different buffer status which lead to different scheduling progresses. Especially if the target gNB has faster progress than the source gNB, the UE will miss many MBS packet after handover, which cannot be tolerated by the high reliability requirement.  As the MBS transmission gap is hard to avoid, especially for inter CU case or inter DU case, filling in the gap should be an important direction to work with. In order to figure out the progress gap by the gNBs, the sequence numbers for the same MBS packet received by different gNBs should be aligned. With that, the source gNB and the target gNB can further proceed to minimize the data gap or forward the data for the UE during mobility.

Q1: Do companies agree that the sequence numbers for the same MBS packet received by different gNBs should be aligned for lossless handover.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | No | PDCP SN will not help here because there is no sync between the PDCP entities in source and target cell. |
| Qualcomm | Yes | UPF shall assign same sequence number in GTP-U for same packet to different gNBs. If this required is confirmed by SA2/CT4, we can discuss PDCP COUNT alignment in RAN3. |
| Lenovo, Motorola Mobility | Yes | The length of GTP-U SN is two bytes which may not sufficient. PDCP SN alignment is RAN issue. It could be better RAN to find a solution firstly. If needed, a LS to SA2 is better. |

As discussed in [2]: The 5G MBS needs to support PTM mode. In PTM mode, the 5G MBS service is multicast over one or multiple cells. The source gNB and target gNB may allocate independent PDCP Count Value for the same packet from CN. One use case is the target gNB may join the multicast IP group later than the source gNB. The PDCP Count value misalignment will cause packet lost during handover from source to target if the existing data forwarding, SN STATUS TRANSFER and PDCP STATUS REPORT are used.

Q2: Do companies confirm the issue on PDCP Count Value misalignment which may cause packet lost during handover if the existing data forwarding, SN STATUS TRANSFER and PDCP STATUS REPORT are used.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Yes | This is not aligned. |
| Qualcomm | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |

As discussed in [2], there are be three solutions to solve the PDCP Count Value misalignment issue and enable loss-less handover.

- Solution 1: PDCP Count Value Coordination based a SN from CN

- Solution 2: Anchor PDCP based solution (DC-liked)

- Solution 3: End marker and dedicated bearer based solution

Q3: companies are invited to provide their views on the potential solutions to solve the PDCP Count Value misalignment issue for loss-less handover.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | ? we should first have the confirmation that lossless is a compelling requirement, is this the case? | Wait SA2 conclusion on key issue 27. |
| Qualcomm | Yes | We can wait for SA2 conclusion first. Some enhancements in handover preparation and data forwarding would be useful. |
| Lenovo, Motorola Mobility | Yes. | It is RAN issue. It could be better RAN to find a solution firstly. If needed, a LS to SA2 is better. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-204691 Service continuity CP and UP aspects during mobility (Huawei, LGU+)

R3-204922 Support of Loss-less handover for 5G MBS (Lenovo, Motorola Mobility)