3GPP TSG-RAN WG3 #109	R3-205583

# Online, 17th - 28th August 2020

Agenda Item:	9.2

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion on SFTD measurements report

Document for:	Approval

# Introduction

CB: # 61_SFN_SFTP_LPPa

-  deployment scenario: are measurements expected to be available at RAN node?

- limit disc. to LPPa

- NRPPa scope already discussed in AI 19

(E/// - moderator)

Summary of offline disc R3-205583

# For the Chairman’s Notes

Propose the following:

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Discussion on deployment scenario

The deployment scenario discussed in [1] concerns multi-RAT scenario when the UE is in NR cell and it has to perform LTE OTDOA; then it needs to receive the SFTD between the reference LTE cell and current NR cell. Those SFTD between different cells have been already agreed and available in RRC, see below:

#### MeasResultCellListSFTD-NR

The IE MeasResultCellListSFTD-NR consists of SFN and radio frame boundary difference between the PCell and an NR cell as specified in TS 38.215 [9] and TS 38.133 [14].

MeasResultCellListSFTD-NR information element

-- ASN1START

-- TAG-MEASRESULTCELLLISTSFTD-NR-START

MeasResultCellListSFTD-NR ::=          SEQUENCE (SIZE (1..maxCellSFTD)) OF MeasResultCellSFTD-NR

MeasResultCellSFTD-NR ::=              SEQUENCE {

physCellId                            PhysCellId,

sfn-OffsetResult                      INTEGER (0..1023),

frameBoundaryOffsetResult             INTEGER (-30720..30719),

rsrp-Result                           RSRP-Range                      OPTIONAL

}

-- TAG-MEASRESULTCELLLISTSFTD-NR-STOP

-- ASN1STOP

MeasResultCellSFTD-NR field descriptions

sfn-OffsetResult Indicates the SFN difference between the PCell and the NR cell as an integer value according to TS 38.215 [9].

frameBoundaryOffsetResult Indicates the frame boundary difference between the PCell and the NR cell as an integer value according to TS 38.215 [9].

It does mean that the importance of collecting this data from the UE is something that has already been proofed for an NR cell, and available at the RAN node. Can companies agree with this first common understanding?

| Company | Comment |
| --- | --- |
| Ericsson | Yes |
| Qualcomm | The description is incorrect in several ways The UE does not “need” to receive the SFTD between the reference LTE cell and current NR cell. It benefits (shorter acquisition time) from doing so, similarly to existing OTDOA scenarios not involving NR serving cell. Also the UE does not receive SFTD in LPP, SFTD is a measurement, the UE receives an estimate of the window for acquiring the LTE reference cell. The last paragraph has no relevance to the problem description. We should start by agreeing the scope of the problem. |
| Ericsson2 | The SFTD represents the SFN and frame timing difference (SFTD): Definition The observed SFN and frame timing difference (SFTD) between an E-UTRA PCell and an NR PSCell (for EN-DC), or an NR PCell and an E-UTRA PSCell (for NE-DC), or an E-UTRA PCell and an NR neighbouring cell is defined as comprising the following two components: - SFN offset = (SFNPCell - SFNTRGCell) mod 1024, where SFNPCell is the SFN of a PCell radio frame and SFNTRGCell is the SFN of the target-cell radio frame of which the UE receives the start closest in time to the time when it receives the start of the PCell radio frame. - Frame boundary offset = , where TFrameBoundaryPCell is the time when the UE receives the start of a radio frame from the PCell, TFrameBoundaryTRGCell is the time when the UE receives the start of the radio frame, from the target cell, that is closest in time to the radio frame received from the PCell. The unit of (TFrameBoundaryPCell - TFrameBoundaryTRGCell) is Ts. Applicable for RRC_CONNECTED The SFN offset is provided from the location served in LPP to UE as nr-LTE-SFN-Offset-r15 Frame boundary offset is also provided to UE via LPP as nr-LTE-fineTiming-Offset-r15 Those two are the ones signaled over LPP, and there is no way for the LMF to receive the information for constructing the OTDOA AD when the UE is NR cell and has to do OTDOA. This is the main problem we are trying to clarify. |
| Qualcomm 2 | Our comments stand. This is not a E-UTRAN problem and anyway as we have tried to explain, this is not a good solution. We can provide an alternative on NRPPa if anyone is interested to solve the problem. |

Then, when the RAN node can report the available SFTD between NR or LTE cells, it can help the location server building the timing difference between LTE and NR Cell which can be used for LTE OTDOA assistance data when UE in NR cell, which will be signaled over LPP. However, today the location server considers that the SFTD information is granted via implementation, but implementation will not work for multi-vendor and for multi RAT environments! What the proposals in [1] try to address is to add the missing protocol transfer from the TRP to the LMF over NRPPa or LPPa.

If companies confirm that such data is already collected from the UEs at the cells, then why not transferring it to the location server for both reducing the process and assessing and improving the integrity of the assistance information?

| Company | Comment |
| --- | --- |
| Ericsson | as explained in [1], those SFTD are always available in the RAN node, and in LPP those IEs are defined in the OTDOA assistance data. Today, constructing assistance data at the E-SMLC and LMF for OTDOA has been always considered granted from these nodes, while some data are based on implementation, most other data are again information that these nodes need to collect from other parts of the network or assumed it has been set in these nodes. We all know that providing an up to date and correct assistance information would be among parameters that can enhance the positioning accuracy. |
| Qualcomm | Perhaps the proponents should explain how OTDOA has existed so far since rel-9 (including assistance data which is very similar to what is needed for the NR-LTE case) without requiring RSTD measurements to be reported to the E-SMLC, particularly in MV scenarios. Basically the scenario and the issue are being melted together with a solution. In fact none of the above even describes the problem in a clean way, which should be the first step. Also it is very rare that there is a single solution to a problem, but the first step is to agree the problem. This discussion is unfortunately being structured in a way that makes it hard to progress. |
| Ericsson2 | Qualcomm should be aware that since Rel-15 we have a new RAT called NR, thus two RATs (LTE and 5G). The OTDOA assistance data in LPP TS 37.355 is not RAT agnostic as in Rel-9 and it has been specified that it requires providing the time difference between the LTE and NR cells. Please check the OTDOA Assistance Data Element definition in LPP. Also, in multi-RAT scenarios, there can be more number of cells contributing to the OTDOA or DL-TDOA method, which can improve the positioning performance. The addition of SFTD measurement information to the E-SMLC and LMF would help providing the time difference between the LTE and NR cells for these nodes to provide as an assistance data and improve the accuracy. |
| Qualcomm | We are somewhat aware of what LPP looks like, but appreciate any information… we think there is a possible gap in NRPPa rel15 which can be easily fixed. |

## LPPa impact

If the UE is in LTE cell and performs the SFTD between LTE and NR Cell, then the protocol transfer over LPPa can be used to provide the information from eNB to ESLMC;

| Company | Comment |
| --- | --- |
| Ericsson | with the OTDOA assistance data from Rel.15 forward, the network is dealing with two RATs (LTE and 5G). Therefore, the addition of SFTD measurement information to the E-SMLC and LMF would help providing the time difference between the LTE and NR cells for these nodes to provide in the assistance data. There is need to provide fine timing difference between LTE and NR cells to UE via LPP, thus SFTD measurements which are available in eNB as part of RRM procedure can be used. As this does not include any additional UE overhead, we hope to get support from UE vendors too as this would in turn help UE to save power by not having to perform the fine timing measurements and also could reduce OTDOA time by not having the UE to request gap for the fine timing detection. |
| Qualcomm | As already explained, the E-SMLC has no use for this information as it cannot set up OTDOA procedures towards a UE that needs the information (such UE is served by NG-RAN by definition). Hence there is nothing to discuss in LPPa. |
| Ericsson2 | E-SMLC can provide it to LMF. This would be beneficial in MV case. |
| Nokia | If the measurements have no relevance to the E-SMLC, it should not be introduced to LPPa. |
| Qualcomm | We have never worked on the basis that something needed at the LMF can be provided to the E-SMLC. So let’s not start. Again this is a NRPPa problem for which there is a fairly simple NRPPa solution. |
| Huawei | Thank for the discussions and the clarifications. It seems that there SFTD introduction could assist the E-SMLC, even if it is not perfect. |

## NRPPa impact

If the UE is in NR cell and performs the SFTD between NR and LTE Cell, then the protocol transfer over NRPPa is needed to provide the information from gNB to LMF;

| Company | Comment |
| --- | --- |
| Ericsson | Yes, as explained above |
| Qualcomm | The above says “limit discussion to LPPa”. |
| Huawei | Yes |

## Second phase

Based on the comments received on the points above, the next phase will be the discussion of the CRs in [3] and [4]

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-205210, Reporting of SFN time difference in LPPa and NRPPa (Ericsson, NTT DOCOMO, Huawei)

R3-205487, Response paper to R3-205210

R3-205211, Reporting of SFTD measurements in LPPa E-CID measurement results (Ericsson, NTT DOCOMO, Huawei)

R3-205213, TP to NRPPa: support of SFTD measurements transfer to LMF (Ericsson, Huawei)

# Comments

to be discussed in F1 positioning CB