3GPP TSG-RAN WG3 #109-e							R3-205483

17-28 August 2020

Online

Agenda Item:	17.2

Source:	ZTE (moderator)

Title:	Summary of RAN slicing Remapping Scenarios

Document for:	Approval

# Introduction

CB: # RANSlicing2-Slice_Remapping_Scenarios

- Identify the scenarios and issues with current deployments :

- Mismatch between expected and actual slice coverage and Fallback from expected slice coverage? (NN)

- slice resource shortage in case of Intra-RA mobility and Inter-RA mobility? (ZTE, LG, HW, CMCC)

- non-supported slice in case of Inter-RA mobility?  (ZTE, LG, HW, CMCC )

- whether the scenario of an S-NSSAI not being supported uniformly in a TA is possible and check with SA2? The discussion in SA2 is ongoing (Qualcomm)

- TP for TR, if agreeable

(ZTE - moderator)

Summary of offline disc R3-205483

The email discussion would split into two phases:

Phase 1:  Please provides your inputs before end of the first week (Friday(2020/8/21),17:00 UTC).

Phase 2:  Moderator would draft TP content based on input and collects further input before the ON-line session start. ( Before Tuesday (2020/8/25) 12:00 UTC).

# For the Chairman’s Notes

Propose the following:

# Discussion

## Based on Rel-15 assumption: an S-NSSAI is uniformly supported in a TA

### user case 1: Mismatch between expected and actual slice coverage [3]

From the mobility pattern it is visible that UE1 and UE2 only moves out of the Slice A coverage area for a very short period and then come back to the Slice A supporting coverage area. This could be one of the indications that there is some mismatch between the network slice planning and actual deployment or the assumed mobility patterns and the actual mobility patterns. Therefore, mechanisms are required to detect such problems as well to rectify them in order to minimize the service interruptions experienced by UEs at network slice border areas.

Moderator ‘s note: It is my understanding that the scenario Similar like “Coverage hole ” of Network slicing deployment. With necessary UE’s measurement and RAN enforcement, the Slice coverage hole can be identified. Before the hole be identified and solved by MNO, the UE’s service continuity can be maintained by slice re-mapping /fall back.

Provide your view :

Can we agree to captured this user case into TP:

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes, but treated with low priority | This use case is possible, but it is related to the misconfiguration or mis-planning of network deployment, which can be tested and remedied by MDT etc. So our view is that it can be considered as one of possible use cases, but with low priority. |
| Qualcomm | Tend to no | The use case of UE1 seems outside of the SI scope: could be considered as per Huawei comment on low priority once we tackle the main issues. So we would not think this should be captured for now. |
| Nokia | Yes. | One could argue instead that this use case is actually the most realistic scenario! Indeed, generally speaking, if the slice is deployed for an enterprise the operator will take care that the slice is supported in the cells/TA that cover the enterprise so that slice re-mapping (and this study item) is not/never needed. Therefore, one could argue that the only justification of slice re-mapping study item is exactly this scenario where the anticipated trajectory of the enterprise UEs may not have been perfectly evaluated in planning phase and therefore temporary re-mapping is preferable compared to breaking the call. Of course, we would acknowledge that this should be a temporary situation because the operator should fix this by adding the slice to additional cells/TA. But still we would need a solution during this temporary phase. |
| LG | Tend to no | Similar view with Huawei and Qualcomm. We think this is related to the wrong planning of network deployment. We need to focus on the main issues (e.g. use case 3 or 4) for the slice availability in RA. |
| NEC | Tend to no | We tend to agree that the issue raised in this use case could be addressed by proper configuration and planning of the network deployment. Nonetheless, the use case could be considered at low priority. |

### user case 2: Fallback from expected slice coverage [3]

From the mobility pattern it is visible that UE3 leaves the Slice A supporting area. This could be the case for the user which belongs to the factory/campus where Slice A is available and moves away at off hours.

Because the user belongs to the factory/campus, it is allowed to use the service(s) of Slice A while staying on Slice A supporting area. When leaving the area, the tenant/operator may still prefer to continue the service even in a degraded or non-optimal mode in order to avoid the interruption of service.

Provide your view :

Can we agree to captured this user case into TP:

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes, but.. | This use case can be merged into section 3.1.4: use case 4. |
| Qualcomm | Yes, but | Agree with Huawei, this is use case 4 below. Here it is also written in a way that is suggesting a hint of a solution. It should be made clear whether strict service continuity is part of this use case or not, or whether it is FFS. Maybe we should also define service continuity. |
| Nokia | Yes |  |
| LG | Yes, but | Agree with Huawei |
| NEC | Yes, but | Agree with Qualcomm, the above text indicates a solution “When leaving the area, the tenant/operator may still prefer to continue the service even in a degraded or non-optimal mode in order to avoid the interruption of service.” However, in our understanding, it may not be suitable, based on the service type, to always use a degraded or non-optimal mode to avoid service interruption. |

### User case 3: Slice resource shortage in case of Intra-RA mobility and Inter-RA mobility [6][10][12][14][15][18][19][20]

[14][15]The following use cases can be considered:

For the intra-RA and inter-RA handover, the target NG-RAN node may reject the PDU session for UE’s ongoing slice due to lack of the resource for the slice;

[20]As shown by Figure 1 (a), the UE’s ongoing slice is supported by both the source and the target node. The source node sends handover request message associated with S-NSSAI for UE’s ongoing slice to the target node. The target node fails to accept the UE with the indicated S-NSSAI due to e.g. high slice-related load of the target node. Under such circumstance, the service is interrupted for the UE.

Provide your view :

Can we agree to captured this user case into TP:

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | This case is mentioned in our R3-205083 as use case 1 as follows. Use case 1: the associated network slice is supported by the target NG-RAN node but rejected. |
| Qualcomm | Yes | Details can be considered, but basic use case is that slice resources are temporarily not available (presumably in RAN). |
| Nokia | Yes |  |
| LG | Yes |  |
| NEC | Yes | It is ok to capture the above use case in the TP. |

### User case 4: Non-supported slice in case of Inter-RA mobility[5][8][10][12][18][19][20]

[20]As shown by Figure 1 (b), the UE is moving toward an area that does not support UE’s ongoing slice. Under such circumstance, the service is interrupted for the UE.

Provide your view :

Can we agree to capture this user case into TP:

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | The figure above is the illustration of R15/R16 principles where the UE allowed S-NSSAIs (slice#1 in the above figure in RA1) are uniform supported with UE’s RA. But when the UE moves out of the RA, the slice may not be supported. |
| Qualcomm | Yes | Agree with Huawei |
| Nokia | Yes |  |
| LG | Yes | Agree with Huawei |
| NEC | Yes | We agree to capture this use case in the TP. We also proposed in [R3-204884] to consider the scenario of UE mobility across two registration areas with different slice support in the SI of the Rel-17 enhancement of RAN slicing. |

### Other user case

Provide user case other than list above:

| Company | User case |
| --- | --- |

## Service continuity when an S-NSSAI not being supported uniformly in a TA.[1]

An example scenario is as follows:

- A UE registers in a tracking Area where both URLLC and eMBB are supported, but URLLLC is supported in Freq. 1 only (eMBB can be supported in both Freq. 1 and Freq. 2.)

- During registration procedure, the UE provides Requested NSSAI including both URLLC and eMBB., the AMF includes URLLC and eMBB in Allowed NSSAI.

- A URLLC application requests to connect, and a PDU Session for URLLC S-NSSSAI is established.

- While the UE is connected, connected mode mobility is initiated towards a cell where URLLC S-NSSAI is not available (e.g. Freq. 2)

The question is: Can service and session continuity be supported in this case, where the application is connected via an eMBB PDU session?

[2]To send LS to SA2 asking to determine whether the scenario of an S-NSSAI not being supported uniformly in a TA is possible, and if it is, if session and service continuity with S-NSSAI change is possible and how.

Moderator ‘s notes: The scenario is in the scope of  SA2 and RAN2 and related to cell selection/reselection scenario.

Meanwhile, SA2 is discussing the same issue and potential LS listed below may be sent to RAN2/3 after Aug meeting.

Qn-1: In Rel-15 and 16, when NG-RAN reports the supported S-NSSAI(s) per TA basis to AMF during NG Setup or RAN Configuration Update, does RAN expect each cell in the tracking area (and in each tracking area of the registration area) supporting the same S-NSSAI(s)? Qn-2: If the answer for question above is yes, does such assumption still apply to Rel-17 or are there requirements to enable different scenarios for Rel-17? Qn-3: If the answer to question above is no, does RAN believe current RAN mechanisms are sufficient to support UE switching to different S-NSSAI within the TA?

Provide your view on it:

| Company | Yes/No/Depends on RAN2 decision/ depends on SA2/Other | Comment |
| --- | --- | --- |
| Huawei | Wait for SA2 further action, e.g. LS | SA2 is studying the use case to address the key issue#7: Support of 5GC assisted cell selection to access network slice, but without final conclusion. E.g., S-NSSAIs within Allowed NSSAI can be differently served by the different frequency bands within UE’s TAs/RA RAN can wait for SA2 further progress, and can have this use case with slice remapping/fallback when UE moves within the TA, if this use case is deemed necessary. |
| Qualcomm | Prefer to send LS | Indeed there is ongoing work in SA2 and we may receive an LS, but this is not given and also the scope seems different. It would be useful to make sure at the outset that we do not spend time on aspects that will not be supported in the CN. Specifically, the scenario we are trying to clarify regarding SSC is the non-availability of a slice in parts of the TA, meaning that no cells support that slice in a particular area, and mobility may happen between supporting and non-supporting areas; this is different from the above draft. We also would like to clarify whether SSC is possible in that scenario in rel-17 from SA2 pov. Of course, other aspects could be added as needed. |
| Nokia | No LS | We object to sending an LS while SA2 is discussing the exact same topic. Wait for SA2. |
| LG | Wait for SA2 | Agree with Nokia. There is no need to discuss the topic in this meeting. Wait for SA2 discussion. |
| NEC | Wait for SA2 progress | We tend to agree with Nokia that RAN3 should wait for SA2 progress on this topic. |

# Conclusion, Recommendations [if needed]

If needed

# References

| 1 | R3-204807 | Service Continuity when a slice becomes unavailable (Qualcomm Incorporated) | discussion |
| --- | --- | --- | --- |
| 2 | R3-204808 | LS on Service Continuity when a slice becomes unavailable (Qualcomm Incorporated) | LS out To: SA2 CC: RAN2 |
| 3 | R3-204839 | Use Cases for Network Slice Service Continuity (Nokia, Nokia Shanghai Bell) | discussion |
| 4 | R3-204840 | RAN Re-mapping Solution: key principles (Nokia, Nokia Shanghai Bell) | discussion |
| 5 | R3-204883 | On RAN slice awareness and service continuity (NEC) | discussion |
| 6 | R3-204884 | On intra-RAT handover service continuity (NEC) | discussion |
| 7 | R3-204902 | Discussion on slice re-mapping and fallback upon handover (China Telecommunication) | discussion |
| 8 | R3-205030 | Discussion on slice Re-mapping at mobility (Ericsson) | discussion |
| 9 | R3-205061 | Description of Slice Remapping (Ericsson) | pCR |
| 10 | R3-205083 | Use cases for network slice service continuity (Huawei) | discussion |
| 11 | R3-205084 | Potential solutions to network slice service continuity (Huawei) | discussion |
| 12 | R3-205184 | Initial Consideration On RAN slicing (ZTE, Lenovo, Motorola Mobility) | discussion |
| 13 | R3-205185 | TP for 38.832 (ZTE) | other |
| 14 | R3-205353 | Discussion on use cases for slice service continuity and slice remapping solutions (LG Electronics) | discussion |
| 15 | R3-205354 | (TP for 38.832) Use cases for slice service continuity and slice remapping solutions (LG Electronics) | pCR |
| 16 | R3-205361 | Discussion on NG based handover slice re-mapping (CATT) | discussion |
| 17 | R3-205362 | Discussion on Xn based handover slice re-mapping (CATT) | discussion |
| 18 | R3-205404 | Discussion on slice re-mapping (Samsung) | discussion |
| 19 | R3-205440 | Service continuity for slicing (CMCC) | discussion |
| 20 | R3-205441 | TP to service continuity for slicing (CMCC) | discussion |

other

| 21 | R3-204809 | On need for UE Capability Check for RAN slicing (Qualcomm Incorporated) | discussion |
| --- | --- | --- | --- |
| 22 | R3-205031 | Reasons and methods for serving slices on different frequencies (Ericsson) | discussion |
| 23 | R3-205085 | General overview of RAN3 impact of SA2 slicing work (Huawei) | discussion |
| 24 | R3-205186 | SA2 impact on RAN3 part (ZTE) | discussion |