| 3GPP TSG-RA WG3 Meeting #11 | Document | R3-000689 |
| --- | --- | --- |
| 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 25.423 | CR | 060 | Current Version: | 3.0.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | RAN#7 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Nokia | Date: |  |
| Subject: | Clarification on the C-RNTI parameter in UL Signalling Transfer procedure |
| Work item: |  |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | The use of the C-RNTI parameter is not clearly defined in 25.423, especially related to the allocation and release of the identifier. This shall be clarified in the description of the Uplink Signalling Transfer procedure and C-RNTI parameter. |
| Clauses affected: | 8.2.1.2, 9.2.1.12 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

#### 8.2.1.2	Successful Operation

When the DRNC receives an Uu message where the UE addressing information is S-RNTI and SRNC-IDDRNC shall send the UPLINK SIGNALLING TRANSFER INDICATION message to the SRNC identified by the SRNC-ID received from the UE.

The DRNC shall include in the message the URA Identity of the URA where the Uu message was received, an indication on whether or not the accessed cell belongs to multiple URAs, and the RNC Identity of all other RNCs that are having at least one cell within the URA where the Uu message was received.

The DRNC shall include in the message the C-RNTI that it allocates to identify the UE in the air interface. When DRNC allocates a new C-RNTI to the UE, it releases the old one.

SRNC shall use the C-RNTI contained in the UPLINK SIGNALLING TRANSFER INDICATION message in case it is required to signal it o the UE in an air interface L3 message.

If the message received from the UE was the first message from that UE in the DRNC, the DRNC shall include the D-RNTI and the identifiers for the CN CS Domain and CN PS Domain that the DRNC is connected to in the UPLINK SIGNALLING TRANSFER INDICATION message. These CN Domain Identifiers shall be based on the LAC and RAC respectively of the cell where the message was received from the UE.

Figure 1: Uplink Signalling Transfer procedure, Successful Operation.

#### 9.2.1.12	C-RNTI

C-RNTI (Cell RNTI) is the UE identifier allocated by  the DRNS to be used over the radio interface. It is unique in the cell.One UE context has one unique C-RNTI value allocated in the DRNS.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| C-RNTI |  |  | INTEGER(0..65535) |  |