3GPP TSG-RAN WG3 #111-e	R3-210990

Online, 25th Jan-5th Feb, 2021

Agenda Item:	10.2.1.3

Source:	China Telecom (moderator)

Title:	Summary of Offline Discussion on Successful Handover Report

Document for:	Approval

# Introduction

CB: # 1002_SONMDT_SuccessHO

- UE Assistant Identifier

- UP information

- Use of SHR to optimize the selection of candidate target cells in CHO

- If possible, provide an agreeable TP

(CT - moderator)

Summary of offline disc R3-210990

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Issue 1: Whether to include UE Assistant Identifier in F1AP for each Successful HO Report.

The Successful Handover Report was defined as a list in the last meeting and corresponding TPs were agreed.

In [1], it is proposed to include UE Assistant Identifier in F1AP for each Successful HO Report, because it may help the DU to identify the successful handover report belongs to which UE and then optimize the related handover parameters.

Companies view are appreciated on this issue.

| Company | Comment |
| --- | --- |
| Nokia | This would indeed be needed if HO Reports are bundled. However, we would prefer to have it as FFS until details of the report are confirmed. |
| Qualcomm | Yes this is needed to associate SHR with UE at DU. |
| China Telecom | Yes, we think including the UE Assistant Identifier in F1AP for each SHR is benefit for the DU to identify the relationship between the UE and the SHR, it is similar with the UE Assistant Identifier in F1AP for “RLF Report Information List”. Besides, the UE report SHR to the network once it detects “near to fail” events, the source DU may not release the UE context at that time. |
| ZTE | Yes, this is needed. |
| Ericsson | Agree with Nokia in principle, but it seems that the SHR will contain information to be linked to a UE or a UE policy. Therefore we are ok with this proposal. |
| CATT | In case the UE context is still kept in DU, this information is useful. |

## Issue 2: Whether to introduce UP information in the SHR for DAPS optimization.

DAPS HO (Dual Active Protocol Stack Handover) has been standardized in rel-16 to improve mobility interruption time at UP level, it aims to achieve 0ms interruption time at UP level. But this 0ms target may not always be reached, even with a successful DAPS HO. The reason for this “DAPS failure” can be radio link quality, too many retransmissions, data forwarding latency, wrong QoS mapping at the target, etc… These reasons can be then analyzed and the node responsible for this failure can optimize its parameters to improve its DAPS function.

In [2], it is proposed to introduce UP information in the SHR, and further discuss which UP information are relevant at UE level.

Companies view are appreciated on this proposal.

| Company | Comment |
| --- | --- |
| Nokia | Isn’t the content of the HO Report being discussed in RAN2? So, this should rather be proposed there. |
| Qualcomm | Instead of categorizing “DAPS failure” types, mobility interruption time (irrespective of HO type - legacy/DAPS/CHO) can instead be signaled as part of SHR as UP assistance information. Interruption time might be computed solely at RAN itself and exchanged between the network interfaces and need not involve UE. We agree to study mobility interruption time further and send LS to RAN2 if there are any UE impacts. |
| China Telecom | We think study the UP information in the SHR for DAPS optimization is significative, but the detailed information contained in SHR should be decided by RAN2. |
| ZTE | We think the information is benefit, but detail IE should be decided by RAN2. |
| Ericsson | The main purpose of DAPS is to reduce UP interruption time at HO. A successful HO is not necessarily a successful DAPS HO if the UE experiences UP data interruption. And the most reliable source to evaluate this is UE UP info. This should be therefore introduced in SHR as the best metric to improve DAPS HO performances. RAN3 is the leading group for SON WI. Therefore, RAN3 can task RAN2 to introduce the needed information in SHR if deemed necessary. What is FFS is how far in the details of the exact UE parameters RAN3 can go and inform RAN2 about. |
| CATT | Seems beneficial, but details needs further discussion. |

## Issue 3: Whether to use SHR to optimize the selection of candidate target cells in CHO.

CHO (Conditional Handover) has been standardized in rel-16 to improve mobility robustness. This feature is also quite costly in terms of resources as multiple target nodes will be reserving resources for a long time. Even in a successful CHO procedure, it might happen that too many target candidates (i.e. target with a very low probability to see the UE in its coverage) were configured. Therefore, optimization on candidate target cell selection may be needed and can be considered in the following two aspects combined with UE SHR mechanism:

- identify good candidates which were not configured;

- filter out target which were not needed.

In [2], it is proposed to use SHR to optimize the selection of candidate target cells in CHO.

| Company | Comment |
| --- | --- |
| Nokia | Well, wouldn’t it be up to implementation how the SHR is used? But in principle it is all right to consider such scenarios. |
| Qualcomm | Same view as Nokia. Not sure of what additional UP information is needed in SHR for CHO optimizations. |
| China Telecom | We think study the SHR for CHO optimization is significative, but the detailed information contained in SHR should be decided by RAN2. |
| ZTE | It is not clear about the benefit, the scenario need further analysis. |
| Ericsson | Depending on the number of prepared target cells, CHO can be very resource consuming. Therefore, one the best criteria to improve CHO is the number of prepared cells. Even if CHO is successful, it is possible that the same result could have been obtained while preparing less resources. Or maybe a better candidate was not prepared but could be detected by the UE. Therefore, some new metrics may be needed in SHR to improve CHO performances. And yes, how to use these metrics are up to implementation, but we need to agree what are the metrics which will be needed in the SHR to fulfill these scenarios, if agreed. |
| CATT | Same view as Nokia. After SHR is received in source node , it may be used for many aspects. It is up to implementation. |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-210111 | (TP for SON BLCR 38.473) Introducing UE Assistant Identifier in F1AP for Successful HO Report (China Telecommunication) | other |
| --- | --- | --- |
| R3-210672 | Successful Handover Report for CHO and DAPS (Ericsson) | discussion |