3GPP TSG-RAN WG3 #111-e	R3-210991

Online, 25 January – 4 February 2021

Agenda Item:	10.2.1.4

Source:	CATT  (moderator)

Title:	Offline Discussion on UE History Information in EN-DC

Document for:	Approval

# Introduction

CB: # 1003_SONMDT_UEHist

- SN maintains the UHI? MN maintains UHI when SN does not exist?

- Which messages (and how) are used: MN-initiated modification or release procedures, SN-initiated modification or release procedures, SN addition procedure, inter-MN handover with/without SN change procedure, MN to eNB/gNB change procedure, eNB/gNB to MN change procedure, etc.

- Access and Mobility Indication is used to transfer SN UHIs?

- Handover Report should be enhanced to indicate SN change PP to SN, including SN UHIs received by MN?

- Independent SN UHI vs. association between MN UHI and SN UHI (or merged MN and SN UHI)

- Whether to include Cell type

- Whether to include originating node of the PSCell

- Whether to include Time spent without SCG

- Whether to include PSCell history information with the list of visited PScells for each last visited PCell

- Whether to include time stamp in UE history information

- Encoding of UHI

- May also discuss other issues based on papers submitted

- Try to reach high-level agreements in the first phase, proceed to TPs in the second phase of the email discussion

(CATT - moderator)

Summary of offline disc R3-210991

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Which node (MN or SN) collects SN UHI (network side UHI)?

At last meeting, we have discussed this topic and did not achieve agreement. In this meeting, all companies provide views on this issue and the proposals for SN to collect SN UHI are captured below:

[1], Proposal 1: SCG UHI is managed in the SN.

[4], Proposal 1: SN collects UE history information of PSCell and forward it to MN during SN procedures

[5], Proposal 1: SN is responsible to collect SN UHI

[7], Proposal 1: It is proposed that MN maintains UHI when SN does not exist and SN maintains the UHI when SN exists

[11], Proposal 1: SN is responsible for collecting the SN UHI

[14], Proposal1: RAN3 to agree SN should be responsible for collecting UHI (network side) for SN

[15], Proposal 1: SN collects UE’s UHI of S-NG-RAN node and the information saved by MN node.

[21], Proposal 1: Agree SN to collect the SN UHI and could send it to MN for subsequent processing

Companies which propose to let MN collect SN UHI are captured below:

[10], Proposal 2: MN collects SN UHI and forwards it to target (or new SN) in case of SN addition/modification/change procedures.

[20], Proposal 4: The master node is responsible for keeping the UE history information (including master cell history and secondary cell history), and the UE history information collected by the master node should have precedence over any UE history information kept by the secondary node.

The main divergence for the two opinions is as follows:

- It is already supported to enable SN node report the PScell to MN node for the purpose of location report. But it causes too much interaction in Xn/X2 and should be initiated by CN.

- The MN does not need to know the intra-SN PSCell change.

- Additional delays in inter-MN handover for SN to collect SN UHI.

- PScell report from SN to MN is optional which relies on support of location report feature. If location report is not supported, then it is not feasible for MN to collect the UHI.

Companies are requested to provide their views on this issue and discuss the pros/cons of MN vs. SN collecting the SN UHI.

| Company | Which node collects SN UHI? | Comment |
| --- | --- | --- |

## Which messages include UHI

At last RAN3 meeting, it had been agreed to include UHI in SN addition and change messages with the detail FFS.

Include SN UHI in the SN addition and change messages (modification FFS); information flow in both directions is not precluded at this stage

Many companies propose to include UHI in XN/X2 messages which are collected in the table below.

| Number | Message | Direction |
| --- | --- | --- |
| 1 | S-NODE ADDITION REQUEST SGNB ADDITION REQUEST | MN->SN |
| 2 | S-NODE ADDITION REQUEST ACKNOWLEDGE SGNB ADDITION REQUEST ACKNOWLEDGE | SN->MN |
| 3 | S-NODE MODIFICATION REQUEST SGNB MODIFICATION REQUEST | MN->SN |
| 4 | S-NODE MODIFICATION REQUEST ACKNOWLEDGE SGNB MODIFICATION REQUEST ACKNOWLEDGE | SN->MN |
| 5 | S-NODE MODIFICATION REQUIRED SGNB MODIFICATION REQUIRED | SN->MN |
| 6 | S-NODE MODIFICATION CONFIRM SGNB MODIFICATION CONFIRM | MN->SN |
| 7 | S-NODE RELEASE REQUEST SGNB RELEASE REQUEST | MN->SN |
| 8 | S-NODE RELEASE REQUEST ACKNOWLEDGE SGNB RELEASE REQUEST ACKNOWLEDGE | SN->MN |
| 9 | S-NODE RELEASE REQUIRED SGNB RELEASE REQUIRED | SN->MN |
| 10 | S-NODE RELEASE CONFIRM SGNB RELEASE CONFIRM | MN->SN |
| 11 | S-NODE CHANGE REQUIRED SGNB CHANGE REQUIRED | SN->MN |
| 12 | S-NODE CHANGE CONFIRM SGNB CHANGE CONFIRM | MN->SN |
| 13 | HANDOVER REQUEST | inter-MN |
| 14 | Access and Mobility Indication | inter-MN |

Companies are requested to list the number of messages in which UHI should be included and provide comments if any.

| Company | Number of messages in which UHI should be included | Comment |
| --- | --- | --- |

## What type of UHI needs to be transferred in XN/X2 message

On the basis of subsection 3.2 in which messages to transfer UHI have been selected, here we further discuss the type of UHI in messages.

The type may be SN UHI, MN UHI or combined SN and MN UHI to be transferred when correlated UHI is adopted as captured below:

[4], Proposal 2: Include SN UHI in the SN release and SN modification messages over X2/Xn interface:

[11], Proposal 12: We propose to define a new SN UHI and add this to the legacy UHI per visited Pcell

Proposal 13: We propose to define a new SN UHI (same as above) and send this from SN to MN

[15], Proposal 5: For XnAP and X2AP, only SN UHI information provide from MN to SN

[20], Proposal 3: The same UE history information should be available in both the primary and the secondary node

If separated UHI is adopted, only SN UHI may be needed to be transferred between MN and SN as below.

[10], Proposal 2: MN collects SN UHI and forwards it to target (or new SN) in case of SN addition/modification/change procedures.

To be more specific, we discuss UHI type according to direction of message.

Companies are requested to provide their views on the type of UHI for the messages direction from MN to SN.

| Company | Type of UHI (i.e.MN UHI,SN UHI or combination of MN and SN UHI) | Comment |
| --- | --- | --- |

Companies are requested to provide their views on the type of UHI for the messages direction from SN to MN.

| Company | Type of UHI(i.e.MN UHI,SN UHI or combination of MN and SN UHI) | Comment |
| --- | --- | --- |

Companies are requested to provide their views on the type of UHI for the inter-MN messages.

| Company | Type of UHI(i.e.MN UHI,SN UHI or combination of MN and SN UHI) | Comment |
| --- | --- | --- |

## Correlation of MN and SN UE history information

It was agreed that there are some benefits in correlating the MN UHI and SN UHI and the feasibility and details of such a solution was FFS.

It is beneficial if the MR-DC based UHI and the legacy UHI are correlated when received. Whether this is feasible and the details of the solution are FFS.

Out of the 10 contributions received this meeting,

- 8 contributions propose to have a correlated MN UHI and SN UHI solution and 7 contributions list PSCell as sub-list per PCell in the legacy list

- 2 contributions don’t see much benefit in correlating SN and MN UHI and prefer to have an independent SN UHI solution

Since it was already agreed that it is beneficial to correlate the UHI of MN and SN,we propose to discuss the feasibility of correlation between MN UHI and SN HUI. If it is feasible, please provide your preferred solution i.e. two dimension or one dimension

And if it is not feasible, please provide the reason.

| Company | Is the correlation of MN UHI and SN UHI feasible or not? | Comment |
| --- | --- | --- |

## Time spent without SCG

Most companies discuss this issue. The contributions which prefer to include this IE are captured as below:

[4], Proposal 4: “Time spent without SCG” should not be included in SN UHI.

[10], Proposal 4: Include “Time Spent without PSCell” in SN UHI.

[11], Proposal 14: Add the stay time without PSCell to the MN+SN UHI)

[14], Proposal 3: Include time stamp in UE history information to help network to correlate the UHI (MN) and UHI (SN).

[20], Proposal 7:	Time spent with no PSCell should be included in the UE history information.

The contribution which prefers to use Time stamp IE for SN UHI to deduce the time spent without SCG:

[16], Proposal 10: Instead of “Time spent without SCG”, RAN3 to consider introduce Time stamp IE for SN UHI

The contribution proposes to not include time spent without SCG IE is captured as below:

[5], Proposal 6: “time spent without SCG” is unnecessary. It’s not expected to store SN UHI in MN when no SCG is configured.

Companies are requested to provide their views on whether the information is needed or not and how to indicate the time spent without SCG on the interface.

| Company | Whether the information on time spent without SCG is useful? | If the information is useful, which solution is preferred to carry this information, i.e. via an explicit IE or deduce from other IEs? |
| --- | --- | --- |

## Whether to include Cell Type

At this meeting, some contributions discuss this issue:

[1], Proposal 4a: Cell type is not included, or included optionally (up to the network configuration)

[11], Proposal 15:  Add the cell type to the SN UHI

[15], Proposal 9: Cell type IE is not used for UE history information of S-Node.

Companies are requested to provide their view on including cell type for SN UHI.

| Company | Yes/No | Comment |
| --- | --- | --- |

## Other UHI related proposals

[1], Proposal 4b: The originating node of the PSCell change is included in the SCG UHI

[1], Proposal 5: RAN3 to consider if the SCG UE History Information is to be encoded directly, or as a container to be passed as an OCTET STRING

[5], Proposal 3: Handover Report should be enhanced to indicate SN change PP to SN, including SN UHIs received by MN.

Companies are requested to provide their view (if any) on the above UHI related proposals.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] | R3-210079 | Solution for handling of the SCG UE history information (Nokia, Nokia Shanghai Bell) |
| --- | --- | --- |
| [2] | R3-210080 | (TP to TS 38.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell) |
| [3] | R3-210081 | (TP to TS 36.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell) |
| [4] | R3-210109 | Discussion on UE history information (China Telecommunication) |
| [5] | R3-210264 | TP for SON BLCR for 38.423: UE History Information in EN-DC (Samsung) |
| [6] | R3-210265 | TP for SON BLCR for 36.423: UE History Information in EN-DC (Samsung) |
| [7] | R3-210297 | Enhancement of UE history information in MR-DC scenario (CATT) |
| [8] | R3-210298 | (TP on UE history information for 36.413) Addition of UE history information for SN (CATT) |
| [9] | R3-210299 | (TP on UE history information for 36.423) Addition of UE history information for SN (CATT) |
| [10] | R3-210344 | UE History Information in MR-DC (Qualcomm Incorporated) |
| [11] | R3-210391 | (TP for SON BLCR for 38.423) UE History Information in MR-DC (Huawei) |
| [12] | R3-210392 | (TP for SON BLCR for 38.413) UE History Information in MR-DC (Huawei) |
| [13] | R3-210393 | (TP for SON BLCR for 36.413 and 36.423) UE History Information in EN-DC (Huawei) |
| [14] | R3-210497 | Discussion on collection of UE history information in EN-DC (NTT DOCOMO, INC.) |
| [15] | R3-210560 | UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom) |
| [16] | R3-210561 | (TP for SON BL CR for TS 37.340) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom) |
| [17] | R3-210562 | (TP for SON BL CR for TS 36.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom) |
| [18] | R3-210563 | (TP for SON BL CR for TS 38.413) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom) |
| [19] | R3-210564 | (TP for SON BL CR for TS 38.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom) |
| [20 | R3-210673 | (TP for SON BL CR for TS 36.413/38.413/36.423/38.423): UE History Information for Secondary Node (Ericsson) |
| [21 | R3-210928 | UE history information in MR-DC (CMCC) |
| [22 | R3-210929 | (TP to TS 36.413)UE history information in MR-DC (CMCC) |
| [23] | R3-210930 | (TP to TS 36.423)UE history information in MR-DC (CMCC) |
| [24] | R3-210931 | (TP to TS 38.413)UE history information in MR-DC (CMCC) |
| [25] | R3-210932 | (TP to TS 38.423)UE history information in MR-DC (CMCC) |

# Appendix