3GPP TSG-RAN WG3 #111-e	R3-210993

Online, 25 Jan – 04 Feb, 2021

Agenda Item:	10.2.1.6

Source:	Samsung (moderator)

Title:	CB: # 1005_SONMDT_SNChangeFail - Summary of email discussion

Document for:	Approval

# Introduction

CB: # 1005_SONMDT_SNChangeFail

- MRO definitions

- For SN-initiated PScell Change failure, which node performs initial analysis?

- Xn message definitions (new or enhance existing one)

- LS to RAN2

- May also discuss other issues based on papers submitted

- Try to reach high-level agreements in the first phase, proceed to TPs and draft LS in the second phase of the email discussion

(SS - moderator)

Summary of offline disc R3-210993

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

# Discussion

## Definitions of MRO issues for PSCell change failure

[1] and [15] propose to not touch MN but use the measurement results from UE to identify suitable PSCell change failure events for MRO.

[7], [10] and [13] propose to catch the behaviors of MN into the MRO definitions for PSCell change failure. And [10] propose to let MN indicate a suitable PSCell.

[4] proposes a compromised definition i.e. not touch MN, not use measurement, but “a suitable cell” is used.

Moderator’s comment:

The definition was discussed two meetings without progress. Measurement result is a good measure to decide a good PScell candiate but not the only one because a cell cannot be a good candidate if there is no Xn interface between the MN and the SN which host the cell as clarified in [10]. If we touch “MN” in the definition, some companies may think the last serving SN performs the initial analysis. Considering the MN’s role will be discussed in the detection part i.e. 3.2. For progress, we can try to make the definition general enough and leave the discussion on the node role to detection part. Based on this consideration, let’s try to see whether we can agree the compromised definition as below:

- Too late PSCell change: an SCG failure occurs after the UE has stayed for a long period of time in the PSCell; a suitable different PSCell is found, e.g. based on the measurements reported from the UE.

- Too early PSCell change: an SCG failure occurs shortly after a successful PSCell change from a source PSCell to a target PSCell or a PSCell change failure occurs during the PSCell change procedure; source PSCell is a suitable PSCell, e.g. based on the measurements reported from the UE.

- Triggering PSCell change to wrong PSCell: an SCG failure occurs shortly after a successful PSCell change from a source PSCell to a target PSCell or a PSCell change failure occurs during the PSCell change procedure; a suitable PSCell different with source PSCell or target PSCell is found, e.g. based on the measurements reported from the UE.

Q1: Is the compromised definition agreeable?

Company’s views are appreciated.

| Company | Comment |
| --- | --- |
| Nokia | The definitions above are technically correct and a good starting point for the discussion. But logically, the “e.g.” before measurements is not necessary: there is no other way but to use the measurements. Missing Xn/X2 is rather a problem that shall be detected and corrected than an obstacle for the definitions. So, we would prefer the version that we propose in [1-2]. |
| ZTE | Fine with the compromise. |
| Samsung | Fine with the compromise for moving forward, even though we prefer to have “MN behaviors” in the definitions as we proposed for last RAN3 meeting. |
| CATT | Fine with the compromise. |

## MN’s role in SN triggered PSCell change failure

Which node should have initial analysis for root cause of SN change failure, MN or SN

There are 2 options in the contributions:

Option 1: MN has initial analysis. [3], [4] and [10]

Option 2: SN has initial analysis. [7]

Q2: which option is acceptable?

| Company | Comment |
| --- | --- |
| Nokia | MN’s role has already been discussed and agreed: the MN shall perform the pre-analysis to identify the node that initiated the last PSCell change and to forward the information from the UE there. All the rest, including detection of the failure type, is up to the node which initiated the wrong change. |
| ZTE | Share the view with Nokia. |
| Samsung | Option 1. In R3-109e meeting, RAN3 agreed the following: In case of a PSCell change failure, when the SN is responsible for SCG mobility, the MN forwards the SCGFailureInformation to the SN initiating the last PSCell change (or the last serving SN, in case of too late SN change). For too late PScelll change, the MN forwards the SCGFailureInformation to the last serving SN. For SN triggered too early/wrong cell PScell change, the MN forwards SCGFailureInformation to the SN which triggered the PScell change. To achieve this, the MN should have initial analysis on the failure type. The SN which received the SCGFailureInformation can have final analysis. |
| CATT | MN is not aware of the SN configuration such as Time threshold (i.e. the Tstore_UE_cntxt) and measure result threshold for judging coverage hole since MN and SN is different RAT and configuration. If MN have to decide too early/too late/to wrong PSCell change, all the parameters needed for MN analysis shall be sent from SN to MN in XN/X2 interface because MN and SN may be different vendor and it is not suitable for OAM to transfer these configuration. It is suitable for MN to recognize last serving SN and send SCG failure information to SN. SN makes analysis for root cause of SN change failure. It is aligned with legacy method and has less impact on protocol. |
| China Telecom | Agree with Nokia, MN can perform initial-analysis/pre analysis to identify the failure causes and forward the failure result and the SCGFailureInformation to source PScell, whether the source node may use this information for further analysis can be up to implementation (or FFS). So we think we should support MN to initial analyze the SCG failure first and then discusses whether to support SN to do further analysis. |

## Which message is used from MN to the initiating SN for SN triggered PSCell change

SCGfailureinformation and other necessary information should be forwarded to source SN from MN within a message in case of SN triggered SN change. For the message:

Alternative 1: Reuse HO Report message. [4] and [13]

Alternative 2: Define a new message. [3], [7] and [10]

Q3: which alternative is acceptable?

| Company | Comment |
| --- | --- |
| Nokia | No strong opinion, but probably a new message would be more logical (it is not a “HO”). But should be left as FFS until principles above ae decided. |
| ZTE | Prefer alternative 1. The MRO for PScell is still belong to Mobility Robustness, therefore, it is reasonable to reuse HO report. |
| Samsung | We prefer Alternative 1. As we discussed in R3-210261, most IEs can be re-used. |
| CATT | Alternative 1 |
| China Teleocm | Alternative 2, not all the mandatory IEs in HO Report message are useful for SN-initiated PScell change scenarios. Besides, PScell change is not a “Handover” procedure. |

Another question is which information should be included in the message except SCGfailureinformation?

[7] proposes SN failure type, new target PScell information and the SN UE X2AP ID for the source SN.

Q4: what information should be included in the Xn message except SCGfailureinformation?

| Company | Comment |
| --- | --- |
| Nokia | At this moment, probably nothing more is needed. But should be left as FFS until principles above ae decided. |
| ZTE | Share the view of Nokia. |
| Samsung | Failure type |
| China Telecom | Failure type is needed, others need FFS. |

In addition, if it is agreed in the last section that the last serving SN has initial analysis, [7] propose the last serving SN send analysis result to source SN, so a new XnAP message like handover report shall be introduced.

Q5: Any view on this proposal?

| Company | Comment |
| --- | --- |
| Nokia | No need to forward it between the SNs, if the MN identify the SN that initiated the wrong PSCell change. |
| ZTE | No need to forward messages from old SN to new SN. |
| Samsung | Share the view from Nokia and ZTE |
| CATT | It is aligned with legacy MRO method and a new XnAP message like handover report is need to transfer analysis result to source SN. |
| China Telecom | No need if MN performs initial analysis. |

## Failure reason detection by Enhanced SCG failure report or depending on the UE context in the network side

3 solutions are proposed in the contributions:

Option 1: Depending on the UE context in the network side [10] and [13]

Option 2: Some additional information should be included in the reports from UE e.g. RA information, Failed cell identity, Previous cell identity and time since failure [7] [14]

Option 3: Both. Option 1 can be used for legacy UEs, and Option 2 can be used for R17 UEs. [4]

Q6: which option is acceptable?

| Company | Comment |
| --- | --- |
| Nokia | Opt. 3 |
| ZTE | Option 1 apply for legacy UEs an R17 UEs. Option 2 as enhancement for R17 UEs , also take into account RAN2’s decision. |
| Samsung | Option 3. This is similar to handover procedure. Without option 2, the MN should always keep the UE context in the previous SN even after successful SN change. This bring a lot of burden to the MN. |
| CATT | For O1, it needs MN to be aware of PSCell change. According to the other issue of UHI in last RAN3 meeting, many companies prefer SN to collects SN UHI and follow the rule that MN is not aware of PSCell change especially in case of intra-SN scenario. So, we prefer O2. Or we may wait for the result of UHI. |
| China Telecom | Option 3 is preferred. |

If it’s agreed that some additional information is included in the reports from UE, which information should be included?

- CGI of the Source PSCell: the source PSCell of the last SN change. The source PSCell could be E-UTRA cell or NR cell.

- CGI of the Failed PSCell: the PSCell in which SCG failure is detected or the target PSCell of the failed SN change. The Failed PSCell could be E-UTRA cell or NR cell.

- timeSCGFailure: the time elapsed since the last SN change initialization until SCG failure.

- connectionFailureType: radio link failure or SN change failure.

- Random access information

Q7: Company view on above information from the UE

| Company | Comment |
| --- | --- |
| Nokia | Should be left as FFS until principles above ae decided. |
| ZTE | Share the view with Nokia. |
| Samsung | a), b), c) |
| CATT | a, b, c, d, e |
| China Telecom | a, b, c, d |

After RAN3 has conclusion, we can send LS to RAN2.

## Mobility Information in S-NODE ADDITION REQUEST ACKNOWLEDGE message and the Handover Report like message

[3] and [4] proposed to add Mobility Information in S-NODE ADDITION REQUEST ACKNOWLEDGE message. It is used to associate the SCG failure information with the configuration related to PSCell change decision if SCG failure occurs after successful PSCell change procedure and the source SN have removed the UE context.

Q8: Any view on this proposal?

| Company | Comment |
| --- | --- |
| Nokia | This depends if UE context is used and if SNs may have different PSCell change criteria depending on the UE type. So far it is not confirmed, so probably Mob Info is not needed. |
| Samsung | It’s needed. SCG failure could occur after successful SN change procedure, it’s possible that source SN have removed the UE context. Even source SN receives SCG failure information, source SN has no idea how to associate the SCG failure information with the configuration related to SN change decision. Therefore it needs a mechanism to associate the SCG failure information with the configuration related to SN change decision in this case. Similar to Mobility Information in handover procedure, the source SN generates a Mobility information which is associated with the configuration related to SN change decision. The information should be sent to MN during SN addition procedure. The MN transmits the Mobility Information back to the source SN in the Handover Report like message. If SCG failure occurs after successful SN triggered SN change, source SN can optimize its configuration according to the information even source SN has removed UE context. |
| China Telecom | Similar view as Samsung. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210076,	Definitions for MRO scenarios for SN change failure (Nokia, Nokia Shanghai Bell)

R3-210077,	Definitions of SCG failure events for MRO for SN change (Nokia, Nokia Shanghai Bell)

R3-210110,	Discussion on MRO for SN Change Failure (China Telecommunication)

R3-210261,	TP for SON BLCR for 38.423: Support of SN change failure (Samsung)

R3-210262,	TP for SON BLCR for 37.340: Support of SN change failure (Samsung)

R3-210263,	LS on information needed for MRO in SCG Failure Report (Samsung)

R3-210294,	Consideration on support of SN change failure in case of MR-DC (CATT)

R3-210295,	(TP on SN Change failure for 38.423) Addition of SCG Failure Information transfer (CATT)

R3-210296,	[Draft]LS to RAN2 on SN change failure (CATT)

R3-210395,	(TP for SON BLCR for 38.423) MRO for SN Change Failure (Huawei)

R3-210396,	MRO for SN Change Failure (Huawei)

R3-210397,	(TP for SON BLCR for 38.300) MRO for SN Change Failure (Huawei)

R3-210565,	Further consideration on MRO SN change failure (ZTE)

R3-210676,	On the SCG Failure Information delivery for MRO use case (Ericsson)

[15]	R3-210677,	(TP for SON BL CR for TS 37.340): Definition of SCG change failure types (Ericsson)