3GPP TSG-RAN WG3 #111-e	draft- R3-211114

Online, 25th January -5th February 2021

Agenda Item:	9.3.8.1

Source:	Ericsson (moderator)

Title:	Summary of Offline on RedundantUL_NG-U_UP_TNLinfo

Document for:	Approval

# Introduction

CB: # 102_RedundantUL_NG-U_UP_TNLinfo

- clarify usage

(E/// - moderator)

Summary of offline disc R3-211114

# For the Chairman’s Notes

TBD

# Discussion

## Background

The issue discussed in [1] is that in PDU Session Resource Modify Request Transfer, the “Additional Redundant UL NG-U UP TNL Information” is defined. But there is no IE for Redundant UL NG-U UP TNL Information either in Tabular or ASN.1 code.

This is very strange as in all the other messages, the two IEs Redundant UL NG-U UP TNL Information and the Additional Redundant UL NG-U UP TNL Information are presented as a “pair”, for the purpose of redundant QoS flow transmission, and the redundant QoS flow transmission when the additional NG-U tunnel is deployed.

Please note that is IE is included in the “UL NG-U UP TNL Modify List” which is supposed to be included (optionally) when the UP addresses are to be modified.

Now suppose we are to set up a new QoS flow, and indicated that the QoS flow has redundant transmission, we would need a corresponding new Redundant UL NG-U UP TNL Information.

And if the split PDU session is to be used, there is also a need for a corresponding new Additional Redundant UL NG-U UP TNL Information. But this one is already included.

In our view it is obvious when we did the feature, we simply forgot the IE Redundant UL NG-U UP TNL Information in the Modify Request for the new established QoS flow.

Proposal 1: RAN3 to agree to including the Redundant UL NG-U UP TNL Information in the Modify Request.

During the online discussion, a few comments raised

- the existing Redundant UL NG-U UP TNL Information can be used.

- Is this related to Split PDU session

- Where is the original tunnel?

## Clarify the case

The case in the issue discussed is related to Rel 16 WID NR-IIoT.

It is decided that a QoS flow could be setup with Redundant QoS Flow transmission, so for one QoS flow, a Redundant NG-U tunnel is setup. The QoS is marked with Redundant QoS Flow Indicator.

We say there is an issue in PDU session modification procedure, that if a new QoS flow is setup and if it is the first QoS flow to be setup with the Redundant QoS Flow, the NG-U tunnel IE is missing in the tabular.

Now let us take an example and go throw the tabular.

Step 1: In the PDU session setup procedure: one QoS flow (QFI=1) in PDU session 1 is setup.

When the procedure finished, we have:

- a NG-U tunnel “Tunnel A” with a pair of “UL NG-U UP TNL “Tunnel A UL” / DL NG-U UP TNL “Tunnel A DL”

- in Tunnel A, there is a PDU session 1 and in PDU session 1 there is a QoS flow with QFI=1

Step 2: we are going to do the following in the PDU session modification for PDU Session 1:

- To setup a new QoS flow, e.g. QFI= 2 in PDU session 1,

- and for this QoS flow QFI =2, the Redundant QoS Flow transmission is also setup and it is the first QoS flow with the Redundant QoS Flow transmission.

Note that the modification procedure to set up a QoS flow is very similar to the PDU session setup procedure, the only difference is that in the PDU session setup procedure, we need to set up the first NG-U tunnel for the PDU session. In the PDU session modification case, the first NG-U tunnel exists already (this may answer the question asked online, “where is the original tunnel”).

#### The below is the subset of the IEs related to the issues that we are discussion in 9.3.4.3	PDU Session Resource Modify Request Transfer.

I have removed the IEs not related to keep the table short.

Remember that we have one NG-U tunnel called Tunnel A.

To simplify, no additional tunnel for PDU session split is involved.

We do not modify the Tunnel A in this exercise!

Exercise 1: Please indicate your view which IEs should be presented in the Tabular. (please follow Ericsson example so it is clear to check later)

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Indicate YES/NO if you think the IE is presented |
| --- | --- | --- | --- | --- | --- |
| UL NG-U UP TNL Modify List |  | 0..1 |  |  | Ericsson: No Xx company: Yes/No |
| >UL NG-U UP TNL Modify Item |  | 1..<maxnoofMultiConnectivity> |  |  | Ericsson: No |
| >>UL NG-U UP TNL Information | M |  | UP Transport Layer Information 9.3.2.2 | UPF endpoint of the NG-U transport bearer, for delivery of UL PDUs. | Ericsson: No |
| >>DL NG-U UP TNL Information | M |  | UP Transport Layer Information 9.3.2.2 | Identifies the NG-U transport bearer at the NG-RAN node. | Ericsson: No |
| >>Redundant UL NG-U UP TNL Information | O |  | UP Transport Layer Information 9.3.2.2 | UPF endpoint of the NG-U transport bearer, for delivery of UL PDUs for the redundant transmission. | Ericsson: No |
| >>Redundant DL NG-U UP TNL Information | O |  | UP Transport Layer Information 9.3.2.2 | Identifies the NG-U transport bearer at the NG-RAN node for the redundant transmission. | Ericsson: No |
| QoS Flow Add or Modify Request List |  | 0..1 |  |  | Ericsson: Yes |
| >QoS Flow Add or Modify Request Item |  | 1..<maxnoofQoSFlows> |  |  | Ericsson: Yes |
| >>QoS Flow Identifier | M |  | 9.3.1.51 QFI = 2 |  | Ericsson: Yes |
| >>Redundant QoS Flow Indicator | O |  | 9.3.1.134 | This IE indicates whether this QoS flow is requested for the redundant transmission. | Ericsson: Yes |
| Additional UL NG-U UP TNL Information | O |  | UP Transport Layer Information List 9.3.2.12 | UPF endpoint of the additional NG-U transport bearer(s) proposed for delivery of UL PDUs for split PDU session. | Ericsson: No |
| Additional Redundant UL NG-U UP TNL Information | O |  | UP Transport Layer Information List 9.3.2.12 | UPF endpoint of the additional NG-U transport bearer(s) proposed for delivery of redundant UL PDUs for split PDU session. | Ericsson: No |

Question 1:  Please indicate in your view which IE is used for the new UL NG-U tunnel that should be setup for the Redundant QoS Flow QFI=2

| Company | View |
| --- | --- |
| Ericsson | It is obvious the Redundant UL NG-U UP TNL Information is missing. If we check the PDU session setup procedure, it is there. |

# Conclusion, Recommendations

TBD

# References

R3-210738	Including the Redundant UL NG-U UP TNL Information in the Modify Request (Ericsson, CATT, ZTE)

R3-210737	Including the Redundant UL NG-U UP TNL Information in the Modify Request (Ericsson, CATT, ZTE)

# Annex, the complete tabular for 9.3.4.3 in NGAP

#### 9.3.4.3	PDU Session Resource Modify Request Transfer

This IE is transparent to the AMF.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| PDU Session Aggregate Maximum Bit Rate | O |  | 9.3.1.102 |  | YES | reject |
| UL NG-U UP TNL Modify List |  | 0..1 |  |  | YES | reject |
| >UL NG-U UP TNL Modify Item |  | 1..<maxnoofMultiConnectivity> |  |  | - |  |
| >>UL NG-U UP TNL Information | M |  | UP Transport Layer Information 9.3.2.2 | UPF endpoint of the NG-U transport bearer, for delivery of UL PDUs. | - |  |
| >>DL NG-U UP TNL Information | M |  | UP Transport Layer Information 9.3.2.2 | Identifies the NG-U transport bearer at the NG-RAN node. | - |  |
| >>Redundant UL NG-U UP TNL Information | O |  | UP Transport Layer Information 9.3.2.2 | UPF endpoint of the NG-U transport bearer, for delivery of UL PDUs for the redundant transmission. | YES | ignore |
| >>Redundant DL NG-U UP TNL Information | O |  | UP Transport Layer Information 9.3.2.2 | Identifies the NG-U transport bearer at the NG-RAN node for the redundant transmission. | YES | ignore |
| Network Instance | O |  | 9.3.1.113 | This IE is ignored if the Common Network Instance IE is included. | YES | reject |
| QoS Flow Add or Modify Request List |  | 0..1 |  |  | YES | reject |
| >QoS Flow Add or Modify Request Item |  | 1..<maxnoofQoSFlows> |  |  | - |  |
| >>QoS Flow Identifier | M |  | 9.3.1.51 |  | - |  |
| >>QoS Flow Level QoS Parameters | O |  | 9.3.1.12 |  | - |  |
| >>E-RAB ID | O |  | 9.3.2.3 |  | - |  |
| >>TSC Traffic Characteristics | O |  | 9.3.1.130 | This IE may be present in case of GBR QoS flows and is ignored otherwise. | YES | ignore |
| >>Redundant QoS Flow Indicator | O |  | 9.3.1.134 | This IE indicates whether this QoS flow is requested for the redundant transmission. | YES | ignore |
| QoS Flow to Release List | O |  | QoS Flow List with Cause 9.3.1.13 |  | YES | reject |
| Additional UL NG-U UP TNL Information | O |  | UP Transport Layer Information List 9.3.2.12 | UPF endpoint of the additional NG-U transport bearer(s) proposed for delivery of UL PDUs for split PDU session. | YES | reject |
| Common Network Instance | O |  | 9.3.1.120 |  | YES | ignore |
| Additional Redundant UL NG-U UP TNL Information | O |  | UP Transport Layer Information List 9.3.2.12 | UPF endpoint of the additional NG-U transport bearer(s) proposed for delivery of redundant UL PDUs for split PDU session. | YES | ignore |
| Redundant Common Network Instance | O |  | Common Network Instance 9.3.1.120 |  | YES | ignore |