3GPP TSG-RAN WG3 #111-e                                                                       R3-211115

25 Jan - 4 Feb 2021

Online

Agenda Item:	9.3.8

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # 103_RANsharingMLB

Document for:	Approval

# Introduction

CB: # 103_RANsharingMLB

- any shortcomings in current specifications?

(ZTE - moderator)

Summary of offline disc R3-211115

# For the Chairman’s Notes

Propose the following:

R3-21xxxa, R3-21xxxc merged

R3-21xxxc rev [in xxxg] – agreed

R3-21xxxd rev [in xxxh] – agreed

R3-21xxxe rev [in xxxi] – agreed

R3-21xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## On the need for RAN sharing enhancement for MLB

In [1], we discussed a simple scenario that the RAN sharing enhancement for MLB could be applied. The source node should be aware of the load status of the target cell within the certain PLMN before offloading the UE.

During the online discussion, some companies commented that the existing signalling is enough. We think this enhancement is needed for the RAN sharing scenario, especially for the common interface model.

-----------------------------------------------------TS 38.300---------------------------------------------------

Annex E:
NG-RAN Architecture for Radio Access Network Sharing with multiple cell ID broadcast (informative)

Each NG-RAN node serving a cell identified by a Cell Identity associated with either a subset of PLMNs, or a subset of SNPNs, or a subset of PNI-NPNs is connected to another NG-RAN node via a single Xn-C interface instance.

Each Xn-C interface instance is setup and removed individually.

Xn-C interface instances terminating at NG-RAN nodes which share the same physical radio resources may share the same signalling transport resources. If this option is applied:

-	Non-UE associated signalling is associated to an Xn-C interface instance by including an Interface Instance Indication in the XnAP message;

-	Node related, non-UE associated Xn-C interface signalling may provide information destined for multiple logical nodes in a single XnAP procedure instance once the Xn-C interface instance is setup;

NOTE 1:	If the Interface Instance Indication corresponds to more than one interface instance, the respective XnAP message carries information destined for multiple logical nodes.

-	A UE associated signalling connection is associated to an Xn-C interface instance by allocating values for the corresponding NG-RAN node UE XnAP IDs so that they can be mapped to that Xn-C interface instance.

NOTE 2:	One possible implementation is to partition the value ranges of the NG-RAN node UE XnAP IDs and associate each value range with an Xn-C interface instance.

-----------------------------------------------------TS 38.300---------------------------------------------------

Based on the highlighted description, in the common interface model, the XnAP message could contain the information of multiple logical nodes.

In current TS 38.423, we can see that for the serving cell information exchange, the source node will send the specified cell information (identified by the peer node with one single NCGI) with supported Broadcast PLMN Identity Info List NR to the target node.

-----------------------------------------------------TS 38.423---------------------------------------------------

#### 9.2.2.11	Served Cell Information NR

This IE contains cell configuration information of an NR cell that a neighbouring NG-RAN node may need for the Xn AP interface.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| NR-PCI | M |  | INTEGER (0..1007, …) | NR Physical Cell ID | – |  |
| NR CGI | M |  | 9.2.2.7 |  | – |  |
| TAC | M |  | 9.2.2.5 | Tracking Area Code | – |  |
| RANAC | O |  | RAN Area Code 9.2.2.6 |  | – |  |
| Broadcast PLMNs |  | 1..<maxnoofBPLMNs> |  | Broadcast PLMNs in SIB1 associated to the NR Cell Identity in the NR CGI IE. | – |  |
| >PLMN Identity | M |  | 9.2.2.4 |  | – |  |
| CHOICE NR-Mode-Info | M |  |  |  | – |  |
| >FDD |  |  |  |  |  |  |
| >>FDD Info |  | 1 |  |  | – |  |
| >>>UL NR Frequency Info | M |  | NR Frequency Info 9.2.2.19 |  | – |  |
| >>>DL NR Frequency Info | M |  | NR Frequency Info 9.2.2.19 |  | – |  |
| >>>UL Transmission Bandwidth | M |  | NR Transmission Bandwidth 9.2.2.20 |  | – |  |
| >>>DL Transmission Bandwidth | M |  | NR Transmission Bandwidth 9.2.2.20 |  | – |  |
| >>>UL Carrier List | O |  | NR Carrier List 9.2.2.63 | If included, the UL Transmission Bandwidth IE shall be ignored. | YES | ignore |
| >>>DL Carrier List | O |  | NR Carrier List 9.2.2.63 | If included, the DL Transmission Bandwidth IE shall be ignored. | YES | ignore |
| >TDD |  |  |  |  |  |  |
| >>TDD Info |  | 1 |  |  | – |  |
| >>>Frequency Info | M |  | NR Frequency Info 9.2.2.19 |  | – |  |
| >>>Transmission Bandwidth | M |  | NR Transmission Bandwidth 9.2.2.20 |  | – |  |
| >>>Intended TDD DL-UL Configuration NR | O |  | 9.2.2.40 |  | YES | ignore |
| >>>TDD UL-DL Configuration Common NR | O |  | OCTET STRING | The tdd-UL-DL-ConfigurationCommon as defined in TS 38.331 [10] | YES | ignore |
| >>>Carrier List | O |  | NR Carrier List 9.2.2.63 | If included, the Transmission Bandwidth IE shall be ignored. | YES | ignore |
| Measurement Timing Configuration | M |  | OCTET STRING | Contains the MeasurementTimingConfiguration inter-node message for the served cell, as defined in TS 38.331 [10]. | – |  |
| Connectivity Support | M |  | 9.2.2.28 |  | – |  |
| Broadcast PLMN Identity Info List NR |  | 0..<maxnoofBPLMNs> |  | This IE corresponds to the PLMN-IdentityInfoList IE in SIB1 as specified in TS 38.331 [8]. All PLMN Identities and associated information contained in the PLMN-IdentityInfoList IE are included and provided in the same order as broadcast in SIB1. | YES | ignore |
| >Broadcast PLMNs |  | 1..<maxnoofBPLMNs> |  | Broadcast PLMNs in SIB1 associated to the NR Cell Identity IE. | – |  |
| >>PLMN Identity | M |  | 9.2.2.4 |  | – |  |
| >TAC | M |  | 9.2.2.5 |  | – |  |
| >NR Cell Identity | M |  | BIT STRING (SIZE(36)) |  | – |  |
| >RANAC | O |  | RAN Area Code 9.2.2.6 |  | – |  |
| >Configured TAC Indication | O |  | 9.2.2.39a | NOTE: This IE is associated with the TAC in the Broadcast PLMN Identity Info List NR IE | YES | ignore |
| >NPN Broadcast Information | O |  | 9.2.2.71 | If this IE is included the content of the Broadcast PLMNs IE in the Broadcast PLMN Identity Info List NR IE is ignored. | YES | reject |
| Configured TAC Indication | O |  | 9.2.2.39a | NOTE: This IE is associated with the TAC on top-level of the Served Cell Information NR IE | YES | ignore |
| NPN Broadcast Information | O |  | 9.2.2.71 | If this IE is included the content of the Broadcast PLMNs IE in the top Served Cell Information NR IE is ignored. | YES | reject |
| SSB Positions In Burst | O |  | 9.2.2.64 |  | YES | ignore |
| NR Cell PRACH Configuration | O |  | OCTET STRING | Containing 9.3.1.139 NR Cell PRACH Configuration as of TS 38.473 [41]. | YES | ignore |
| CSI-RS Transmission Indication | O |  | ENUMERATED (activated, deactivated, ...) | This IE indicates the CSI-RS transmission status of the given cell. | YES | ignore |

-----------------------------------------------------TS 38.423---------------------------------------------------

Similarly, in the common interface model, for the Resource Status Reporting procedure, the target node could send the load information of requetsed subset or all PLMNs associated with the cell (NR CGI) back to the source node via a single RESOURCE STATUS UPDATE message. Such handling is align what we designed in TS38.300 for non-UE associated Xn-C interface signalling for common interface and it should be supported as well as per-PLMN specific interface model.

Companies are invited to provide their view on whether to introduce this enhancement over Xn.

| Company | Comment |
| --- | --- |
| ZTE | Needed As analyzed above, we think such enhancement is necessary to support the common interface model in RAN Sharing, in addition, it also helps to save signalling load over interfaces. |
| Nokia | Not needed. Even with common transport the logical node model applies. |

## RAN sharing related cause value for Mobility Settings Change procedure

In the case of RAN sharing, if the primary PLMN of source cell target cell are different, which means that they could be managed by different operators with different RAN sharing strategy and policy, then the mobility parameter negotiation may be not admitted. And this could lead to the failure of Mobility Settings Change procedure. However, if the source cell does not acknowledge this failure reason, it will retry to perform mobility parameter negotiation with the same target cell repeatedly, which could result in the unnecessary signalling load.

Therefore, one new cause value for RAN sharing reason should be added in the MOBILITY CHANGE FAILURE message, i.e. Negotiation not allowed[3].

Companies are invited to provide their view on whether this cause value can be introduced.

| Company | Comment |
| --- | --- |
| Nokia | In our view this scenario is not valid in deployments based on logical nodes. |

## If companies agree with this enhancement, the corresponding CRs could be considered.[2][3]

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-210824, “Discussion on RAN Sharing Enhancement for MLB in NR”, ZTE, China Telecom, China Unicom

R3-210825,	“CR for TS38.300 on RAN Sharing Enhancement for MLB”, ZTE, China Telecom, China Unicom

R3-210828,	“CR for TS38.423 on RAN Sharing Enhancement for MLB”, ZTE, China Telecom, China Unicom