3GPP TSG-RAN WG3 #111	R3-211037

25 January-04 February 2021

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on Onbaording- Cell Access

Document for:	Approval

# Introduction

CB: # 1101_PRN_Onboarding

- Which messages carry onboarding support indication? What information is signaled (e.g. indication granularity)?

- Impact on NNFS? How RAN knows if AMF supports onboarding?

- May discuss other issues based on contributions submitted

- LS to SA2

- If there is progress, attempt to agree BL CRs

(Nok - moderator)

Summary of offline disc R3-211037

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# Discussion

## Cell Access for onboarding

This section deals with access for onboarding, which is part of key issue#4 by SA2. The questions below correspond to points raised in the papers and aim to seek companies’ opinion.

Q1: Can O-NPN (Onboarding NPN) be a PLMN or an SNPN?

| Company | Comment |
| --- | --- |
| Nokia | According to SA2, O-NPN can be either a PLMN or an SNPN. We can further call them O-PLMN and O-SNPN in what follows. |

Q2: Do all AMF(s) of the O-NPN necessarily support onboarding?

| Company | Comment |
| --- | --- |
| Nokia | No. only a subset of the AMF(s) may support onboarding. |

Q3: If answer to Q2 is “no”, which information should NG-RAN node receive about connected AMF(s) in order to enable proper selection of AMF at cell access?

| Company | Comment |
| --- | --- |
| Nokia | NG-RAN node needs to know whether AMF supports onboarding function or not. |

Q4: how should NGRAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | AMF can provide this information in NG Setup Response message as proposed in tdocs 160/161. |

Q5: should AMF also send the SO-SNPN IDs to the NG-RAN node?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need for this but this could be double-checked with SA2 (see below proposed LS). |

UE is assumed to send the onboarding register type to the AMF over NAS and UE indicates also this over RRC to trigger NG-RAN node for proper AMF selection.

Q6: Do you think that NG-RAN node should additionally relay over NGAP Initial UE Message the “onboarding” indication received in RRC setup complete? If Yes, why?

| Company | Comment |
| --- | --- |
| Nokia | There seems no such agreement in SA2 at this time. |

Onboarding uses a specific “restricted PDU session” for UP remote provisioning.

Q7: Do you think that NG-RAN node shall be informed of this special PDU session at PDU Session Setup Request?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see any reason why at this time. |

Q8: Do you think that all NG-RAN nodes shall support onboarding or is it possible that only a subset of them supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | To keep it simple we think onboarding feature support should be uniform in the whole O-NPN in R17. |

Q9: If answer to Q8 is “only a subset of NG-RAN nodes supports onboarding is possible” do you think that NG-RAN nodes should indicate to AMF whether it supports onboarding?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |

Q10: do you see the need for onboarding as a criterion for the NGAP Overload control??

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Cell Access for external credentials

This section deals with access for authentication via external credentials, also called key issue#1 by SA2.

Q11: Which information should NG-RAN node receive about connected AMF(s) in order to select a proper AMF

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node needs to receive the support of the feature of authentication by external credentials and may also receive the Group IDs of the partners. |

Q12: How should NG-RAN node receive this information?

| Company | Comment |
| --- | --- |
| Nokia | The NG-RAN node can receive this information from the NG Setup Response message as proposed in tdocs 160/161. |

Q13: Do you think that some information needs to be sent in the NGAP Initial UE Message at access time and if yes which one?

| Company | Comment |
| --- | --- |
| Nokia | We don’t see the need at this time. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Baseline CRs

A baseline CR is proposed for TS 38.300 in tdoc 160. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |

A baseline CR is proposed for TS 38.413 in tdoc 161. Please indicate comments on it.

| Company | Comment |
| --- | --- |
| Nokia | OK as starting point. |

## Possible LS to SA2

Which question would you like to ask to SA2 for access for onboarding?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Does AMF needs to indicate a list of supported SO-IDs to NG-RAN nodes in addition to “onboarding support” (in analogy with sending the list of supported GIDs for authentication with external credentials). Q2: Whether information needs to be included in NGAP Initial UE Message for the case of access for onboarding |

Which question would you like to ask to SA2 for access using eternal credentials?

| Company | Comment |
| --- | --- |
| Nokia | Q1: Whether information needs to be included in NGAP Initial UE Message for the case of authentication with external credentials. |

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-20xxxx